## Slide 1
CS 118: Bridges versus Routers: To Switch or to Route
George Varghese

## Slide 2
Bridge
B
C
A B
A
A, B
C
How to build database
automatically?

## Slide 3
REPEAT FRAMES
LEARN AND FILTER MULTICAST AND AGING
CENTRALIZED: ROOTED TREE
MESSAGE PASSING: ROOT,DISTANCE ESTIMATES
FAILURES: ADD AGE FIELD
AGE HELLOS
BASIC BRIDGING IDEAS
SPANNING TREE IDEAS
TUNING PARAMETERS: COST,ROOT−PRIORITY
LETS START BY REVIEWING BRIDGING

## Slide 4: Understanding Bridge Router Topologies
Host B
Host A
R1
R2
B1
D
E
C
Web Browser
Web Server
m1
m2
m3
m4
m6
m7
128.6.*
m5
M5 etc. MAC Addresses
128.5.* etc IP Addresses
128.5.*
128.5.1.2
128.6.8.7

## Slide 5: Bridge View of the World
B1
m2
m3
m4
All routers are just MAC addresses to Bridges. R1 is
just m4
m1
m1, m2 up
m3, m4 down

## Slide 6: Router view
Host B
Host A
R1
R2
D
E
C
m1
m3
m6
m7
128.6.*
m5
128.6.* 
128.5.* down
128.5.*
A  m1
C  m2
D  m3
ARP table at R1
Forwarding table at R1
Naming: IP , MAC and Translation

## Slide 7
BASIC QUESTION
RD | RS | Hop Count | Fragment Number | C.F
Original Data Link was single hop. But bridges make things multihop
So why have routers? Good question.
Main reason is that Data Link Headers were developed before bridges. So no support for Data Link relays in Data Link Header. The opposite is true for routing headers.
Data Link Routing Header
D S .
C.F.= Congestion Feedback

## Slide 8
Why Bridges are Bad: Hetrogeneous Links
Address Incompatibility (e.g., HDLC and Ethernet)
Max Packet Size Incompatibility (e.g., FDDI and Ethernet)
Bandwidth Incompatibility (e.g., FDDI and Ethernet)

## Slide 9
Why Bridges are Bad: Large Networks
802 address is flat (like social-security numbers). Routing addresses hierarchical (like postal addresses). Bridges have to learn all addresses in an extended LAN. (more memory) Routers only learn addresses within each level of hierarchy.
Spanning Tree inefficient. Does not route packets on shortest path between two points. Increased latency and smaller throughput. Also flooding wastes throughput.

## Slide 10: WHY SPANNING TREES ARE BAD IN THE WIDE AREA
B1
B2
B3
B4
B6
B5
Chicago Office
LA Office
Tampa Office
Spanning Tree algorithm has to break
Loops. So can’t use say this link

## Slide 11
Why hierarchical addresses?
Crucial for scaling :
If we used bridges to connect the global Internet, each bridge would store billions of MAC addresses
So MAC addresses are flat and unique worldwide but IP addresses are hierarchical
Scalability requires hierarchy. Like telephone numbers and postal addresses but IP is weirder as we said in the Miniflip and we will study next

## Slide 12
Why Bridges are Good
Generality: Bridges allow stations with different routing protocols to use the same Extended LAN.
Cost-Performance (since they do less, bridges cost less than routers with the same performance)
Control Traffic: Smaller amount of routing control traffic (Spanning Tree traffic is small by comparison)

## Slide 13
Conclusion
Each has a place:
Bridges can be used to connect a small number of compatible LANs to form an Extended LAN,
Routers connect Extended LANs to form a Routing Network.
Most routers today are multiport devices some ports can be bridges (switched ports) and some can be routers (router ports). Manager can configure