## Slide 1: Designing Protocols
CS 118: Computer Networks
George Varghese

## Slide 2: Part 1: Common system issues

## Slide 3: Systems design choices
Naming: VM address, page tables (OS), relational table names (databases)
Synchronization: locking and interrupt handling (OS), transaction serialization (databases)
Resource allocation: time sharing (OS), handling concurrent transactions (databases)
Error control: recovery after a crash (OS), rollback after transaction failure (databases)

## Slide 4: Ditto in Networks
Naming: time slots (physical), MAC addresses (DL), IP addresses (IP), IP address + ports (TCP)
Synchronization: clock recovery (physical), packet sending (Ethernet), routes (IP), sequence #s (TCP)
Resource allocation: WDM, stat muxing in LANs, flow control, congestion control in TCP
Error control: spacing levels (Physical), CRCs (Data Link), LSP jumps (routing), retransmission (TCP)
True for all systems (databases, OS) but one new one
Interconnection strategy: repeater (Physical), bridge (Data Link), router (IP), gateway (TCP and higher)

## Slide 5: Part 2: Designing a Protocol

## Slide 6: Motivating Example
You too: Likely some of you will design at least an app protocol. Arguably the “science” in 118
My Google Interview: design a protocol to broadcast stock quotes to multiple locations in US so all quotes are delivered nearly at the same time.
Problem: this is done over a vanilla Internet where packets can be delayed varying amounts & lost
Hidden Assumption: Interviewer (a seasoned Google architect) was waiting for me to ask this. What?

## Slide 7: What is a Protocol?
Algorithms to synchronize state variables at a sender and possible multiple distant receivers to provide a specified service

## Slide 8: Protocols studied in 118
Clock recovery: synchronize receiver sampling times to sender midbit times + prop delay. Service?
Sliding window: synchronize packets sent and received using sequence #s. Service?
Old Ethernet: synchronize collisions so if one station detects collisions, all do. Service?
Spanning Tree: synchronize tree root and distance among bridges. Service?
Link State: synchronize LSPs among routers. Service?
TCP Initialization: synchronize ISNs. Service?

## Slide 9: Protocol Challenges/Threats
Asynchrony: Different packets take different time, possibly different routes with large upper bounds
Loss: Packets can be lost. How?
Reordering: Packets can be reordered. How?
Nodes Crash: Nodes can crash and restart any time
Link Crashes: So can links
Getting started: Unlike algorithms in a single computer, have to initialize state at sender & receiver(s)

## Slide 10: Protocol Mechanisms
Asynchrony: Cues like transitions, flags, acks, sequence numbers
Loss: Retransmission
Reordering: Sequence numbers
Nodes Crash: Time outs, nonces
Link Crashes: Hellos, time outs
Getting started: NVRAM, clocks, nonces

## Slide 11: Part 3: Removing Protocol Assumptions Clean designs

## Slide 12: Example 1: Stock Broadcast
Asynchrony: ?

## Slide 13: Example 2: DNS over UDP?
Reliability: ?

## Slide 14: Example 3: Radia
Addressing:
Does a small IPV4 address require new mechanisms for address assignment (DHCP), a way to cope (NAT), and a whole larger address space (IPV6)
Let’s hear from Radia
Bottom line: CLNP is a way of combining the best of IP (prefixes, hierarchy) with uniqueness of Ethernet. So the “new proposed Internet” address would be 14 bytes of cloud specific prefix and 6 bytes of your Ethernet address as low order bytes to get a 20 byte address

## Slide 15: CLNP would finesse things
DHCP: No need for a server as when you move within an organization your network address stays same. When you go to new “cloud” you ask cloud for its 14 byte prefix and stick your Ethernet address at end
NAT: No need as there are plentiful addresses (20 bytes)
IPv6: No need as its only 12 byte addresses
But to be fair DHCP and NAT have some security advantages and our Internet still works: Facebook, Uber, remote banking: what would we be without the Internet with all its warts and flows