## Slide 1: Layer 2-3 Myths, Missteps, and Mysteries
Radia Perlman
Radia.Perlman@Dell.Com
Radia.Perlman@dell.com

## Slide 2: Plug for my books
A place to get them at a discount direct from the publisher (40% off print book):
informit.com/Perlman, with code PERLMAN40 (through 2024)

## Slide 3: Understanding Network Protocols

## Slide 4: Network Protocols
Nobody would have designed what we have today
You need to understand the history of weird decisions

## Slide 5: Layers 2 and 3 Stuff

## Slide 6: Why do we need both Ethernet and IP?
Answer that “Everyone knows”
  IP is “layer 3”. Ethernet is “layer 2”
What does it mean to be “layer 3” vs “layer 2”?

## Slide 7: So, first we need to review network “layers”
This is in all network books
ISO credited with naming the layers
It’s just a way of thinking about networks…actual implementations subdivide for more layers, or combine layers, or do “layer violation” where one layer looks at the headers of other layers
What’s important for this talk, though…
  Layer 1: physical layer – send a stream of bits to a neighbor
  Layer 2: use layer 1’s stream of bits, and mark the beginning and end of a packet, maybe a checksum. Send a packet to a neighbor
  Layer 3: have routers/switches forward packets from link to link to deliver a packet from a source to a destination across a network

## Slide 8: What layer is “Ethernet”?
Ethernet was intended to be layer 2
Layer 2: just between neighbors – not forwarded
But we are forwarding Ethernet packets – how did that happen?
Bridges/routers/switches all forward packets between links…so (I claim) all should be considered layer 3

## Slide 9: Back then…
I was the designer of layer 3 of DECnet
  the routing protocol I designed for DECnet can work with any layer 3 protocol, and is still widely deployed for routing IP
  ISO adopted it, and called it IS-IS
  IETF pretty much copied it, making it more complicated, and called “their thing” OSPF

## Slide 10: Parameters

## Slide 11: I hate computers
I design stuff for people like me
Avoid parameters
  Have the designers pick a number that’s good enough
  Have the system measure stuff and choose a number
If you have to have a parameter, make sure it can’t be set incorrectly
But sometimes it’s legal at A and at B, but the values won’t interwork
Example: IS-IS Hello timer
And the way that OSPF copied it

## Slide 12: What’s a routing algorithm?
Routers exchange information with their neighbors
Compute a forwarding table

## Slide 13: Forwarding Table
Switch/router/bridge
destination
Destination/output port
Destination/output port
Destination/output port
…
Port 1
Port 2
Port 3
Packet

## Slide 14: Link State Routing

## Slide 15
A
B
C
D
E
F
G
6
2
5
1
2
1
2
2
4
A network

## Slide 16
A
B
C
D
E
F
G
6
2
5
1
2
1
2
2
4
C
B/2
F/2
G/5
Each node creates a “link state packet” saying who it is, and who its neighbors are. This is C’s link state packet.
It gets sent to all the other nodes

## Slide 17
A
B
C
D
E
F
G
6
2
5
1
2
1
2
2
4
A
B/6
D/2
B
A/6
C/2
E/1
C
B/2
F/2
G/5
D
A/2
E/2
E
B/1
D/2
F/4
F
C/2
E/4
G/1
G
C/5
F/1
Everyone has the above database of link state packets

## Slide 18
A
B
C
D
E
F
G
6
2
5
1
2
1
2
2
4
A
B/6
D/2
B
A/6
C/2
E/1
C
B/2
F/2
G/5
D
A/2
E/2
E
B/1
D/2
F/4
F
C/2
E/4
G/1
G
C/5
F/1
This database allows each node to compute its own forwarding database

## Slide 19: How to flood LSPs
Keep the most recently generated LSP from each other router
Receive an LSP from source Fred, from neighbor N
If it’s newer, replace the stored one and flood the new one
How to know if it’s newer than the one stored from Fred?
Most recently received?
Need sequence number
But, how big is the sequence number? Use modular arithmetic

## Slide 20: Comparing sequence numbers
x
>x
<x

## Slide 21: What happens if things get into bad states?
Your PC…reboot
Computer networks
  Diagnose the problem by sending messages on the (broken) network
  Fix it by sending messages on the (broken) network

## Slide 22: ARPANET algorithm
Compare sequence number of newly received LSP from source Fred, from neighbor N, with stored LSP from source Fred
Whichever one is bigger, keep that one
If it’s the newly received one, flood it to all your neighbors (other than the one you received it from)
“Flood it” (in ARPANET algorithm) means send it once, to your neighbors, with no acks
So source must issue new LSP, even if it hasn’t changed, every few seconds

## Slide 23: ARPANET Disaster
Symptom: Net didn’t work
These guys were really lucky
Same guys who designed the algorithm, wrote the code, and managed the network, all from BBN

## Slide 24: ARPANET disaster
x
y
z
xyzxyzxyz
xzyxzyxzy
yzxyzxyzx

## Slide 25: What now?
Networks don’t have on/off switches
First crash and reload BBN router
Still broken---examine core dump
Realize the problem
Create patched code to ignore LSPs from Fred
One by one, crash and load rtrs with patch
One by one, load rtrs with real code again
Hope it never happens again by accident (or on purpose!)

## Slide 26: My first paper
Predicted this in ARPANET algorithm
Made a case that networks need to be more resilient than single systems
Argued for “self-stabilization”
Showed how to make this type of algorithm self-stabilizing, and made it a lot more efficient
  Various things, like large linear sequence number space, and reliable transmission to neighbors, comparing LSP database
The paper was rejected
Last sentence of the paper “This is how to make the network self-stabilizing once whatever is causing disruption is disconnected from the network, but it wouldn’t be possible to make the network function while the corruption is happening
When I went back to grad school 10 years after having dropped out, my manager challenged me to either prove or disprove that statement
That was my proposed thesis
And it turned out to be trivial—talk about that later

## Slide 27: Back to history
I was designing layer 3
Then along came Ethernet

## Slide 28: Original Ethernet: A way for a bunch of nodes to share the same wire
No leader to call on them…all peers
If more than one speaker, receivers get garbage

## Slide 29: CSMA/CD
CS: Carrier Sense (listen before you start speaking)
MA: Lots of nodes share the same wire
CD: Collision Detect (listen even while you are talking in case someone else decides to talk at the same time, in which case both stop, and start random time later
If try to load more than 60% traffic, too many collisions
Limited number of nodes (hundreds), and distance…so OK for within a building…not for the Internet

## Slide 30: Ethernet Addresses
Ethernet has 6 byte addresses, and only needs to identify nodes on a single link
IP has 4 byte addresses and was intended to identify all nodes in the Internet
Why would the Ethernet designers use a 6 byte address when an “Ethernet” only supported a few hundred nodes?
  It eliminates the need for users to configure addresses
Manufacturer purchases a block of addresses, and configures a unique address into each device
Slight rant: For bizarre reasons, this built-in “address” is known as the “MAC address”

## Slide 31: I saw Ethernet as a new type of link
I had to modify the routing protocol to accommodate this type of link
For instance, the concept of “pseudonodes” so that instead of n2 links, it’s n links with n+1 nodes

## Slide 32
Instead of:
Use pseudonode
Pseudonodes

## Slide 33: But Ethernet was a link in a network, not a network
I wish they’d called it “Etherlink”

## Slide 34: Ethernet packet
data
dest
source

## Slide 35: Layer 3 Packet
data
dest
source
hop cnt

## Slide 36: It’s easy to confuse Ethernet with layer 3
It looks sort of the same
How Ethernet differs from layer 3 headers (like IP)
  Flat addresses (no way to summarize a bunch of addresses in a forwarding table)
    there wasn’t supposed to be “forwarding tables” in Ethernet…no forwarding
    but great for configuration (burden on manufacturer, not user)
  No hop count field…
    But it never occurred to the Ethernet inventors that anyone would be forwarding an Ethernet packet

## Slide 37: How Ethernet evolved from CSMA/CD to spanning tree
People built apps on Ethernet, with no layer 3
(Layer 3) router can’t forward without the right envelope
I tried to argue…
The applications were good, and the implementers were considered heroes
The application would have been just as good if they’d done it correctly…on top of layer 3

## Slide 38: Problem Statement (from about 1983)
Need something that will sit between two Ethernets, and
let a station on one Ethernet talk to another
A
C
Without modifying the endnode, or Ethernet packet, in any way!

## Slide 39: The basic concept
Bridge just listens “promiscuously”, and forwards to other port(s) when the “ether” is free (or it gets the token, …)
This requires a topology without loops

## Slide 40: What to do about loops?
Just tell customers “no loops”?
  What about miscabling?
  What about backup paths?
So…desire for loop-pruning algorithm
  Allowing any physical topology
  Pruning to a loop-free topology for sending data
  So…the birth of the spanning tree algorithm (to be described)

## Slide 41
9
3
4
11
7
10
14
2
5
6
Physical Topology

## Slide 42
9
3
4
11
7
10
14
2
5
6
Pruned by Spanning Tree

## Slide 43
9
3
4
11
7
10
14
2
5
6
A
X
Path from A to X

## Slide 44: “Everyone knows”
Ethernet is wildly successful
“Sure is lucky the industry didn’t go with that silly token ring or token bus way of sharing a link”
But wired Ethernet quickly became spanning tree with point-to-point links
  A variant is used on wireless links
“Ethernet” today has nothing to do with the original CSMA/CD Ethernet invention – no clever way of sharing a link needed

## Slide 45: Saga of spanning tree algorithm
Manager asked me on Friday afternoon
Left for vacation for a week
No email or cell phones
Friday night I realized just how to do it
Finished the spec by Tuesday afternoon
How I spent the remainder of the week

## Slide 46: Algorhyme
I think that I shall never see A graph more lovely than a tree.
A tree whose crucial property Is loop-free connectivity.
A tree which must be sure to span So packets can reach every LAN.
First the root must be selected, By ID it is elected.
Least cost paths from root are traced, In the tree these paths are placed.
A mesh is made by folks like me. Then bridges find a spanning tree.
Radia Perlman
Notes: Copyright 2002 Radia Perlman and Charlie Kaufman. All Rights Reserved.

## Slide 47: Bother with spanning tree?
Maybe just tell customers “don’t do loops”
First bridge sold...

## Slide 48: First Bridge Sold
A
C

## Slide 49: Why spanning tree Ethernet is a kludge
You don’t get optimal paths
Unused links (those not selected to be in tree)
Temporary loops really dangerous (header has no hop count)

## Slide 50: Why was bridging so popular?
Originally, there were lots of layer 3 protocols (IPX, Appletalk, IP, DECnet), so you’d need a lot of different routers, or expensive multi-protocol routers…bridges just worked and were cheap
Zero configuration required
And bridges really helped IP be more tolerable (more later)

## Slide 51: Why do we need both Ethernet and IP?

## Slide 52: Why not get rid of Ethernet and use only IP?
World has converged to IP as layer 3, and it’s in the network stacks – so original reasons for needing bridged Ethernet is gone
On a link with just 2 nodes, why do you need a 6-byte source and 6-byte destination address just to talk on that one link??
Why can’t you just forward things with layer 3?
If IP were designed differently, we wouldn’t need Ethernet header anymore!
There were other layer 3 protocols that could have done all the link forwarding with layer 3

## Slide 53: What’s wrong with IP?
IP is configuration intensive, moving VMs disruptive
  Every link must have a unique block of addresses
  Routers need to be configured with which addresses are on which ports
If something moves, its address changes
  If you move from one side of an IP router to another, your layer 3 address has to change
  You can’t have a cloud with a flat address space, where nodes can move around without changing IP address

## Slide 54: IP: Each Link Different Address Block
A
C
2*
51*
271*
289*
*
51*
289*
*
Internet

## Slide 55: Layer 3 doesn’t have to work that way!
CLNP / DECnet...20 byte address
  Top 14 bytes shared by all nodes within cloud
  Inside the cloud, route to 6 byte ID -- nodes can move within the cloud without changing their address
  Enabled by “ES-IS” protocol, where endnodes periodically announce themselves to the routers
14 bytes
6 bytes
Prefix shared by all nodes in large cloud
Endnode ID

## Slide 56: CLNP
Cloud 1
Cloud 2
Cloud 3
14 byte prefix, with lots of levels of hierarchy, routes to a cloud
Inside cloud, route based on last 6 bytes
14 byte prefix
6 byte

## Slide 57
IP Plus Ethernet
CLNP
Ethernet
IP gets you to destination “link”
Need to do ARP to get Ethernet address
Bottom 6 bytes of CLNP
Top 14 bytes of CLNP address gets you to “cloud”
True layer
3 routing inside final circle.
No need for layer 2 header
CSMA/CD?
Spanning tree?
TRILL?
VXLAN?

## Slide 58: With IP
One prefix per link (like IP)
One prefix per cloud
2*
25*
28*
292*
22*
293*
2*
CLNP: zero configuration inside cloud

## Slide 59: Worst decision ever
1992…Internet could have adopted CLNP
Someone modified TCP to work on top of CLNP…and all Internet applications therefore would work with CLNP
Easier to move to a new layer 3 back then
  Internet smaller
  Not so mission critical
  IP hadn’t yet (out of necessity) invented DHCP, NAT (explained soon), so CLNP gave understandable advantages
CLNP much cleaner than IP
  “Level 1” (routing based on bottom 6 bytes of address) is cloud with flat address, and true layer 3 routing (hop count, best paths)

## Slide 60: Reasons given at the time not to adopt CLNP
“It would be ripping out the heart of the Internet and putting in a foreign thing”
“We don’t like the ISO layer 6”
“We’re not immediately out of IPv4 addresses, and I’m sure we could invent something way more brilliant”

## Slide 61: Decision
Let’s do something new, and call it IPv6

## Slide 62: IPv6
Just a 16-byte version of IP, with 8 bytes for “prefix” and 8 bytes for “node ID on last link”
  8 bytes on top is inconveniently small for administering addresses
  8 bytes on bottom is way too much (e.g., with DHCP dynamically handing out addresses in a cloud, 4 bytes is fine)
    Why not 6 bytes? They thought at the time 8 byte UIDs would catch on
Technically inferior to CLNP!
  IPv6 (like IPv4) needs a different prefix on every “link”

## Slide 63: Some good stuff that might not have happened if the industry had made the right decision

## Slide 64: DHCP (Dynamic Host Configuration Protocol)

## Slide 65: How does an endnode get a layer 3 address?
CLNP…stick Ethernet address into bottom 6 bytes
IP…configure
Then DHCP invented

## Slide 66: DHCP
DHCP server
Pool of IP addresses on the “link”
(broadcast) Find DHCP server
I need an IP address
You can have this IP address

## Slide 67: What’s cool about DHCP
Don’t need 6 bytes for “address on link”
  Addresses could be smaller, or top part could be bigger
Enhances privacy
Certainly DHCP could have been used with CLNP, but would anyone have thought of it?

## Slide 68: NAT (Network Address Translation)

## Slide 69
NAT
Internet
g
F, H, K
Make mapping g/K
Private network
Z
S=g, D=Z
S=K, D=Z
S=Z, D=K
S=Z, D=g

## Slide 70: What’s cool about NAT
No way to talk to a node inside unless it talks first
Certainly could have worked with CLNP, but would anyone have thought of it (since global addresses were plentiful)

## Slide 71: Thank you!