## Slide 1: TCP Congestion Control
CSE 118: Computer Networks
George Varghese
(some slides by Alex Snoeren)

## Slide 3: Flow vs Congestion Control
Sender
Receiver
Network
Flow Control: Matching speed of sender to receiver speed
Congestion Control: Matching speed of sender to network speed

## Slide 4: He saved the Internet (1980s)

## Slide 5
A(1,2)
Windows provide static flow control. Can provide dynamic flow control if receiver acks indicate Lower and Upper Window Edge.
Need to avoid deadlock if window is reduced to 0 and then increase to c > 0. In OSI, receiver keeps sending c. In
TCP, sender periodically probes an empty window.
FLOW CONTROL
D(2)
D(0)
D(1)
1,2
Normally would slide to 1,3 but receiver reduces window to 2

## Slide 6
WHEN LINK FROM S TO FIRST ROUTER WAS UPGRADED FROM
19.2 KBPS TO 1 MBPS, THE TIME FOR A FILE TRANSFER WENT
UP FROM A FEW SECONDS TO A FEW HOURS
2) THIS HAPPENED IN AN EXPERIMENT IN DEC IN THE 1980s.
SHOWED THE NEED FOR CONGESTION CONTROL (DECBIT)
VERY SIMILAR EXPERIENCES IN INTERNET LED VAN JACOBSON
TO PROPOSE TCP CONGESTION CONTOL. VAN IS AN AFFILIATE
PROFESSOR AT UCLA!
S
19.2 M
D
19.2
19.2
WHY CONGESTION CONTROL IS NEEDED
Upgrade to 1 M

## Slide 7: Congestion Control Overview
How fast should a sending host transmit data?
  Not too fast, not to slow, just right…
Should not be faster than the sender’s share
  Bandwidth allocation
Should not be faster than the network can process
  Congestion control
Congestion control & bandwidth allocation are separate ideas, but frequently combined

## Slide 8: Fair Bandwidth Allocation
How much bandwidth should each flow from a source to a destination receive when they compete for resources?
  What is a “fair” allocation?
Router
Source
2
Source
1
Source
3
Router
Router
Destination
2
Destination
1
10Mbps
4Mbps
10Mbps
6Mbps
100Mbps
10Mbps

## Slide 9: Congestion
Buffer intended to absorb bursts when input rate > output
But if sending rate is persistently > drain rate, queue builds
Dropped packets represent wasted work; goodput < throughput
Destination
1.5-Mbps T1 link
Router
Source
2
Source
1
100-Mbps FDDI
10-Mbps Ethernet
Packets dropped here

## Slide 10: Uncontrolled congestion?
Network Load
Throughput
Latency
Congestion
collapse
Loss due to
Congestion

## Slide 11
A
B
C D
WHY CONGESTION COLLAPSE CAN OCCUR
All packets go one hop and get dropped because of congestion
So no packets make progress. Goodput goes to 0,
Like gridlock in LA but more like livelock here.

## Slide 12: Congestion Collapse
Rough definition: “When an increase in network load produces a decrease in useful work”
Why does it happen?
  Sender sends faster than bottleneck link speed
  Packets queue until dropped
  In response to packets being dropped, sender retransmits
  All hosts repeat in steady state…

## Slide 13: Mitigation Options
Increase network resources
  More buffers for queuing
  Increase link speed
  Pros/Cons of these approaches?
Reduce network load (TCP strategy)
  Send data more slowly
  How much more slowly?
  When to slow down?

## Slide 14: Designing a Control Scheme
Open loop
  Explicitly reserve bandwidth in the network in advance
Closed loop (TCP Strategy)
Respond to feedback and adjust bandwidth allocation
Network-based
  Network implements and enforces bandwidth allocation
Host-based (TCP Strategy)
  Hosts are responsible for controlling their sending rate

## Slide 15
DETECT CONGESTION
FEEDBACK INFORMATION TO THE SOURCE
SOURCE ADJUSTS WINDOW: INCREASE POLICY DECREASE POLICY
TWO INTERESTING CASES:
  HOW A SOURCE REACHES STEADY STATE.
  HOW A SOURCE REACTS TO A NEW SOURCE TO PROVIDE A FAIR ALLOCATION.
CONGESTION AVOIDANCE VERSUS CONGESTION CONTROL
S
1 M
19.2
19.2
FEEDBACK CONGESTION CONTROL
D
New source

## Slide 16: Proactive vs. Reactive
Network Load
Throughput
Latency
“Knee”
“Cliff”
Congestion
collapse
Congestion avoidance: try to stay to the left of the knee
Congestion control: try to stay to the left of the cliff
Loss due to
Congestion

## Slide 17: Detecting Congestion
Explicit congestion signaling
  Source Quench: ICMP message from router to sender
  DECBit / Explicit Congestion Notification (ECN):
    Router marks packet based on queue occupancy (i.e. indication that packet encountered congestion along the way)
    Receiver tells sender if queues are getting too full
Implicit congestion signaling
  Packet loss
    Assume congestion is primary source of packet loss
    Lost packets indicate congestion
  Packet delay
    Round-trip time increases as packets queue
    Packet inter-arrival time is a function of bottleneck link

## Slide 18: Throttling Options
Window-based (TCP)
  Constrain number of outstanding packets allowed in network
  Increase window to send faster; decrease to send slower
  Pro: Cheap to implement, good failure properties
  Con: Creates traffic bursts (requires bigger buffers)
Rate-based (many streaming media protocols)
  Two parameters (period, packets)
  Allow sending of x packets in period y
  Pro: smooth traffic
  Con: fine-grained per-connection timers, what if receiver fails?

## Slide 19: Choosing a Send Rate
Ideally: Keep equilibrium at “knee” of power curve
  Find “knee” somehow
  Keep number of packets “in flight” the same
  Don’t send a new packet into the network until you know one has left (I.e. by receiving an ACK)
  What if you guess wrong, or if bandwidth availability changes?
Compromise: adaptive approximation
  If congestion signaled, reduce sending rate by x
  If data delivered successfully, increase sending rate by y
  How to relate x and y? Most choices don’t converge…

## Slide 20: TCP’s Probing Approach
Each source independently probes the network to determine how much bandwidth is available
  Changes over time, since everyone does this
Assume that packet loss implies congestion
  Since errors are rare; also, requires no support from routers
Sink
45 Mbps T3 link
Router
Source
100 Mbps Ethernet

## Slide 21: Basic TCP Algorithm
Window-based congestion control
  Unified congestion control and flow control mechanism
  rwin: advertised flow control window from receiver
  cwnd: congestion control window
    Estimate of how much outstanding data network can deliver in a round-trip time
  Sender can only send MIN(rwin,cwnd) at any time
Idea: decrease cwnd when congestion is encountered; increase cwnd otherwise
  Question: how much to adjust?

## Slide 22: Congestion Avoidance
Goal: Adapt to changes in available bandwidth
Additive Increase, Multiplicative Decrease (AIMD)
  Increase sending rate by a constant (e.g. MSS)
  Decrease sending rate by a linear factor (e.g. divide by 2)
Rough intuition for why multiplicative is good
  One source reaches steady state window of 24
  New source comes up and starts with window of 1
  When both increase and detect congestion, first source cuts to 12 and other to 1. Eventually they equalize. Fairness!

## Slide 23: TCP Bandwidth Probing
TCP uses AIMD to adjust congestion window
  Converges to fair share of bottleneck link
  Increases modestly in good times
  Cuts drastically in bad times
But what rate should a TCP flow use initially?
  Need some initial congestion window
  We’d like to TCP to work on all manner of links
  Need to span 6+ orders of magnitude, e.g., 10 K to 10 Gbps.
  Starting too fast is catastrophic! So start with cwnd = 1

## Slide 24: Slow Start
Goal: quickly find the equilibrium sending rate
Quickly increase sending rate until congestion detected
  Remember last rate that worked and don’t overshoot it
TCP Reno Algorithm:
  On new connection, or after timeout, set cwnd=1 MSS
  For each segment acknowledged, increment cwnd by 1 MSS
  If timeout then divide cwnd by 2, and set ssthresh = cwnd
  If cwnd >= ssthresh then exit slow start
Why called slow? Its exponential after all…

## Slide 25
10
1
S
D
Linear
threshold
Timeout
Window
(cwnd)
Slow Start
Time
Fast Retransmit
TCP CONGESTION CONTROL SUMMARY

## Slide 26: Slow Start Example
1
2
Ack 2
3
Ack 3
4
5
6
7
cwnd=1
cwnd=2
cwnd=4
cwnd=8
Sender
Receiver
Ack 4
Ack 5
Ack 6
Ack 7
Ack 8

## Slide 27: Basic Mechanisms
Timeout
ssthresh
Slow start
Congestion
avoidance

## Slide 28: Fast Retransmit & Recovery
Fast retransmit
  Timeouts are slow (default often 200 ms or 1 second)
  When packet is lost, receiver still ACKs last in-order packet
  Use 3 duplicate ACKs to indicate a loss; detect losses quickly
    Why 3? When wouldn’t this work?
Fast recovery
  Goal: avoid stalling after loss
  If there are still ACKs coming in, then no need for slow start
  If a packet has made it through -> we can send another one
  Divide cwnd by 2 after fast retransmit
  Increment cwnd by 1 MSS for each additional duplicate ACK

## Slide 29: Fast Retransmit Example
1
2
Ack 2
3
4
5
6
7
Sender
Receiver
Ack 4
Ack 4
Ack 4
Ack 4
Ack 4
Ack 3
4
3 Dup
Acks
Fast
retransmit
Fast recovery
(increase cwnd by 1)
8

## Slide 30: More Sophistication
Fast recovery

## Slide 31: Short Connections
Short connection: only contains a few pkts
How do short connections and Slow-Start interact?
  What happens when a packet is lost during Slow-Start?
  What happens when the SYN is dropped?
Bottom line: Which packet gets dropped matters a lot
  SYN
  Slow-Start
  Congestion avoidance
Do you think most flows are short or long?
Do you think most traffic is in short flows or long flows?

## Slide 32: Open Issues
TCP is designed around the premise of cooperation
  What happens to TCP if it competes with a UDP flow?
  What if we divide cwnd by 3 instead of 2 after a loss?
There are a bunch of magic numbers
  Decrease by 2x, increase by 1/cwnd, 3 duplicate acks, initial timeout = 3 seconds, etc.
But overall it works really well!
  Still being constantly tweaked…

## Slide 33: TCP CC Summary
TCP Probes the network for bandwidth, assuming that loss signals congestion
The congestion window is managed with an additive increase/multiplicative decrease policy
  It took fast retransmit and fast recovery to get there
  Fast recovery keeps pipe “full” while recovering from a loss
Slow start is used to avoid lengthy initial delays
  Ramp up to near target rate, then switch to AIMD

## Slide 34
10
1
S
D
Linear
threshold
Timeout
Window
(cwnd)
Slow Start
Time
Fast Retransmit
TCP CONGESTION CONTROL SUMMARY

## Slide 35: TCP + Router Scheduling
So far we’ve done flow-based traffic policing
  Limit the rate of one flow regardless of the load in the network
In general, need scheduling at routers as well!
  Dynamically allocate resources when multiple flows compete
  Give each “flow” (or traffic class) own queue (at least theoretically)
Weighted fair queuing
  Schedule round-robins among queues in proportion to some weight parameter. Deficit Round Robin

## Slide 36: Why we need router scheduling
Bottleneck link
(10 Mbps)
1 UDP (10 Mbps) and 31 TCPs sharing a 10 Mbps line
UDP (#1) - 10 Mbps
TCP (#2)
TCP (#32)
.
.
.
UDP (#1)
TCP (#2)
TCP (#32)
.
.
.

## Slide 37: UDP vs. TCP w/FIFO

## Slide 38: TCP vs. UDP w/Fair Queuing

## Slide 39: (Weighted) Fair Queuing
Flow 1
Flow 2
Flow n
I/P
O/P
Deficit Round Robin is
Often used. Shreedhar
And Varghese

## Slide 40: How DRR works

## Slide 41: After sending packet

## Slide 42
10
1
S
D
DECbit/ECN sets a congestion bit
RED randomly drops a packet
WHY ROUTERS ALSO DO RANDOM EARLY DETECT
Q: Why would a router drop a perfectly good packet even if has buffer space
A: As an early form of congestion warning if one does not have a congestion bit. Many IP routers have such a bit today, called the ECN bit

## Slide 43: Some new ideas
HTTP Pipelining: To reduce latency browser opens up multiple connections. Still slow over TCP.
QUIC: Layered below HTTP and above TCP, places multiple streams in a single connection. Finesses slow start. Loss on one stream does not interrupt other stream. Avoids extra handshakes for TLS
TCP fluctuates too much. New protocols like DCTCP adjust more smoothly in Microsoft Data Centers. Also used by Apple

## Slide 44: Lecture Summary
Unlike a reliable data link we also need to match speed of sender to receiver AND the whole network
TCP increases and decreases its window using Slow Start + AIMD, decreasing on loss or ECN
Needs to be accompanied by router scheduling mechanisms like DRR and RED/ECN setting
TCP fluctuates too much. New protocols like DCTCP adjust more smoothly in Microsoft DCs.