## Slide 1: Naming: why so many?
CS 118: Computer Networks
George Varghese
Some slides courtesy Alex Snoeren

## Slide 2: But first a quick routing review

## Slide 3: Link State, DV suboptimal
Shortest paths only:
  Lots of bandwidth left on the table
One Size fits all
  Does not differentiate traffic classes like Voice over IP, video
Hard to express policies
  Many large organizations use BGP to finesse this lacl
New: Software Defined Networks within organizations
  Google B4 and Microsoft SWAN have all routers send local info (as in LSPs) to a central site that can use centralized algorithms to calculate second shortest routes, routes for each traffic class etc
  In some sense, replacing protocols by algorithms

## Slide 4: Wide Area SDN (B4/SWAN)
Google WAN
Central SDN Controller
Extra info like congestion, traffic types
User
Data Center 1
Data Center 2
Search Traffic (low latency)
Backups (high bandwidth)

## Slide 5: BGP Review: Routes flow from sources
Princeton CS router sends route to Border Router
Border router sends aggregate prefix route to ISP
Left border router in ATT sends route to right Border
AS 88
Princeton
AS 7018
AT&T
AS 11
Harvard
192.0.2.1
128.112.0.0/16
AS path = 7018 88
Next Hop = 12.127.0.121
12.127.0.121
128.112.0.0/16
AS path = 88
Next Hop = 192.0.2.1
128.112.8.0/24, CS
Cost = 1
Next Hop = 123.2.2.1
Default Route *
Cost = 1
Next Hop = 131.1.1.1

## Slide 6: Review: Data Packets flow in reverse
The best routes are installed in the Forwarding Table
Now a data packet to Princeton CS flows in reverse . .
For traffic to Harvard, need routes from Harvard
AT&T
Harvard
128.112.0.0/16  12.127.0.121
128.112.0.0/16  192.0.2.1
128.112.8.0/24  123.2.2.1
* -> 131.1.1.1
Forwarding Table
Princeton

## Slide 7: So what does BGP do
Only way in distance vector to tune routes is via link cost
In BGP, one can “control” routes in more complex ways
Choose between routes based on attributes and local network policy specified in config files at routers
Princeton Prefix
Path 2, Atttributes 2
Princeton prefix
Path 1. Attributes 1
Princeton prefix
Attributes 3 (or drop)
Princeton

## Slide 8: Common uses of Attributes
Local Preference
  Prioritize route received on an interface (e.g., cheaper ISP)
AS Path Length
  Rough measure of shortest (count of networks to destination)
MED
  Hint to one’s ISP as to how to split traffic when there are multiple exits to the ISP
Community
  A way to tag all routes of a specific type so that remote routers can act on tag (say drop route) based on one community value as opposed to a long list of prefixes

## Slide 9: Default Route Selection
First Local Preference
  Operator knows best
AS Path Length
  After that shortest path (roughly speaking) makes sense
MED
  Other things being equal, honor MED priorities
eBGP over iBGP
  Other things being equal, a route from an external border router makes more sense than one from an internal router
Shortest IGP weight (from Link State, or Distance Vector)
  Other things being equal, pick shortest cost to border router

## Slide 10: BGP is suboptimal
Local knowledge only:
  your neighbors best routes may not be your best
AS Path Length
  Does not measure real distance or latency
Other Metrics
  May care about cost etc. and have to hack BGP attributes
New: Software Defined Networks within organizations
  Google Espresso has BGP speakers but they send all BGP messages to a central cluster that also does measurements and picks more globally optimal route to customer ISPs
  Read Google blog: Search for “Google Blog Espresso”

## Slide 11: Google Espresso
Google WAN
Central SDN Controller
Level Crossing
MCI
BGP
BGP
Extra info like congestion

## Slide 12: Back to naming: why so many? How assigned? How mapped?
ccle.ucla.edu
131.71.29.8
58:B0:35:F2:3C:D9

## Slide 13: Similar in Operating Systems
Naminglecture.pptx
File Descriptor = 10
Track 5, Sector 10
ccle.ucla.edu
131.71.29.8
58:B0:35:F2:3C:D9

## Slide 14: Three topics in naming
How to get a an IP address to get started (DHCP)
How to map from user-friendly names like ccle.ucla.edu to an IP address to send (DNS)
How to build a large private network with only 1 assigned public IP address: magic. No (NAT).

## Slide 15
Browser points to ccle.ucla.edu
LAPTOP
CCLE
IP
ROUTER
Q: How do we go from ccle.edu to an IP address for CCLE
A: App (browser) maps using the Domain Name Service
131.71.29.8
User types “http:ccle.ucla.edu”

## Slide 16
TCP’S VIEW OF THE WORLD
CCLE
LAPTOP
NETWORK
Well−known Extension: 80
Local Extension
Socket: 3345
11
131.71.29.1
Q: How do IP addresses get assigned
A: DHCP (Dynamic Host Control Protocol
131.71.29.8

## Slide 17: Layers of Identifiers
Host name (e.g., ccle.ucla.edu)
  Used by humans to specify host of interest
  Unique, selected by host administrator
  Hierarchical, variable-length string of alphanumeric characters
IP address (e.g., 131.71.29.8)
  Used by routers to forward packets
  Unique, topologically meaningful locator
  Hierarchical namespace of 32 bits
MAC address (e.g., 58:B0:35:F2:3C:D9)
  Used by network adaptors to identify interesting frames
  Unique, hard-coded identifier burned into network adaptor
  Flat name space (of 48 bits in Ethernet)

## Slide 18: Naming Hierarchies
Host name: ccle.ucla.edu (human readable)
  Domain: registrar for each top-level domain (e.g., .edu)
  Host name: local administrator at UCLA assigns to each host
IP addresses: 131.71.70.238 (for scalable routing)
  Prefixes: ICANN, regional Internet registries, and ISPs
  Hosts: static configuration, or dynamic using DHCP
MAC addresses: 58:B0:35:F2:3C:D9 (for unique ID)
  OIDs (first 3 bytes): assigned to vendors by the IEEE
  Adapters: assigned by the vendor from its block

## Slide 19: Mapping Between Identifiers
Domain Name System (DNS):
  Given a host name, provide the IP address
  Given an IP address, provide the host name
Address Resolution Protocol (ARP)
  Given an IP address, provide the MAC address
  To enable communication within the Local Area Network
Dynamic Host Configuration Protocol (DHCP)
  Automates host boot-up process
  Given a MAC address, assign a unique IP address
  … and tell host other stuff about the Local Area Network

## Slide 20: Address Resolution Protocol
Recall: every node maintains an ARP table
  (IP address, MAC address) pair
Consult the table when sending a packet
  Map destination IP address to MAC address
  Encapsulate and transmit the data packet
What if the IP address is not in the table?
  Broadcast: “Who has IP address x.x.x.x?”
  Response: “MAC address yy:yy:yy:yy:yy:yy”
  Sender caches the result in its ARP table
Have you started your Programming Assignment yet?

## Slide 21: Whence come IP Addresses?
You already have a bunch from the days when you called Jon Postel and asked for them (e.g. UCLA!)
You get them from another provider
  E.g. buy service from Sprint and get a /24 from one of their address blocks
You get one directly from a routing registry
  ARIN: North America, APNIC (Asia Pacific), RIPE (Europe), LACNIC (Latin America), AFRINIC (Africa)
  Registries get address from IANA (Internet Assigned Numbers Authority)

## Slide 22: How Do You And I Get One?
Well from your provider!
But how do you know what it is?
Manual configuration
  They tell you and you type that number into your computer (along with the default gateway, DNS server, etc.)
Automated configuration
  Dynamic Host Resolution Protocol (DHCP)

## Slide 23: Bootstrapping Problem
Host doesn’t have an IP address yet
  So, host doesn’t know what source address to use
Host doesn’t know who to ask for an IP address
  So, host doesn’t know what destination address to use
Solution:
  shout on LAN using well known DHCP multicast address (like ARP, but not broadcast) to discover server who can help
  Install DHCP server on the LAN to answer distress calls
host
host
host
...
DHCP server
Notes: UDP packet. SRC of 0.0.0.0 and DST of 255.255.255.255

## Slide 24: DHCP
Broadcast-based LAN protocol algorithm
  Host broadcasts “DHCP discover” on LAN (e.g. Ethernet broadcast)
  DHCP server responds with “DHCP offer” message
  Host requests IP address: “DHCP request” message
  DHCP server sends address: “DHCP ack” message w/IP address
Easy to have fewer addresses than hosts (e.g. UCLA wireless) and to renumber network (use new addresses)
What if host goes away (how to get address back?)
  Address is a “lease” not a “grant”, has a timeout
  Host may have different IP addresses at different times?

## Slide 25: Domain Name System (DNS)
Distributed administrative control
  Hierarchical name space divided into zones
  Distributed over a collection of DNS servers
Hierarchy of DNS servers
  Root servers
  Top-level domain (TLD) servers
  Authoritative DNS servers
Performing the translations
  Local DNS servers
  Resolver software

## Slide 27: DNS: Distributed Database
com
edu
org
ac
uk
zw
Unnamed root
bar
west
east
foo
my
ac
cam
usr
generic domains
country domains
my.east.bar.edu
usr.cam.ac.uk

## Slide 28: DNS Root Servers
13 root servers (see http://www.root-servers.org/)
  Labeled A through M
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software C. Palo Alto, CA (and 17 other locations)
I Netnod, Stockholm (plus 3 other locations)
K RIPE London (+ Amsterdam, Frankfurt)
M WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign, ( 11 locations)

## Slide 29: Using DNS
Local DNS server (“default name server”)
  Usually near the end hosts who use it
  Local hosts configured with local server (e.g., /etc/resolv.conf) or learn the server via DHCP
Client application
  Extract server name (e.g., from the URL)
  Do gethostbyname() to trigger resolver code
Server application
  Extract client IP address from socket
  Optional gethostbyaddr() to translate into name

## Slide 30: Example
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

## Slide 31: Akamai: Fake out DNS to find “closest” copy of Service
Central Akamai Servers
Extra info like congestion
You
Service (Seattle)
Service (Chicago)
Service (LA)
Local DNS
Root DNS

## Slide 32: Reliability
DNS servers are replicated
  Name service available if at least one replica is up
  Queries can be load balanced between replicas
UDP used for queries
  Need reliability: must implement this on top of UDP
  Try alternate servers on timeout
  Exponential backoff when retrying same server
Cache responses to decrease load
  Both at end hosts and local servers

## Slide 33: Private Address Space
Sometimes you can’t get/don’t want IP addresses
  An organization wants to change service providers without having to renumber its entire network
  A network may be unable obtain (or cannot afford) enough IP addresses for all of its hosts. Recall IP address depletion.
IP provides private address space anyone can use
  10/8, 192.168/16, 172.16.0/20
  These addresses are not routable—Internet routers should drop packets destined to these so-called bogons
What good are they if can’t use them on the Internet?

## Slide 34: Network Address Translation
Gateway router can rewrite IP addresses as packets leave or enter a given network
  I.e., replace private addresses with public ones
  Router needs to see and update every packet
Maintains a mapping of private-to-public addresses
  Simple case is a one-to-one mapping
  Anytime network changes provider, just update mapping table
  In more clever scenarios, can map a set of private addresses to a smaller set of public addresses
  In the extreme map the entire private network to one public IP!

## Slide 35: IP Masquerading
A.K.A. Network Address and port Translation (NApT), Port Address Translation (PAT), or, colloquially, just NAT.
Entire local network uses just one IP address as far as outside world is concerned:
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus).

## Slide 36: A NAT’d Network
10.0.0.4
10.0.0.2
10.0.0.3
10.0.0.1
138.76.29.7
local network
(e.g., home network)
10.0.0.0/8
rest of
Internet
Packets with source or
destination in this network
have 10.0.0.0/8 address for
source, destination (as usual)
All packets leaving local
network have same single source NAT IP address: 138.76.29.7,
different source port numbers

## Slide 37: NA(p)T Example
10.0.0.4
10.0.0.2
10.0.0.3
S: 10.0.0.4:3345
D: 132.239.8.45:80
1
10.0.0.1
138.76.29.7
1: host 10.0.0.4
sends packet to
132.239.8.45:80
NAT translation table
WAN side addr LAN side addr
138.76.29.7:5001 10.0.0.4:3345
…… ……
S: 132.239.8.45:80
D: 10.0.0.4:3345
4
S: 138.76.29.7:5001
D: 132.239.8.45:80
2
2: NAT router
changes packet
source addr from
10.0.0.1:3345 to
138.76.29.7:5001,
updates table
S: 132.239.8.45:80
D: 138.76.29.7:5001
3
3: Reply arrives
dest. address:
138.76.29.7:5001
4: NAT router
changes packet
dest addr from
138.76.29.7:5001 to 10.0.0.4:3345

## Slide 38: NAT Challenges
End hosts may not be aware of external IP address
  Some applications include IP addresses in application data
  Many NATs will inspect/rewrite certain protocols, e.g., FTP
NAT’d end hosts are not reachable from the Internet
  All connections must be initiated from within private network
  Many protocols for NAT traversal to get around this

## Slide 39: NAT: What’s the trick?
How can we can we communicate with multiple hosts in a private network using 1 public IP
  Hack: We use the TCP Port numbers to disambiguate
  So we are extending IP space from 32 to 32 + 32 = 64!
But like all hacks it causes issues (see challenges)
  Right solution is IPv6, 128 bit addresses
  Enough everyone and their devices without hacks like NAT
  IPv6 deployment increasing: over 9 million domain names and 23% of all networks do both IPv6 and v5.
  Big pushes in Japan and India

## Slide 40: Summary
IP to MAC Address mapping
  Dynamic Host Configuration Protocol (DHCP)
  Address Resolution Protocol (ARP)
Domain Name System
  Distributed, hierarchical database
  Distributed collection of servers
  Caching to improve performance
  Hacks like Akamai to find “closest” service