## Slide 1: CS174A Lecture 13

## Slide 2: Announcements & Reminders
2/25/24: A3 due; will be discussed during this week’s TA session
3/06/24: A4 due; will be discussed during this week’s TA session
3/07/23: Prof Demetri’s presentation (Zoom, no recording)
Team Project Timelines: see project info document on Canvas
  Team project grade increased from 150 to 175 (download latest team project info)
3/19/24: Final exam, 6:30-8:15 PM, in person, location TBD
  Final exam grade reduced from 150 to 125 (download latest syllabus)
  Study guide and book exercises posted
  3/18 & 3/19: Office hours, Noon-1PM

## Slide 3: Discussion Session This Friday
Team project
Assignment #3
Assignment #4

## Slide 4: Last Lecture Recap
Barycentric Coordinates, Bilinear Interpolations
Flat and Smooth Shading

## Slide 5: Next Up
Non-Photorealistic Rendering
Global Illumination
Mappings: Texture, Bump, Displacement, Environment
Shadows
  Shadow volumes
  2-pass z-buffer algorithm
Hidden Surface Removal
  Ray casting

## Slide 6: Shading Recap
Flat Shading
  Illuminate a poly only once
  No interpolation
Gouraud Shading
  Illuminate vertices of poly
  Interpolate colors at vertices
Phong Shading
  Illuminate each point inside poly
  Interpolate normals at vertices
Illumination in WS/ES, interpolation in SS

## Slide 7: Illumination Recap
  I = ka * Ia * Od + fatt * kd * Ip * (N·L) * Od + fatt * ks * Ip * (R·V)n
Material Properties: ka, kd, ks: ambient, diffuse, specular reflection coefficients of object Od: color of object Ia: intensity of ambient light Ip: intensity of point light
n: specular exponent
Geometric Properties: N: orientation of object at point being illuminated L: depends on location of point and light R: depends on N and L V: depends on location of point and eye fatt: depends on distance between point and light
Aatt: depends on distance between point and eye

## Slide 8: Non-Photorealistic Shading
Cartoon like effects
Color = (N·L > 0.5) ? Color1 : Color2
Color changes with object’s shape and light’s position
Silhouette: (N·V < 0.01) ? Black : Color

## Slide 9: Global Illumination
Ray Tracing: shadows, reflections, refractions
Radiosity
  Based upon light energy conservation
  Requires solution of a large set of equations involving all surfaces

## Slide 10: Mappings
Texture Mapping
Bump Mapping
Displacement Mapping
Environment Mapping
Procedural Mapping

## Slide 11: Texture Mapping
AKA Pattern mapping
Map a digitized image onto a poly face
Individual elements are called Texels
u,v and s,t coordinates
Use texel color as diffuse color
Texture replication (as in A4)

## Slide 12: Texture Mapping: Aliasing
Due to high-frequency patterns
Mip Mapping (as in A4); MipMap, MipMap example

## Slide 13: Multi-Texturing
Apply multiple textures on the same object – blend

## Slide 14: Bump & Displacement Mappings
Displacement Mapping:
  Displace point on surface of object
  Change object’s geometry
P’ = P + B * N
Bump mapping
  Distort normal to simulate bump without altering object’s geometry
Bu,Bv = partial derivatives of B wrt u,v
Ps,Pt = partial derivatives of P wrt s,t

## Slide 15: Displacement Mapping
Points actually move
Requires hidden surface removal
Bump vs. Displacement 1
Bump vs. Displacement 2

## Slide 16: Environmental Mapping
AKA Reflection Mapping
Use polar (or spherical) coordinates of reflected ray to map
Map defined usually on 6 faces of a box (cube map) or a sphere

## Slide 17: Environmental Mapping
More examples
I = ambient + diffuse + specular + kr * Ir
  kr: coefficient of reflection
  Ir: reflection intensity

## Slide 18: Shadow Algorithms
Types
  Object precision: shadow volume method
  Image precision: 2-pass z-buffer method
Main Idea
  P is not visible from light source ⇔ P is in shadow
Strategy
  Identify areas on polys which are not directly visible from light source
  Mark these areas
  Do HSR from eye position
  Areas marked for shadow are rendered only with ambient light

## Slide 19: Shadow Volume Method
Create a shadow volume for each front facing poly
Put shadow volume in poly database
Do parity test to determine if a visible point is in shadow
    Initial value = # of shadow volumes containing eye position
    Increment for front-facing shadow poly
    Decrement for back-facing shadow poly
    If parity > 0 ⇒ point is in shadow

## Slide 20: Shadow Volume Method

## Slide 21: 2-Pass Z-Buffer Method
Aka Shadow Map method
Do z-buffer (full) from light position
  store results in shadow buffer or depth buffer
Do z-buffer (scanline or full) from eye position
  For each (visible) pixel in scanline
    Do inverse map point to WS
    Map to SS of shadow buffer
    Compare z with that of shadow buffer at x,y
    If shadow_buf[x][y] < z, then point is in shadow

## Slide 22: 2-Pass Z-Buffer Method
First Pass: from light’s position

## Slide 23: 2-Pass Z-Buffer Method
Second Pass: from eye’s position
ShadowMap Viewer

## Slide 24: 2-Pass Z-Buffer Method (Contd.)
Advantages
  Simple to implement
Disadvantages
  Shadow distant from light source may appear blocky
  A large size of shadow-buffer is required
  Depth buffer bit resolution – usually 8-bit
  Umbra vs. penumbra