## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3: RISC-V Control and Status Instructions
User-level CSR Table
Standard mapping
  FPU flags
  Cycle
  Time
  Instret
  HPM Counters
Notes: HPM: hardware performance monitoring counter

## Slide 4: RISC-V Control and Status Instructions
Privilege Levels: defines the level of access that software has to the processor and system resources. They enable:
  Access control: control what an application can do
  Security: run an application in isolation from others

## Slide 5: RISC-V Control and Status Instructions
RIS-V Privilege Levels
  User-level (U)
  Hypervisor (H)
  Supervisor (S)
  Machine-level (M)
Hypervisor
H

## Slide 6: RISC-V Control and Status Instructions
CSRs Privilege Mapping
Why reserving dedicated bits for level?
Notes: Reserving the bit simplifies the hardware decoding of the CSR address and enables the hardware to perform privileged detection in parallel.

## Slide 7: RISC-V Control and Status Instructions
User-level (U): User-level CSRs are accessible from the user mode, which is the least-privileged mode of operation. These registers typically contain information or controls that are safe to expose to user applications, such as performance counters that can be read without compromising system integrity.

## Slide 8: RISC-V Control and Status Instructions
Supervisor-level (S): Supervisor mode is used by operating systems to control system resources and manage user applications. It has a lower privilege than M-mode but can still perform system-level tasks.

## Slide 9: RISC-V Control and Status Instructions
Hypervisor-level (H): Hypervisor mode is an optional privilege level introduced in newer versions of the RISC-V specification, designed for virtualization. It sits between M-mode and S-mode and is used to run and manage virtual machines.

## Slide 10: RISC-V Control and Status Instructions
Machine-level: Machine-level CSRs are accessible from machine mode, which is the most privileged mode of operation. These registers are used for controlling low-level, sensitive aspects of the hardware, such as interrupt handling, exception handling, and access to physical memory.
Note: default level for low-level embedded CPUs

## Slide 11: RISC-V Control and Status Instructions
How is the privilege level set/modified?
CPU starts at machine level (M)
S/W can use CSR mstatus to lower the privilege level
CPU can use exception handling to increase the privilege level
RISC-V mret, sret, uret are system return instructions for switching back to previous privilege level after exception handling.

## Slide 12: RISC-V Control and Status Instructions
How is the privilege level enforced?
If software running at a lower privilege level attempts to execute a privileged instruction, or a protected address space, or privileged interrupt, the processor will raise an exception

## Slide 13: RISC-V Control and Status Instructions
Timers and counters
  64-bit registers
  RD_CYCLE: total cycle time
  RD_TIME: wall-clock time
  RD_INSTRET: total instructions
Notes: walltime is the actual time taken from the start of a computer program to the end

## Slide 14: RISC-V Control and Status Instructions
Timers and counters
  How to read RD_CYCLE on 32-bit machine?
  Why could this be challenging?
    Counter 32-bit overflow
  Solution
    Read Low 32-bit
    Read high 32-bit

## Slide 15: RISC-V Control and Status Instructions
Assembly code
  csrrs x2, cycle, x0
  csrrs x3, cycleh, x0
What timing issue may emerge from the above code?
  x2 and x3 may not match
  Hundreds of CPU cycles can happen between the two calls
  Reading cycleh could happen after cycle 32-bit overflow

## Slide 16: RISC-V Control and Status Instructions
Solution
  loop: csrrs x3, cycleh, x0
  csrrs x2, cycle, x0
  csrrs x4, cycleh, x0
  bne x3, x4, loop
How does this work?
  It takes a while for cycleh change
  The loop handle the overflow cases

## Slide 17: RISC-V Registers
32 general-purpose registers
Separate floating-point registers
Register r0=0x0 - why?
Hidden PC register
  accessible via CSRs only
Notes: Why Zero?
- predominant value for comparisons and arithmetic operations
- simple instruction decoding when no registers is needed
- simple register file access logic when no register is needed

## Slide 18: RISC-V Registers
ABI Calling convention:
Arguments: a0-7
Return: r0
Temporaries: t0-6
Saved registers: s0-11
Who back up registers during calls?
  Caller/parent
  or Callee/child
Notes: Why Zero?
- predominant value for comparisons and arithmetic operations
- simple instruction decoding when no registers is needed
- simple register file access logic when no register is needed

## Slide 19: RISC-V Registers
Return address (ra)
  Store the return address during function calls
  Hold the next PC of the caller
  Example: what is the value of ra when bar() is executing?
void bar() {
<print(“hello”);>
}
void foo() {
bar(); // call bar()
<print(“world\n”);>
}
# foo
0F00: ???
0F04: ???
0F08: jal ra, 0xF80
0F0C: ???
…
# bar
0F80: ???
0F84: ???
0F88: ???
0F8C: jalr x0, 0(ra)
Notes: ra will hold the next instruction address when calling jal.

## Slide 20: RISC-V Registers
Stack pointer (sp)
  Used for managing function call stack.
  The stack holds function’s temp variables that could not fit into registers.
  Initialized to a starting location at boot time.
  Stack base address decided by startup code.
  la is a “load address” pseudo instruction
    resolve to one or multiple RISC-V native instructions
    depending on address value
# stack initialization
la gp, STACK_BASE_ADDR

## Slide 21: RISC-V Registers
Stack pointer (sp)
  Example: A program uses 16 bytes of stack storage.
# Assume that x5 and x6 contain values that we want to preserve
# First, we'll adjust the stack pointer to allocate 8 bytes of space
addi sp, sp, -8 # Decrement the stack pointer by 8 bytes
# Now we'll store x5 and x6 onto the stack at the allocated space
sw x5, 0(sp) # Store x5 at the beginning of the allocated space
sw x6, 4(sp) # Store x6 right after x5
# ... the code can now use x5 and x6 for other operations…
add x5, x0, x1
add x6, x0, x1
# To restore the values of x5 and x6, we'll load them back from the stack
lw x5, 0(sp) # Load x5 from the stack
lw x6, 4(sp) # Load x6 from the stack
# Finally, we'll adjust the stack pointer back to free the 8 bytes
addi sp, sp, 8 # Increment the stack pointer by 8 bytes to restore its original value

## Slide 22: RISC-V Registers
Global pointer (gp)
  Points to the middle of a global data segment
  Why the middle?
    Reduces instruction’s immediate value when accessing global variables
    Recall LD/ST instruction use signed immediate offsets
  Example C code:
int counter = 10;
void increment_counter() {
counter++;
}
int main() {
increment_counter();
return 0;
}

## Slide 23: RISC-V Registers
Global pointer (gp)
  Initialized to a starting location at boot time.
  Linker computes and exports __global_pointer macro to startup code
  la is a “load address” pseudo instruction
    resolve to one or multiple RISC-V native instructions
    depending on address value
# stack initialization
la gp, __global_pointer

## Slide 24: RISC-V Registers
Global pointer (gp)
  Assembly program
increment_ counter :
lw t1, 0(gp) # Load current value of counter
addi t1, t1, 1 # Increment the value
sw t1, 0(t0) # Store the incremented value back to counter
ret
main:
call increment_ counter
li a0, 0 # Set return value of main to 0
ret

## Slide 25: RISC-V Registers
Thread pointer (tp)
  used to efficiently access thread-local storage (TLS)
  TLS holds data unique to each thread in a multi-threading environment
  Example:
#include <iostream>
#include <thread>
#include <vector>
thread_local int tl_counter = 0;
void incrementCounter() {
tl_counter++; }
int main() {
std::vector<std::thread> threads;
for(int i = 0; i < 5; ++i) {
threads.push_back(std::thread(incrementCounter));
} for(auto& t : threads) t.join(); return 0;
}

## Slide 26: RISC-V Registers
Thread pointer (tp)
  Initialized to a starting location at boot time.
  Linker computes and exports __tcb_aligned_size macro to startup code.
csrr t0, VX_CSR_MHARTID
sll t1, t0, STACK_LOG2_SIZE #
sub sp, sp, t1
# set thread pointer register
# ensure cache line alignment
la t1, __tcb_aligned_size # allocated TLS size
mul t0, t0, t1
la tp, _end + 63
add tp, tp, t0
and tp, tp, -64
ret

## Slide 27: RISC-V Registers
Thread pointer (tp)
  Assembly code for incrementCounter()
# Pseudocode for RISC-V assembly to increment a TLS variable
# Assume that the offset of tl_counter within the TLS is known and is 'offset'
incrementCounter:
# Load the address of tl_counter from the thread's TLS using the 'tp' register
addi t0, tp, offset # t0 = address of tl_counter
# Load the current value of tl_counter
lw t1, 0(t0) # t1 = *t0 (the value of tl_counter)
# Increment the value
addi t1, t1, 1 # t1 = t1 + 1
# Store the incremented value back into tl_counter
sw t1, 0(t0) # *t0 = t1
# Return from the function
ret
Notes: .

## Slide 28: Review: Digital Circuits

## Slide 29: Combinational Circuits
Combinational circuits
  Output depends on current inputs only
  Consist of a connection of multiple logic gates
    And/Or/Not

## Slide 30: Combinational Circuits
Combinational circuits
  Example1
From: Quick start Guide to Verilog (© springer Nature Switzerland)

## Slide 31: Combinational Circuits
Combinational circuits
  Example2: multiplexer
From: Quick start Guide to Verilog (© springer Nature Switzerland)

## Slide 32: Sequential Circuits
Sequential circuits
  Output depends on current inputs and prior state
  Need a storage/memory to hold prior state
  e.g. storage element
    D-flip-flops
    RAMs
Notes: RAM: random addressable memory

## Slide 33: Sequential Circuits
D-Flip-flop:
  Digital storage element
  Input is propagated to output at the rising edge of the clock
  Registers are implemented using D-Flip-flops
From: Quick start Guide to Verilog (© springer Nature Switzerland)

## Slide 34: Applications of D-Flip-Flop
D-Flip-flop are use for:
  Data storage
  Data synchronization
  Finite state machines
  Pipelining
  Timing resolution
    Reduce combinational propagation delays
    Improve clock speed
Combinational Logic
Register
clock
Notes: Signal is stronger at the output of D-flip-flop

## Slide 35: Finite State Machines
Definition: State-driven model of computation to design sequential circuits.
Mealy type FSM
  (state, input)  output
  Pros: Smaller number of states
    Due to partial inputs handling
  Cons: Input critical path
    Why?

## Slide 36: Finite State Machines
Moore type FSM
  (state)  output
  Pros: High-speed
    Why?
  Cons: Large number of states
    due to full inputs handling
    can affect circuit size

## Slide 37: Finite State Machines
Moore type FSM
  (state)  output
  Pros: High-speed
    Why?
  Cons: Large number of states
    due to full inputs handling
    can affect circuit size

## Slide 38: Finite State Machines
Example: Serial Bit Sequence Detector
From: Quick start Guide to Verilog (© springer Nature Switzerland)

## Slide 39: Finite State Machines
Example: Serial Bit Sequence Detector
From: Quick start Guide to Verilog (© springer Nature Switzerland)

## Slide 40: RISC-V CPU Implementation

## Slide 41: Basic RISC-V CPU Datapath
RISC-V ISA subset:
Simple hardware
ALU-R
ALU-I
LD/ST
Branch

## Slide 42: Basic RISC-V CPU Datapath
Basic Steps:
Fetch instruction from PC
Register file access
ALU execution
Memory access
Next PC update

## Slide 43: Basic RISC-V CPU Datapath
Next PC calculation:
Program counter stored in PC
Can perform the addition in parallel
While reading the next instruction

## Slide 44: Basic RISC-V CPU Datapath
Register File:
32 total registers (5-bit addressing)
2x 5-bit source register addresses
1x 5-bit destination register address
RegWrite: write enable
How to decode register address?

## Slide 45: Basic RISC-V CPU Datapath
Register File:
How to decode register address?
  No combinational logic needed
  why?

## Slide 46: Basic RISC-V CPU Datapath
Branch operations:
Register access
Immediate generation
Branch target calculation
Branch condition evaluation
Parallelism?
  2-3, 4
Critical path?
  2-3

## Slide 47: Basic RISC-V CPU Datapath
Memory Operations:
Address calculation
Memory access
ALUSrc select
  0: register
  1: immediate

## Slide 48: Basic RISC-V CPU Control Path
CPU control logic:
Main control
  Register File
    RegWrite
    MemtoReg
  ALU
    ALUOp
    ALUSrc
  Data memory
    MemRead
    MemWrite
  Branch
ALU control
  ALU operation