## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3: Homework #3 Questions?

## Slide 4: RISC-V CPU Implementation

## Slide 5: Basic RISC-V CPU Datapath
RISC-V ISA subset:
R-type
I-type
LD/ST
Branch

## Slide 6: Basic RISC-V CPU Datapath
Basic Steps:
Fetch instruction from PC
Register file access
ALU execution
Memory access
Next PC update

## Slide 7: Basic RISC-V CPU Datapath
Next PC calculation:
Program counter stored in PC
Can perform the addition in parallel
While reading the next instruction

## Slide 8: Basic RISC-V CPU Datapath
Register File:
32 total registers (5-bit addressing)
2x 5-bit source register addresses
1x 5-bit destination register address
RegWrite: write enable
How to decode register address?

## Slide 9: Basic RISC-V CPU Datapath
Register File:
How to decode register address?
  No logic needed
  why?

## Slide 10: Basic RISC-V CPU Datapath
Branch operations:
Register access
Immediate generation
Branch target calculation
Branch condition evaluation
Parallelism?
  2-3, 4
Critical path?
  2-3

## Slide 11: Basic RISC-V CPU Datapath
Memory Operations:
Address calculation
Memory access
ALUSrc select
  0: register
  1: immediate

## Slide 12: Basic RISC-V CPU Control Path
CPU control logic:
Main control
  Register File
    RegWrite
    MemtoReg
  ALU
    ALUOp
    ALUSrc
  Data memory
    MemRead
    MemWrite
  Branch
ALU control
  ALU operation

## Slide 13: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
R-Type | 0110011 |  |  |  |  |  | 

## Slide 14: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
R-Type | 0110011 | 1 | 0 | 0 | 0 | 0 | 0

## Slide 15: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
I-Type | 0010011 |  |  |  |  |  | 

## Slide 16: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
I-Type | 0010011 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 17: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
LW | 0000011 |  |  |  |  |  | 

## Slide 18: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
LW | 0000011 | 1 | 1 | 0 | 1 | 0 | 1

## Slide 19: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
SW | 0100011 |  |  |  |  |  | 

## Slide 20: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
SW | 0100011 | 0 | 1 | 0 | 0 | 1 | 0

## Slide 21: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
BEQ | 1100011 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 22: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
R-Type | 0110011 | 1 | 0 | 0 | 0 | 0 | 0
I-Type | 0010011 | 1 | 1 | 0 | 0 | 0 | 0
LW | 0000011 | 1 | 1 | 0 | 1 | 0 | 1
SW | 0100011 | 0 | 1 | 0 | 0 | 1 | 0
BEQ | 1100011 | 0 | 0 | 1 | 0 | 0 | 0
How to determine the type of instruction with minimal logic?

## Slide 23: Basic RISC-V CPU Control Path
Instruction | Opcode | RegWrite | AluSrc | Branch | MemRead | MemWrite | MemtoReg
R-Type | 0110011 | 1 | 0 | 0 | 0 | 0 | 0
I-Type | 0010011 | 1 | 1 | 0 | 0 | 0 | 0
LW | 0000011 | 1 | 1 | 0 | 1 | 0 | 1
SW | 0100011 | 0 | 1 | 0 | 0 | 1 | 0
BEQ | 1100011 | 0 | 0 | 1 | 0 | 0 | 0
R-Type := intrs[4] & instrs[5]
I-Type := intr[4] & ~instr[5]
LW := ~instr[4] & ~instr[5]
SW := ?
BEQ := ?

## Slide 24: Basic RISC-V CPU Control Path
ALUOp?
Only 4 operations:
AND
OR
ADD
SUB
BEQ := (rs1 – rs2)
Instruction | Opcode | Func3 | Func7 | ALU Fn | ALU Op
AND | 0110011 | 000 | 0000000 | ADD | 10
SUB | 0110011 | 000 | 0100000 | SUB | 11
OR | 0110011 | 110 | 0000000 | OR | 01
AND | 0110011 | 111 | 0000000 | AND | 00
ADDI | 0010011 | 000 | xxxxxxx | ADD | 10
ORI | 0010011 | 110 | xxxxxxx | OR | 01
ANDI | 0010011 | 111 | xxxxxxx | AND | 00
LW | 0000011 | 010 | xxxxxxx | ADD | 10
SW | 0100011 | 010 | xxxxxxx | ADD | 10
BEQ | 1100011 | 000 | xxxxxxx | SUB | 11

## Slide 25: Single-Cycle Processor
Single-cycle Processor:
Cycle I
  Instruction memory read
  Control Units produce output
  ALU produces output
  Data memory read
  Next PC calculation
Note: Assume Instruction and data memory read is asynchronous (same cycle), however memory updates are only visible in next cycle.
Advantages?

## Slide 26: Single-Cycle Processor
Single-cycle Processor Advantages:
Simple to design
Efficient design (resource usage)
Limitations?

## Slide 27: Single-Cycle Processor
Single-cycle Processor Limitations:
Weak performance
  Long latency

## Slide 28: Single-Cycle Processor
Single-cycle Processor Latency:
Long propagation delay
  Signal propagation from source to destination
  Source: input or register
  Destination: output or register
Imbalanced datapath
Which path is the longest?
Why it affects latency?

## Slide 29: Single-Cycle Processor
Single-cycle Processor Latency:
How this affect CPU latency?
Longest delay determines the clock speed
CPU clock affects performance
CPU Time = InstCount * CPI * CycleTime
How to reduce propagation delay?

## Slide 30: Single-Cycle Processor
Reducing Propagation Delay
Split the datapath into smaller chunks
Insert registers in between
Update control logic
  Control registers inputs/outputs

## Slide 31: Multi-Cycle Processor
Change to multi-cycle architecture
4 stages
  IF: Instruction Fetch
  ID: Register access
  EX: ALU operation
  MEM: Memory access
  WB: Write back
IF
ID
EX
MM
WB

## Slide 32: Multi-Cycle Processor
Improved Propagation Delay
Longest propagation delay?
  max(IF, ID, EX, MEM, WB)
  Should be smaller
IF
ID
EX
MM
WB
How is the overall performance impacted?

## Slide 33: Multi-Cycle Processor
Multi-cycle Processor Performance
Pros: Cycle Time is reduced
Cons: CPI is increased: a single instruction takes multiple cycles to complete
CPU Time = InstCount * CPI * CycleTime
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W

## Slide 34: Pipelined Processor
Observations?
H/W resources are under utilized
When an instruction is stage WB
IF, ID, E, and MEM stages are idle (do nothing)
IF
ID
EX
MM
WB

## Slide 35: Pipelined Processor
Solution
Fetch a new instruction each cycle
e.g: Executing instructions sequence: I0, I1, I2, I3, I4
IF
ID
EX
MM
WB
I0
I1
I2
I3
I4

## Slide 36: Pipelined Processor
How it work?
The PC should be incremented each cycle
Online instructions are kept in pipeline registers
IF
ID
EX
MM
WB
I0
I1
I2
I3
I4

## Slide 37: Pipelined Processor
Resource utilization

## Slide 38: Pipelined Processor
Multi-cycle vs Pipelined performance
Time
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
Time
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W

## Slide 39: Pipelined Processor
Multi-cycle vs Pipelined performance
The CPI is reduced
Ideal pipelined CPI is 1
  One instruction complete each cycle
CPU Time = InstCount * CPI * CycleTime

## Slide 40: 5-Stage Pipeline RISC-V Processor

## Slide 41: 5-Stage Pipeline RISC-V Processor
Pipelined control logic
Propagate the flags along the pipeline

## Slide 42: Basic RISC-V CPU Control Path
Data & Control Path