## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
FPGAs
Memory Mapped I/O
DMA

## Slide 4: Image Edge Detection Accelerator
Sobel filter acceleration on FPGA using HLS
Input image
Sober filter
Output image
Conv.
HLS
FPGA
Jupyter notebook

## Slide 5: Pynq FPGA Board
https://www.tul.com.tw/images/PYNQ-Z2_PA_v2_pp_20201209_STD.pdf
Zynq APSoC

## Slide 6: Zynq APSoC Architecture
SoC FPGA architecture
  PS: ARM Cortex A9 CPU
  PL: Xilinx Zynq FPGA
Connect with AMBA interconnect

## Slide 7: FPGA vs. ASIC
http://anysilicon.com/wp-content/uploads/2016/01/FPGA-vs-ASIC.jpg
NRE: Non-recurring engineering costs

## Slide 8: FPGA Architectures
How to implement programmable circuits?
High level view:
  Every combination logic is eventually a truth table
  Example: half adder
Input |  | Out
A | B | S
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Input |  | Out
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 9: Look-up-tables (LUTs)
Implement truth table (LUTs) in small memories and program the memory values
  Usually SRAM
A | B | S
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0
1
1
0
Addr
Output
0
0
0
1
Output
2-input, 1-output LUTs
00
01
10
11
01
10
11
A
B
Addr
A
B
S
C
Address: inputs

## Slide 10: LUTs
Combine two tables: when the outputs are used together
0
1
1
0
S
0
0
0
1
C
0
1
1
0
S
0
0
0
1
C
00
01
10
11
00
01
10
11
00
01
10
11
Addr
Addr
A
B
Addr
A
B

## Slide 11: How to build Sequential Logic?
Sequential logic:
  Needs to maintain states
Truth table won’t be enough to build sequential logic.
Possible solution
  Add a flip-flop to the output of LUT
3-in, 2-out
LUT
FF
FF
3-in, 1-out
LUT
FF

## Slide 12: How to build a register?
LUT simply passes inputs to appropriate output
3-in, 2-out
LUT
FF
FF
x(1)
x(0)
y(1)
y(0)
0 | 0
0 | 1
1 | 0
1 | 1
0 | 0
0 | 1
1 | 0
1 | 1
y(1)
y(0)
FF
FF
x(1)
x(0)
y(1)
y(0)
0 0 0
0 1 0
0 0 1
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
x(0)
x(1)
Inputs/Outputs
LUT functionality
Corresponding Truth Table

## Slide 13: Basic Units in the FPGA
Xilinx: Configurable Logic Blocks (CLBs)
Altera: Logic Elements (LE)  Logic Array Blocks (LAB)
First issue: How to make flip-flop optional?
  Simples way: Use a mx
3-in, 1-out
LUT
FF
2x1

## Slide 14: More than 1 LUTs
Internal connections between LUTs
3 input LUT
3 input LUT
2-1 MUX
FF
2x1
FF
2x1
Connecting more than 1 LUTs
Carry in

## Slide 15: Using Multiple LUTs
f1= (abc + def) (g + h + i) (jk +lm)
a b c d e f g h l j k l m
x
y
z
a b c j k l m
x
y
z
g h i
d e f
4 input LUT
5 input LUT
This can be implemented by
Four 5 input LUT

## Slide 16: Determining the LUT size
K-bit LUR: 2^k configuration memory bits
From: Principles and Structures of FPGAs ( © Springer Nature. 2018)
As the number of LUT input increases the number of LUT decreases.
  Better for performance
  Under utilizations
Area trade-off
4 to 6 inputs LUT are mostly common
LUT and FF

## Slide 17: Island-style FPGA Overview
Arranged as 2-D structure
Hard block: the usage is already fixed
  e.g. DSPs
Soft Logic: Programmable units :
  Xilinx-configurable logic block (CLB)
  Altera: logic array block
From: Principles and Structures of FPGAs ( © Springer Nature. 2018)
Check the Area in a chip for wires vs. logic

## Slide 18: Classification of FPGA routing structure
From: Principles and Structures of FPGAs ( © Springer Nature. 2018)

## Slide 19: Hierarchical-type FPGA
Altera Flex 10K, Apex, ApexII

## Slide 20: DSP Block
FPGA is slow on multiplications, floating point operations
Include custom DSP units instead of mapping onto LUTs
Example units:
  Multipliers
  MAC (Multiply-Accumulate)
  Barrel Shifter
  Square root
From: Principles and Structures of FPGAs ( © Springer Nature. 2018)

## Slide 21: Memory Using LUTs
LUTs  SRAM
Asynchronous access is possible
  Fast but small size (2^6 = ~ 64 bits)
  Use too much? Not much space left for LUTs
From: Principles and Structures of FPGAs ( © Springer Nature. 2018)

## Slide 22: Memory Blocks in FPGA
Dedicated Memory blocks in FPGA chip
  Block RAM (BRAM)
  Xilinix-7 series BRAM
  Each has 36K-bits
  Each BRAM can be either
    One 36-K bit memory
    Two independent 18-K bit memory
    One Two-ports 18-K bit memory
Can’t read the updated data at the same clock as writing
Synchronous write and read (different from distributed RAM)
Ideal for on-chip caches and scratchpads
From: Principles and Structures of FPGAs ( © Springer Nature. 2018)

## Slide 23
Fabric with Block RAM
  Block RAM can be placed anywhere
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
BR
BR
BR
BR
BR
BR
. . .
. . . .

## Slide 24: Programming FPGAs
How to program/configure FPGAs
  We have to initialize SRAM values in LUTS, MUX control signals, switch signals…
  Basic idea: Include FF’s in fabric to control programmable components
  Use skip mux to route programing bits to desire location
3-in, 1-out
LUT
FF
2x1
LE
Select?
FF
FPGA can be programmed to use/skip mux by storing appropriate bit

## Slide 25
FPGAs programmed with a ”bitfile”
Basic idea:
  Send a bit stream file and shift in bitfile one bit at a time
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
Shift register shifts bits to appropriate location in FPGA

## Slide 26
Memory Interconnect

## Slide 27: PS/PL Interfaces
How to communicate with PL and PS?
  Need to choose a right interface
Zynq uses 4 interfaces
  General Purpose Ports (GP)
    Memory-mapped transfer (e.g. CSRs)
  High-Performance Ports (HP)
    High-speed transfer (e.g. DDR memory)
  Accelerator Coherency Port (ACP)
    Coherency access to PS caches
  General Purpose I/O (GPIO)
    Best for control signals (start, idle, busy, etc…)
Notes: ACP Port = Accelerator Coherency port (Allocate mode)

## Slide 28: AXI Protocol
Master initiates the transactions
Slave handles the response
AXI
Slave
AXI
Master
Write transaction data
Read transaction data
© Mohammad Sadri
Write transaction
  Write address channel ()
  write data channel ()
  write response channel ()
Read Transaction
  Read address channel ()
  read response channel ()

## Slide 29: AXI Channels
Master and Slave handshaking with address channel
Every exchange of data is called a transaction (transaction includes the address/data and response)
4 burst mode (4 beats)
https://www.allaboutcircuits.com/technical-articles/introduction-to-the-advanced-extensible-interface-axi/

## Slide 30: AXI global signals
Any AXI component has two global signals:
  the clock ACLK
  an active-low asynchronous reset ARESETN.
AXI4 signals are sampled on the rising edge of the clock and all signal changes must occur after the rising edge.

## Slide 31: AXI4-Write Transaction
Separate addr & data channels
Master write request
  awfire = awvalid & awready
  wfire = wvalid & wready
  Can both ‘fire’ in same cycle
Slave write response
  bfire = bvalid & bready

## Slide 32: AXI4-Read Transaction
Master read request
  arfire = arvalid & arready
Slave read response
  rfire = rvalid & rready

## Slide 33: AXI4 Protocols
AXI4: A high performance memory mapped data and address interface. Capable of Burst access to memory mapped devices.
AXI4-Lite: A subset of AXI, lacking burst access capability. Has a simpler interface than the full AXI4 interface.
AXI4-Stream: A fast unidirectional protocol for transferring data from master to slave.
https://www.realdigital.org/doc/a9fee931f7a172423e1ba73f66ca4081

## Slide 34: AXI4 Stream Protocol
Simple transfer of data in a single transaction (no address!)
A transfer fires when
  tvalid & tready == 1
End of packet fires when
  tlast == 1
https://www.realdigital.org/doc/a9fee931f7a172423e1ba73f66ca4081
AXI Stream Slave
AXI Stream Master
3
2
1
0
tvalid
tready
tdata
tlast

## Slide 35: AXI Interfaces
AXI Interfaces
Memory
Mapped
Stream
Full AXI
(Burst Capable)
AXI-Lite
(Single-beat)
addr
Data
Resp
Data
Data
Data
<Burst>
with side channel
without side channel
(tkeep, tstrobe)
Data
Data
Data
Data
Data
tlast
Data
Tkeep or tstrobe are used to select valid bytes in tranfered block

## Slide 36: AXI Interconnect
How to connect multiple AXI components?
© Mohammad Sadri
AXI
Slave 1
(UART)
AXI
Master 1
(CPU)
AXI
Slave 2
(GPIO)
AXI
Slave 3
(RAM)
AXI
Master 2
(Master)
AXI Interconnect
Address Range: 4K
Address offset: 0x400000
Address: 0x400000 – 0x400FFF
Address Range: 4K
Address offset: 0x401000
Address: 0x401000 – 0x401FFF
Address Range: 4K
Address offset: 0x402000
Address: 0x402000 – 0x402FFF
Address table

## Slide 37: AXI interconnect
Master and Slave could have different clocks
Master and Slave could have different data #bits
  e.g. 64 bits CPU, 32 bits slave.
Hierarchical AXI interconnect is also possible
AXI slave address shouldn’t overlap
© Mohammad Sadri

## Slide 38: AXI Data Mover
Camera input
HDMI
Allocated Shared Memory
DRAM
CPU
?
?
We need to read/write stream of data from a peripherals (e.g. HDMI)
Peripherals use AXI Stream interface with no address
We need to store the data somewhere in memory for CPU to read using a memory mapped AXI interface
© Mohammad Sadri

## Slide 39: AXI Data Mover
Camera input
HDMI
Allocated Shared Memory
DRAM
CPU
Transfer Stream data to/from a memory mapped region
M_AXIS_MM2S
S_AXIS_S2MM
CPU configures the AXI data Mover Units
© Mohammad Sadri

## Slide 40: AXI Data Mover
Microarchitecture
  Command/status queues
  Command/status logic drive the mover engine

## Slide 41
DMA

## Slide 42: PIO Data transfer
Programmed input-output (PIO)
Peripheral devices: network adapter, GPU, of FPGA etc.
Memory-mapped IO (MMIO)
Processor
Memory
Peripheral
Peripheral
Address Range | 
0 – 0x100 | SSD
0x100-0x200 | Network interface
0x200-0x300 | GPU
Introduction to Direct Memory Access (DMA) by Vipin Kizheppatt
System Bus

## Slide 43: PIO Data Transfer
Only Processor can access memory
The transfer is software control
Peripherals go through the process to access memory
  Processor use local registers to store read data before transfer to peripheral
Only one operation at a time (read or write)
Only one device at a time
Even processor cannot perform any other work

## Slide 44: IO Programming
Sampling: always valid data, CPU can read whenever it wants
  Specific register
Polling: CPU must query device to see whether it is ready
Interrupts: Device notify CPU when ready
DMA: Device is able to control transfer of data to/from memory
IO controllers
  Device performs a series of IO operations w/ intervention, requires interrupt when it’s done
IO coprocessors
  Device is a separate, fully programmable computer

## Slide 45: DMA
Peripheral or Processor can be a master
Processor is not needed. Much faster
Multiple master can exist.
One read/write can be a large chunk
Introduction to Direct Memory Access (DMA) by Vipin Kizheppatt
45
Processor
Memory
Peripheral
Peripheral
System Bus

## Slide 46: Bus Arbitration
We can only have one master accessing memory at the time
Arbitration policy (round-robin, prior request etc.)
Introduction to Direct Memory Access (DMA) by Vipin Kizheppatt
46
Processor
Memory
Peripheral
Peripheral
Arbiter
Req
Grant
Req
Grant
System Bus
Req
Grant

## Slide 47: DMA controller
How does DMA controller know when to start?
DMA controller is set up by a software (start address, length, direction of communication)
  Processor push transfer command into DMA command queue
  Status register. (DMA transfer is done, status register set. Processor polls)
DMA is the master to all peripherals but a slave to a processor
Introduction to Direct Memory Access (DMA) by Vipin Kizheppatt
47
Processor
Memory
DMA controller
Peripheral
System Bus

## Slide 48: DMA controller – Option #2
Peripheral is directly connected to DMA controller
  System Bus can be used for other purpose
Introduction to Direct Memory Access (DMA) by Vipin Kizheppatt
48
Processor
Memory
DMA controller
Peripheral
System Bus

## Slide 49: PYNQ Board DMA Architecture
Supports high-performance burst transfer
The control interface uses R/W AXI-lite port
The data interface uses R/W AXI ports from HP or ACP
You PL module uses AXI Stream to access DMA

## Slide 50: DMA on Zynq
External DDR
How does PL access external Memory ?
Introduction to Direct Memory Access (DMA) by Vipin Kizheppatt
AXI GP Port
HP GP Port

## Slide 51: DMA on Zynq
External DDR
4 General Port AXI Port (master(2), slave(2))
4 High Performance Slave AXI Ports
DMA controller is instantiated in PL DMA is master
DDR controller is multi-port.
Multiple requests can be done
Introduction to Direct Memory Access (DMA) by Vipin Kizheppatt
DDR controller (scheduler/interface)

## Slide 52: DMA on Zynq
Peripheral
DRAM
Memory

## Slide 53
Power Management

## Slide 54
Q&A

## Slide 55: References
https://www.xilinx.com/html_docs/xilinx2020_1/vitis_doc/programmingvitishls.html#tlb1539734222626
Vitis High-Level Synthesis User Guide : https://www.xilinx.com/support/documentation/sw_manuals/xilinx2021_1/ug1399-vitis-hls.pdf
AXI DMA v 7.1 https://www.xilinx.com/support/documentation/ip_documentation/axi_dma/v7_1/pg021_axi_dma.pdf
https://www.xilinx.com/html_docs/xilinx2020_1/vitis_doc/programmingvitishls.html#tlb1539734222626

## Slide 56
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech