## Slide 1: Border Gateway Protocol
CSE 118: Computer Networks
George Varghese
Many slides courtesy Alex Snoeren
Computing routes from UCLA to the world as opposed to computing routes within UCLA

## Slide 2
REMINDER TO VOTE FROM AVALON KELLY OF UCLA AND CAL PIRG

## Slide 3: IP’s Abstract View of World
Network
2
Network z
Internet
Network y
Network 10
Network Numbers were 8, 16, or 24 bits

## Slide 4: Classless New World: Prefixes
18.32.3/24
11.12.1.1/30
Internet
192.2.3.4/28
123.32/16

## Slide 5: IP Addresses and Prefixes
32 bytes written as A.B.C.D, where A, B, C, D are integers from 1 to 255 representing one byte of IP address
.For example, an EE server in CMU can be 128.2.1.155, first byte is 10000000
A Prefix is represented by slash or wildcard notation, For example CMU is 128.2/16 which means that all IP addresses in CMU start with 10000000 0000 0010 *
Another way to encode prefixes is with a mask. For example, to represent a /16 use a bit mask with 16 1’s and 16 0’s. So you can AND with mask to find prefix

## Slide 6: Get Started by DHCP and ARP
CMU (128.2/16)
Philos, 128.2.15/24
128.2.15.*
128.2.10.*
EE, 128.2.1/24
A:, 128.2.1.155
B:, 128.2.15.16
DHCP
Server
DNS
Server

## Slide 7: So far: Route Computation within an Autonomous System (AS)
AS9
CMU (128.2/16)
Link State, or Distance Vector used within
AS between routes to compute routes
EE, 128.2.1/24
Hist, 128.2.10/24
Philos, 128.2.15/24
128.2.15.*
128.2.10.*

## Slide 8: BGP: Routing between ASes
AS701
UUnet
AS73
Univ of Wash
AS7018
AT&T
AS1239
Sprint
AS9
CMU (128.2/16)
128.2/16 9
128.2/16
9 701
128.2/16
9 7018 1239
Shorter AS Paths are
more preferred
128.2/16 9
128.2/16
9 7018

## Slide 9: UCLA (from ipinfo.io)
Many more including three more /16’s and many /24’s

## Slide 10: How Prefixes help us scale
AS701
UUnet
AS52
UCLA
AS9
CMU (128.2/16)
Shorter AS Paths are
more preferred
R1
*  R2
R2
R5
R4
R3
128.97. * R3
UCLA CS Web Server
128.97.1.1
128.97. * R4
128.97.1. * R5

## Slide 11: Why Interdomain Routing: Policy

## Slide 12: Possible Polices

## Slide 13: BGP Overview
Border Gateway Protocol (BGP)
  The canonical path vector protocol
  How routing gets done on the Internet today
AS relationships
  Customer/Provider
  Multihoming
  Peer-to-peer
Internet AS hierarchy

## Slide 14: Border Gateway Protocol
Interdomain routing protocol for the Internet
  Prefix-based path-vector protocol
  Policy-based routing based on AS Paths
  Evolved during the past 28 years
1989 : BGP-1 [RFC 1105], replacement for EGP
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771], support for CIDR
2006 : BGP-4 [RFC 4271], update

## Slide 15: Basic BGP Operation
AS1
AS2
Establish session
Exchange all
active routes
Exchange incremental
updates
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 16: Step-by-Step
A node learns multiple paths to destination
  Stores all of the routes in a routing table
  Applies policy to select a single active route
  … and may advertise the route to its neighbors
Incremental updates unlike distance vector
  Announcement
    Upon selecting a new active route, add own node id to path
    … and (optionally) advertise to each neighbor
  Withdrawal
    If the active route is no longer available
    … send a withdrawal message to the neighbors

## Slide 17: A Simple BGP Route
Destination prefix (e.g., 128.112.0.0/16)
Route attributes, including
  AS path (e.g., “7018 88”)
  Next-hop IP address (e.g., 12.127.0.121)
AS 88
Princeton
128.112.0.0/16
AS path = 88
Next Hop = 192.0.2.1
AS 7018
AT&T
AS 11
Harvard
192.0.2.1
128.112.0.0/16
AS path = 7018 88
Next Hop = 12.127.0.121
12.127.0.121

## Slide 18: Data Packets flow in opposite direction from BGP updates
Notice how Next Hop Info from last slide is crucial to build forwarding table at each route used to choose next hop
Have to do ARP as well to get MAC address of next hop
AS 88
Princeton
To D from S
Next Hop = 192.0.2.1
AS 7018
AT&T
AS 11
Harvard
192.0.2.1
To D from S
Next Hop = 12.127.0.121
12.127.0.121
Dest = D 128.112.3.1
Source = S

## Slide 19: Distance Vector versus BGP
Only way in distance vector to tune routes is via cost
In BGP, one can “control” routes in more complex ways
128.112.0.0/16
Cost = 40
Distance Vector, within an AS,
only attribute is cost, Always
Pick & propagate shortest
Path Vector, between ASes,
Multiple attributes, Complex
Choices settable in config files
10
20
128.112.0.0/16
Cost = 30
128.112.0.0/16
Cost = 30
128.112.0.0/16
AS Path = 7018 88
Community = 8
128.112.0.0/16
AS Path = 152 33 88
Community = 10
128.112.0.0/16
AS Path = 52 152 33 88
Community = 10

## Slide 20: (some) BGP Attributes
AS path: ASs the announcement traversed
Next-hop: where the route was heard from
Origin: Route came from Inside (IGP) or outside (EGP)
Local pref: Statically configured ranking of routes within AS
Multi Exit Discriminator: preference for where to exit network
Community: opaque data used for tag routes that are to be treated equivalently.

## Slide 21: BGP Decision Process
Default decision for route selection
  Highest local pref, shortest AS path, lowest MED, prefer eBGP over iBGP, lowest IGP cost, router id
Many policies built on default decision process, but…
  Possible to create arbitrary policies in principal
    Any criteria: BGP attributes, source address, prime number of bytes in message, …
    Can have separate policy for inbound routes, installed routes and outbound routes
  Limited only by power of vendor-specific routing language

## Slide 22: Example: Local Pref
AS 1
AS 2
AS 4
AS 3
13.13.0.0/16
local pref = 80
local pref = 100
local pref = 90
Higher Local
preference values
are more preferred
AS 5

## Slide 23: Example: Short AS Path
AS701
UUnet
AS73
Univ of Wash
AS7018
AT&T
AS1239
Sprint
AS9
CMU (128.2/16)
128.2/16 9
128.2/16
9 701
128.2/16
9 7018 1239
Shorter AS Paths are
more preferred
128.2/16 9
128.2/16
9 7018

## Slide 24: AS Paths vs. Router Paths
AS 4
AS 3
AS 2
AS 1
Mr. BGP says that
path 4 1 is better
than path 3 2 1

## Slide 25: More intricate feature: MEDs
Way to do load balancing by passing a hint to next AS
Request Harvard send traffic to Princeton sciences via R2
AS 88
Princeton
AS 7018
AT&T
AS 11
Harvard
128.112.12.0/24
AS path = 7018 88
192.0.2.1
128.112.12.0/24
sciences
128.112.12.0/24
AS path = 88
MED = 200
128.112.12.0/24
AS path = 88
MED = 100
128.112.18.0/24
arts
MED removed before
Passing to Harvard
12.127.0.121
R1
R2

## Slide 26: Doing MEDs in Cisco router config at Princeton exit
neighbor R1 route-map setMED-R1 out
neighbor R2 route-map setMED-R2 out
access-list 1 permit 128.112.12.0 255.255.255.0 // sciences
access-list 2 permit 128.112.18.0 255.255.255.0 // arts
route-map setMED-R1 … match ip address 1 set metric 100
// for R1 send science prefix with lower MED priority
route-map setMED-R1 … match ip address 2 set metric 200
// for R1 send arts prefix with higher MED prioriity
route-map setMED-R2 … match ip address 1 set metric 200
// for R2 send science prefix with higher MED priority
route-map setMED-R2 … match ip address 2 set metric 100
// for R2 send arts prefix with lower MED priority

## Slide 27: Feature 2: community
Way to tag multiple routes with same tag value
Then remote routers can act on tag (e.g., filter)
AS 7018
ATT
AS 52
UCLA
AS 701
UUNet
Filter if community = D
CMU and Princeton are not sent to
UUNET so UCLA does not provide transit
128.112.0.0/16
Princeton
128.2.0.0/16
CMU
128.112.0.0/16
AS path = 88 7018
128.112.0.0/16
ASPath =88 7018
Community = D

## Slide 28: Example: Aggregation

## Slide 29: BGP Has Lots of Problems
Instability
  Route flapping (network x.y/z goes down… tell everyone)
  Long AS-path decision criteria defaults to DV-like behavior (bouncing)
  Not guaranteed to converge, NP-hard to tell if it does
Scalability still a problem
  >500,000 network prefixes in default-free table today
  Tension: Want to manage traffic to very specific networks (eg. multihomed content providers) but also want to aggregate information.
Performance
  Non-optimal, doesn’t balance load across paths

## Slide 30: Business Relationships
Neighboring ASes have business contracts
  How much traffic to carry
  Which destinations to reach
  How much money to pay
Common business relationships
  Customer-provider
    E.g., Princeton is a customer of USLEC
    E.g., MIT is a customer of Level3
  Peer-peer
    E.g., UUNET is a peer of Sprint
    E.g., Harvard is a peer of Harvard Business School

## Slide 31: Multi-Homing
Customers may have more than one provider
  Extra reliability, survive single ISP failure
  Financial leverage through competition
  Better performance by selecting better path
  Gaming the 95th-percentile billing model
Provider 1
Provider 2

## Slide 32: Scaling iBGP
The default way of a full mesh between all border routers has O(N^2) overhead, where N is # border routers
Two common ways to scale IBGP in large ISPs: confederations and route reflectors
In confederations, we divide a large AS into stub AS’s hierarchically, so stub AS’s don’t know internals of each
In route reflectors, leaf border routers send BGP messages to a central reflector that sends to all clients. Can generalize to a tree of reflectors.

## Slide 33: Asking ChatGPT
When to Use Confederations
Very Large, Hierarchical Networks: Confederations are useful in large networks where the ISP has a very complex, hierarchical design,
Administrative Control and Scalability: Each sub-AS can have its own policies, making it easier to delegate control over different parts of the network.
When to Use Route Reflectors:
Simplified Design for Medium to Large Networks: Route reflectors simplify BGP by reducing the need for a full iBGP mesh without introducing the complexity of confederations. They’re a good choice for ISPs looking to scale a network that isn't complex enough to justify a confederation.

## Slide 34: Conclusions
Link State and Distance vector are used to route within a Domain/AS/ISP/Enterprise
BGP is used to compute routes between ASes
Basically like distance vector gossip except you add not just a total cost but list of all Ass in path so far.
AS Path helps policy because any router can choose to drop based on AS’s in path.
AS Path also helps prevent loops without a hop count