## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Agenda
About me
Logistic
Q/A
Course Introduction

## Slide 3: About me
Name: Blaise-Pascal Tine
Email: blaisetine@cs.ucla.edu
DM me on campuswire
Office Hours: Fridays 4:30-5:30 PM
Location: Eng VI 499
  in-person or remote

## Slide 4: About me
Research Interests
  Custom hardware extensions for GPU
    Graphics, ML, security, etc…
    ISA extensions
    Compiler optimizations
  Custom hardware extensions for FPGAs
  High-Level Synthesis for hardware design
  Hardware design automation
Looking a fun H/W research project? – email me

## Slide 5: About me
Country of origin: Cameroon
First language: French, Ngemba
My hobbies:
  Painting: oil, acrylic, digital
  Programming:
    Old school: Pascal, BASIC
    Web: HTML5, Javascript
    Managed: Java, C#
    Interpreted: Python
    Native: C/C++
    Hardware: Verilog, VHDL
Acrylic

## Slide 6: Teaching Assistant
TA: Turan Vural
Email: turan@g.ucla.edu
Office Hours: Wednesdays

## Slide 7: Tell us about you
School/Department
Background
Why are you taking this course?
Project partner
Form: https://forms.gle/rJjMRQAJ5e8pp1B1A

## Slide 8: Course Syllabus
Course website: https://blaisetine.github.io/m151b
Computer Model, Abstractions, and Technologies
Processor Design Metrics and Objectives
Instruction Set Architecture Design
Pipelining
Data and Controls Hazards
Branch Prediction
Super-Scalar Processors and Out-of-Order Execution
Cache and Memory Hierarchy
Power Management
Advanced Topics: GPUs, Accelerators, and Custom Architectures

## Slide 9: Reading Material
Book
David A. Patterson and John L. Hennessy, Computer Organization and Design: the Hardware/Software Interface: RISC-V Edition.
Additional Course Materials
Will be provided by the instructor.

## Slide 10: Campuswire
Self enrollment
Check out Bruinlearn’s syllabus section
Encourage participation with bonus points
TA and I will regularly check

## Slide 11: Waiting List
The class is full!
Overflow 95/80
You can audit the course!

## Slide 12: Homework
6 homework assignments
Individual work
Submitted by midnight on Thursday or Friday morning.
Due the following Thursday before class.
Multiple choice tests
5 pts each

## Slide 13: Projects
2 projects
  CPU pipeline implementation and optimization
  Required knowledge of C++
  3 weeks duration
Group project: teams of 2
  Can be done individually if you prefer to work solo
Encourage teamwork
  Most learn better from peers
  Most understand better by explaining to someone else
Separate submission
Must submit the same work you did with your partner
15 pts each

## Slide 14: Exams
Mid-term on 02/08/2024 – 15 pts
Final on 03/19/2024 – 20 pts
Use computer in class
Will offer a review session

## Slide 15: Participation
In class attendance
  Check attendance via QR code
  At least 70%
In class participation
  Will hand out a form before the final
Campuswire participation
5 pts (50% attendance, 50% participation)

## Slide 16: Grading
30% Homework
30% Projects
15% Midterm
20% Final
5% Participation
Distribution
  A: 90+
  B: 80+
  C: 70+

## Slide 17: Policies
Late Assignment: Not allow
  Except Dean of student approval
Bad submission: -5% of the grade
  Wrong file name
  Missing files
Regrade
  Must request within a week
  Written justification
  Be aware of full regrade!

## Slide 18: Q & A
7 minutes recess

## Slide 19: Class Assignment
In which ways Apple M1 chip better than Intel core i9 and AMD Ryzen processors?
How do you explain the Apple M1 chip success?
Why is everybody not using Apple M1?

## Slide 20: Class Assignment
In which ways is the Apple M1 chip better than Intel Core i9 and AMD Ryzen processors?
How would you explain the success of the Apple M1 chip?
Why isn't everyone using the Apple M1?

## Slide 21: Apple Chip Progression
From a mobile (phone) to desktop (MAC)
Single-thread performance Increase (2015-2021)
  Intel ~28%
  Apple ~198% or 2.98x
Intel still has an edge on single thread
https://www.anandtech.com/show/16226/apple-silicon-m1-a14-deep-dive/4
Notes: * Intel Core i7-1185G7 (4-cores) was relatively weaker than Intel Core i7-11850H (8-cores)

## Slide 22: Apple M1 Efficiency
70% less power for same performance compared to competition!
Performance per watt (flops per watt)
How did they get here?
https://www.apple.com
Notes: https://www.apple.com/newsroom/2021/10/introducing-m1-pro-and-m1-max-the-most-powerful-chips-apple-has-ever-built

## Slide 23: Apple M1 PRO Chip layout
Hybrid architecture
  Efficient cores
  Performance cores
Neural Processing Units
Internal DDR memory
Shared GPU-CPU memory
SLC (system-level cache)
Notes: https://www.apple.com/newsroom/2021/10/introducing-m1-pro-and-m1-max-the-most-powerful-chips-apple-has-ever-built/

## Slide 24: Apple silicon characteristics
Instruction set architecture (ISA)
  ARM ISA
  RISC architecture advantages
    Smaller instructions set
    Simpler pipeline
      efficient decode. Execute
    Energy efficient processor
    Easier compiler optimizations
  RISC challenges
    More instructions per work
      e.g. memory operations
      CISC single-thread advantage
Notes: RISC => relaxed instruction set computer
X86 ALU memory operands

## Slide 25: Apple silicon characteristics
Process Technology
  5 nanometer for M1 chip from TSMC
  Intel was still on 3rd generation 10 nm
  Why it matter?
    Higher transistor density
    More cores per area => more flops per area
    Higher clock speed due to shorter delay
Notes: TSMC (Taiwan semiconductor manufacturing company)
NM is the size of the smallest feature that can be reliably manufactured in a chip's fabrication process.
In the early days of semiconductor manufacturing, the "nm" measure was more closely aligned with the length of the silicon channel between the source and drain of the transistor.

## Slide 26: Apple silicon characteristics
Integrated components
  Reduce communication overhead
    Increase energy efficiency
  Increase communication bandwidth
    Bypass pins shortage
  Integrated GPU
  Integrated SSD controller
Notes: TSMC (Taiwan semiconductor manufacturing company)
Higher clock speed => smaller transistor device, short delay

## Slide 27: Apple silicon characteristics
Near Memory Computing
  Integrated Memory
  Reduce memory latency
  Reduce communication overhead
    Increase energy efficiency
  Increase communication bandwidth
    Bypass pins shortage
Notes: TSMC (Taiwan semiconductor manufacturing company)
Higher clock speed => smaller transistor device, short delay

## Slide 28: Apple silicon characteristics
Hardware specialization
  Move common expensive tasks into silicon
  Increase energy efficiency
  Neural processing units (NPUs) (AI)
  Media encode/decode engines (video, images)
Notes: TSMC (Taiwan semiconductor manufacturing company)
Higher clock speed => smaller transistor device, short delay

## Slide 29: Apple silicon characteristics
Heterogenous computing
  Little cores and big cores
  high-performance "Firestorm" cores
  high-efficiency "Icestorm" cores
  optimize for performance or power efficiency as needed
Notes: TSMC (Taiwan semiconductor manufacturing company)
Higher clock speed => smaller transistor device, short delay

## Slide 30: Apple silicon characteristics
Microarchitecture optimizations
  Unified memory
  CPU and GPU share the same memory pool
  Eliminates unnecessary copies
  Larger pool increases capacity / utilization
Notes: TSMC (Taiwan semiconductor manufacturing company)
Higher clock speed => smaller transistor device, short delay

## Slide 31: Apple silicon characteristics
Hardware-software codesign
  Apple own both the hardware and system stack
  allows for tight integration
  Controlled ecosystem of critical applications
    Profiling and optimizations
Notes: TSMC (Taiwan semiconductor manufacturing company)
Higher clock speed => smaller transistor device, short delay

## Slide 32: The Classic CPU Performance Equation
CPU time = Instruction Count x CPI x Clock Cycle Time
  CPI = Clock Cycle per Instruction
CPU time =
How do you increase performance?
  Reducing the CPU time
SPECint benchmarks – Patterson & Hennessy book
Notes: VAX-11/780, was announced in October 1977 at 5 Mhz, 32-bit

## Slide 33: Reducing CPU Time
CPU time =
Reduce Instruction Count
  Software, compiler, ISA
Reduce CPI
  Microarchitecture
Increase Clock Rate
  Process technology
  Hardware design

## Slide 34: Moore’s law
Gordon Moore predicted in 1965’s the doubling of transistors count every two years.
His prediction was fairly accurate in the decades that followed up to the 2010’s

## Slide 35: Dennard’s (MOSFET) Scaling
Dynamic Power = alpha * CFV2
  Alpha = transistor switching rate (represents how active the transistor is)
  C = capacitance
  F = frequency
  V = voltage
Dennard’s scaling (1974)
  As transistors get smaller the capacitance and voltage decreases
  So, you can increase frequency while keeping the power constant
  Higher frequency means higher performance
Notes: Alpha is also called activity factor of the transistor
Capacitance = capacity for storing electric charge

## Slide 36: Breakdown of Dennard’s Scaling (2006)
As transistors got too small
  Leakage current between transistor gate
  Threshold voltage couldn’t be reduced further
    Higher power density (watt/mm2)
  Heat dissipation from densely packed transistors
  Instability of transistors when approaching atomic scale
Notes: Robert Dennard
Capacitance = capacity for storing electric charge
Voltage = electric charge of a circuit
Power density = power per unit area (Watt/mm2)

## Slide 37: Memory Wall
DRAW technology scaling
  Is slower than processor’s
  slower clock than CPU’s
Memory Latency
  Getting data from memory
  Takes more CPU cycles
Multi-core area
  Increases memory requests
  Increases demand on memory bandwidth

## Slide 38: The big picture
-1984
  Process technology
1984-2004
  Process technology
  Microarchitecture optimizations
2004+
  Power wall
  Memory wall
  ILP wall
SPECint benchmarks – Patterson & Hennessy book
Notes: VAX-11/780, was announced in October 1977 at 5 Mhz, 32-bit

## Slide 39: The end of Moore’s Law
Multicore Area
Increase the number of cores
Kunle Olukotun, Lance Hammond, Herb Sutter, Mark Horowitz and extended by John Shalf.
Notes: VAX-11/780, was announced in October 1977 at 5 Mhz, 32-bit

## Slide 40: Multicore area challenges
Limitations application parallelism
Inter-core communication
Memory wall
Heat dissipation
Power management
Physical limits
Kunle Olukotun, Lance Hammond, Herb Sutter, Mark Horowitz and extended by John Shalf.

## Slide 41: Great area for computer architects
How do we continue to scale performance?
It will require a holistic approach
At all layers of the computing stack
  Technology nodes
  Microarchitecture
  Compilers
  Systems and Applications
The progress won’t stop ;-)

## Slide 42: What we will learn in this class
The fundamentals of computer architecture
Understand the design decisions when building a processor
How to simulate and evaluate a processor