## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
Control Hazards
Project #1

## Slide 4
Control Hazards: Speculation
Practical Branch stats
  About 20% of instructions is control-flow
    50% of forward branches (if-then-else) are taken
    90% of backward branches (loops) are taken
    30% of all branches are not-taken

## Slide 5
Control Hazards: Speculation
Practical Branch stats
  About 20% of instructions is control-flow
    50% of forward branches (if-then-else) are taken
    90% of backward branches (loops) are taken
    30% of all branches are not-taken

## Slide 6
Control Hazards: Speculation
Practical Branch stats
  About 20% of instructions is control-flow
    50% of forward branches (if-then-else) are taken
    90% of backward branches (loops) are taken
    30% of all branches are not-taken
Not-taken prediction accuracy?
  Only 30%
  Cost: 3 cycles

## Slide 7
Control Hazards: Speculation
Predict: Always Taken
What do we need?
  Target: NextPC
  Needed in IF stage

## Slide 8
Control Hazards: Speculation
Predict: Always Taken
  How to obtain the branch target?
  We can predict

## Slide 9
Control Hazards: Speculation
When do we know the branch target?
  Hard to computeConditional Branches: BEQ/BNE
    PC = (R[rs1] ops R[rs2]) ? (PC + imm) : PC + 4
    In ID stage
    Prediction accuracy: High

## Slide 10
Control Hazards: Speculation
When do we know the branch target?
  Direct Jumps, Function calls: JAL
    PC = PC + imm
    In ID stage
    Prediction accuracy: High

## Slide 11
Control Hazards: Speculation
When do we know the branch target?
  Indirect Jumps, Dynamic Calls, Returns: JALR
    PC = R[rs1] + imm
    After ID stage
    Preduction accuracy: Low

## Slide 12
Control Hazards: Speculation
How do we predict the address?
  We need to track the history of previous branch targets
  If a branch was visited before reuse its previous target
  There is a chance it will execute the same path

## Slide 13
Control Hazards: Speculation
Branch Target Buffer (BTB)
  A table that stores branch targets
  Indexable using the current PC
    Why using the PC?

## Slide 14
Control Hazards: Speculation
How BTB works?
  Use PC to lookup the BTB
  Found a match?
    NextPC = BTB entry;
  Otherwise
    NexPC = PC + 4;

## Slide 15
Control Hazards: Speculation
BTB implementation questions:
  Where is BTB accessed?
  How do we know that the current PC is a branch before accessing the BTB?
  When do we update the BTB?
  How do we update the BTB?

## Slide 16
Control Hazards: Speculation
Where is BTB accessed?
  NextPC is needed in IF stage
  BTB should be accessed in IF stage

## Slide 17
Control Hazards: Speculation
How do we know that the current PC is a branch before accessing the BTB?
    Only branches are added into BTB
    Make sure to clear BTB at startup

## Slide 18
Control Hazards: Speculation
When do we update the BTB?
  When we can compute branch target
  In ID stage:
    Add dedicated adder
    JALR timing issue – register file access
  In EX stage:
    Add dedicated adder
    No timing issue
  Should be done in only one place
    Why?

## Slide 19
Control Hazards: Speculation
How do we update the BTB?
  Check if branch
  Calculate NextPC
  Update BTB
    BTB[PC] = NextPC

## Slide 20
Control Hazards: Speculation
BTB Hardware Implementation
  Implementing a hash table in H/W is expensive
    Lookup area cost
    Lookup latency
    Table size must be small

## Slide 21
Control Hazards: Speculation
BTB Hardware Implementation
  Use a Tagged-based Lookup table
  Fixed size: btb_size
  Indexing: btb_index
  Lookup: btb_tag

## Slide 22
Control Hazards: Speculation
BTB Hardware Implementation
  PC address is 4-byte aligned
    lower 2 bits are zero
  Formulas:
    index_bits = log2(btb_size)
    pc_index = (pc >> 2) & index_bits
    pc_tag = (pc >> 2) >> index_bits

## Slide 23
Control Hazards: Speculation
BTB Hardware Implementation
  Initialization:
    Clear valid bit at reset
  BTB lookup:
    btb <= BTB[pc_index];
    if (btb.valid == 1 && btb.tag == pc_tag) { PC = btb.target; } else { PC = PC + 4; }
  BTB update:
    BTB[pc_index] <= {1, pc_tag, target};
valid | tag | target
16 entries
1 bit
26 bits
30 bits
BTB hardware table

## Slide 24
Control Hazards: Speculation
Improving Branch prediction
  Predicting always taken is about 70% accurate
  which is better than always not taken (30%).
  How do we improve the prediction accuracy?

## Slide 25
Control Hazards: Speculation
Code reordering optimization
  If H/W implements static prediction
    Not Taken or always Taken
  Reorder code to prioritize predicted path
  Pros/cons?
    Pros: improved accuracy
    Cons: architecture specific

## Slide 26
Control Hazards: Speculation
BTFNT (Backward Taken, Forward Not Taken)
  Loops usually have a few iterations, so this is like always predicting that the loop is taken
  Loop back-edge => backward direction
  Pros/Cons?
    Pros: Improved accuracy
    Cons: limited to loops only

## Slide 27
Control Hazards: Speculation
Using a Branch predictor
  Predict the outcome dynamically using the branch history
  Recurring branches tend to repeat their pattern (e.g. loops)

## Slide 28
Control Hazards: Speculation
One-Bit Branch Predictor
  BTB entry hold a single bit: taken=1 or not_taken=0.
  Index the table using lower K bits of PC
  Update the table when the condition is resolved.
K bits of branch instruction PC
index
BHT: 2^K 1-bit entries
Use this entry to predict this branch:
0: predict not taken
1: predict taken

## Slide 29
Control Hazards: Speculation
One-Bit Branch Predictor
  FSM

## Slide 30
Control Hazards: Speculation
One-Bit Branch Predictor
  Examples
DC08: TTTTTTTTTTT ... TTTTTTTTTTNTTTTTTTTT…
100,000 iterations
DC44: TTTTT ... TNTTTTT … TNTTTTT …
2 / 100
DC50: TNTNTNTNTNTNTNTNTNTNTNTNTNTNT …
2 / 2
How often is branch outcome != previous outcome?
2 / 100,000
99.9%
98.0%
00.0%

## Slide 31
Control Hazards: Speculation
One-Bit Is not enough!
  Example: short loop (8 iterations)
    Taken 7 times, then not taken once
    Act: TTTTTTTNTTTTTTNTTTTTTTNT…
    Pred: XTTTTTTTNTTTTTTNTTTTTTTN
    Corr: XooooooMMooooooMMooooooMM
    Misprediction rate: 2/8 = 25%
  Execute the same loop again
    First always mispredicted (previous outcome was not taken)
    Then 6 predicted correctly
    Then last one mispredicted again
  Each fluke/anomaly results in two mispredicts per loop

## Slide 32
Control Hazards: Speculation
Two-Bit Branch Predictor
0
1
FSM for Last-time
Prediction
0
1
2
3
FSM for 2bC
(2-bit Counter)
Predict NT
Predict T
Transistion on T outcome
Transistion on NT outcome
Smith, ISCA 1981

## Slide 33
Control Hazards: Speculation
Two-Bit Branch Predictor

## Slide 34
Control Hazards: Speculation
Can we do better?
  1-BC and 2-BC predictors use last branch outcome to predict
  Observation1: global branch correlation
      The branch outcome is correlated with outcome from previous branches
  Observation2: local branch correlation
      The branch outcome is correlated with prior-outcome from same branch

## Slide 35
Control Hazards: Speculation
Global branch correlation
Local branch correlation
if (cond1) { --//-- } if (cond1 and cond2) { --//--
}
for (x: 0 -> 1023) {
--//--
}

## Slide 36
Control Hazards: Speculation
Two-level Branch Predictor
Level1: history of last N branches
Level2: last direction the branch took
1
1 1 ….. 1 0
Branch History Register (BHR)
00 …. 00
00 …. 10
11 …. 11
0
1
2
3
index
2-Bit BHT
previous one
Yeh&patt’92

## Slide 37
Control Hazards: Speculation
Two-level Branch Predictor
Example:
BHR 00000
Br1 : taken  BHR 00001
Br2: not-taken  BHR 00010
Br3: taken  BHR 00101
New BHR = old BHR<<1 | (br_dir);
0 0 0 0 0 0
History length
Initialization value (0 or 1)
1 : branch is taken
0: branch is not-taken
Past
Present

## Slide 38
Control Hazards: Speculation
Two-level Branch Predictor
Branch X: if (cond1)
Branch Y: if (cond 2)
Branch Z : if (cond 1 and cond 2)
…….1 0
BHR
…….1 1
…….01
…….00
BHT
Branch X | Branch Y | Branch Z
1 | 0 | 0
1 | 1 | 1
0 | 1 | 0
0 | 0 | 0

## Slide 39
Control Hazards: Speculation
Gshare Branch Predictor
Different branches may see the same history but have different outcome
Need additional context
1 1 ….. 1 0
2bc
2bc
2bc
2bc
BHR
index
0x809000
PC
XOR
McFarling’93
Predictor size: 2^(history length)*2bit

## Slide 40
Control Hazards: Speculation
Gshare Branch Predictor: algorithm
predict_func(pc, actual_dir) { index = PC xor BHR taken = (2bit_counters[index] >= 2) ? 1 : 0 correctly_predictied = (actual_dir == taken) ? 1 : 0 // stats }
update_func(pc, actual_dir) { index = PC xor BHR if (actual_dir) INC_SAT(2bit_counter[index]) else DEC_SAT(2bit_counter[index]) BHR = BHR << 1 | actual_dir }

## Slide 41
Control Hazards: Speculation
Improving Return Call Prediction
RISC-V JALR
  PC = R[rs1] + imm
Target dependents on rs1

## Slide 42
Control Hazards: Speculation
Return Stack Buffer (RSB)
Use hardware stack
  About 4-8 entries
On function call:
  Push current return address
On function return:
  Pop last return address
  Use that for prediction

## Slide 43
Control Hazards: Speculation
Return Stack Buffer (RSB)
Tail recursion optimization
  if (stack.top == ra) => skip
Integration with BTB:
  Predict NextPC from BTB or RSB
  How to choose?
    Extend BTB with “isRA” column

## Slide 44
Project #1

## Slide 45
Project #1
Deadline: Next week
What to do:
  decode & execute
  data forwarding – handle stall cases
  3 cycles stall on branches
Help:
  README has a lot of info
  TA|me office hours

## Slide 46
Q&A

## Slide 47
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech