## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
Super Scalar Processors

## Slide 4
CPU Performance
Latency
  Time it takes to complete a task
Throughput
  Number of tasks completed per given time

## Slide 5
CPU Performance
Example of throughput
  Computation capacity: FLOPS (floating-point operations per sec)
  Memory bandwidth: GB/s (memory bytes transfer per sec)

## Slide 6
CPU Performance
How do we improve CPU performance?
CPU Time = IC * CPI * CT
IC: instruction count
CPI: cycles per instructions
CT: clock cycle time

## Slide 7
CPU Performance
Review: How do we improve CPU performance?
CPU Time = IC * CPI * CT
IC: instruction count
CPI: cycles per instructions
CT: clock cycle time

## Slide 8
CPU Performance
Multi-cycle architecture affect?
  smaller CT
  Why?
  Any downside?
  CPI increases
CPU Time = IC * CPI * CT
IC: instruction count
CPI: cycles per instructions
CT: clock cycle time

## Slide 9
CPU Performance
Pipeline architecture improve?
  Smaller CT
  Smaller CPI
CPU Time = IC * CPI * CT
IC: instruction count
CPI: cycles per instructions
CT: clock cycle time

## Slide 10
CPU Performance
More pipeline stages improve?
  Smaller CT
  Same CPI
CPU Time = IC * CPI * CT
IC: instruction count
CPI: cycles per instructions
CT: clock cycle time

## Slide 11
CPU Performance
Downside of more pipeline stages?
  CT reduction is limited
  CPI will increase: more pipeline hazards
  Hardware cost: more forwarding paths
CPU Time = IC * CPI * CT
IC: instruction count
CPI: cycles per instructions
CT: clock cycle time

## Slide 12
CPU Performance
How do we reduce CPI?
  Increase the instruction throughput

## Slide 13
CPU Performance
IPC: Instructions per cycle
  Instruction throughput
  IPC = 1 / CPI
  How many instructions to executed per cycle
  Higher is better
CPU Time = (IC * CT) / IPC
IC: instruction count
IPC: instructions per cycle
CT: clock cycle time

## Slide 14
CPU Performance
CPU Paralleling Types
  ILP: instruction-level parallelism
  TLP: thread-level parallelism
  MLP: memory-level parallelism

## Slide 15
SuperScalar Processor
Exercice: How do we extend scalar pipeline for IPC=2?
IF Stage:
  PC
    No replication
  Instruction Memory
    Multiple read ports
Nader ECE-M116C

## Slide 16
SuperScalar Processor
Exercice: How do we extend scalar pipeline for IPC=2?
ID Stage:
  Decode
    Replication
  Register file
    Multiple read ports
Nader ECE-M116C

## Slide 17
SuperScalar Processor
Exercice: How do we extend scalar pipeline for IPC=2?
EX Stage:
  ALU
    Replication
    Partitioning
Nader ECE-M116C

## Slide 18
SuperScalar Processor
Exercice: How do we extend scalar pipeline for IPC=2?
MEM Stage:
  Data Memory
    No replication
Nader ECE-M116C

## Slide 19
SuperScalar Processor
Exercice: How do we extend scalar pipeline for IPC=2?
WB Stage:
  Register File
    Multiple write ports
Nader ECE-M116C

## Slide 20
SuperScalar Processor
Exercice: How do we extend scalar pipeline for IPC=2?
Nader ECE-M116C

## Slide 21
SuperScalar Processor
Exercice: How do we extend scalar pipeline for IPC=2?
Nader ECE-M116C

## Slide 22
SuperScalar Processor
Hardware complexity
  Data forwarding cost
  Replicate the path

## Slide 23
SuperScalar Processor
Data dependency issue? (N=2)
  ADD r1 <- r1, r3
  ADD r6 <- r4, r3
  No

## Slide 24
SuperScalar Processor
Data dependency issue? (N=2)
  ADD r3 <- r1, r2
  ADD r3 <- r4, r1
  Yes: WAW: write ordering should be enforced
  Delay the bottom write

## Slide 25
SuperScalar Processor
Data dependency issue? (N=2)
  ADD r3 <- r1, r2
  ADD r6 <- r4, r3
  Yes: RAW: r3 read before being written
  Need expensive checks

## Slide 26
SuperScalar Processor
How many RAW checks? (N=4)
  ADD rd1 <- rs1a, rs1b
  ADD rd2 <- rs2a, rs2b
  ADD rd3 <- rs3a, rs3b
  ADD rd4 <- rs4a, rs4b
  12 checks: 6 + 4 + 2

## Slide 27
SuperScalar Processor
Tradeoffs
  Pros:
    Higher IPC
  Cons:
    Hardware cost
      Replication
      Dependency checks
    Pipeline stalls limit IPC

## Slide 28
SuperScalar Processor
SuperScalar best-case performance
  When instructions have no dependencies
  Doesn’t happen often enough
  Need to allow other non-dependent instructions to execute

## Slide 29
SuperScalar Processor
Scalar: can process at most one instruction per cycle
SuperScalar: can process at most N instructions per cycle

## Slide 30
Out of Order Execution
If the next instruction cannot move forwards due to dependencies, we skip it and pick the next one.
The instruction window size determines pipeline utilization
Notes: Instr window = range of instructions to search

## Slide 31
Out of Order Execution
OoO Design Challenges?
  Finding an available instruction
  How do we track dependencies when ordering is broken?
  How do we handle pipeline hazards?
  How do we preserve ordering for external states?
    Register and memory
Notes: Instr window = range of instructions to search

## Slide 32
Static Scheduling
Compiler re-order the instruction
  Internally track dependencies
  Check register use
How do we do that in the compiler?
add r1,r2,r3
sub r4,r1,r3
and r6,r2,r7
All sources are ready?
Why not execute them?
add r1,r2,r3
and r6,r2,r7
sub r4,r1,r3
Notes: Instr window = range of instructions to search

## Slide 33
Dynamic Scheduling
How to reduce register dependencies?
Notes: Instr window = range of instructions to search

## Slide 34
Dynamic Scheduling
Can we increase the number of registers to work with?
  You cannot change the ISA (our S/W contract)
Notes: Instr window = range of instructions to search

## Slide 35
Dynamic Scheduling
Solution:
  Use internal registers: “physical” registers
  We will call ISA registers “logical” or “architected”
  initially map logical registers to physical registers
Notes: Instr window = range of instructions to search

## Slide 36
HW Register Renaming
Needed Features:
  mapping mechanism
  physical registers
    allocation/deallocation mechanism
    allocated vs. free registers
Notes: Instr window = range of instructions to search

## Slide 37
HW Register Renaming
Exercise:
  Identify all data dependencies
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
I4: OR R8, R5, R2
I5: XOR R2, R4, R11
Program code
RAW
WAR
WAW
Notes: Instr window = range of instructions to search

## Slide 38
HW Register Renaming
Exercise
  3 RAWs
  1 WAR
  1 WAW
  Which instructions cannot be reordered?
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
I4: OR R8, R5, R2
I5: XOR R2, R4, R11
Program code
RAW
WAR
WAW
Notes: Instr window = range of instructions to search

## Slide 39
HW Register Renaming
Exercise
  I3 can not exec before I2 because I3 will overwrite R5
  I5 can not go before I2 because I2, when it goes, will overwrite R2 with a stale value
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
I4: OR R8, R5, R2
I5: XOR R2, R4, R11
Program code
RAW
WAR
WAW
Notes: Instr window = range of instructions to search

## Slide 40
HW Register Renaming
Exercise
  I3 can not exec before I2 because I3 will overwrite R5
  I5 can not go before I2 because I2, when it goes, will overwrite R2 with a stale value
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
I4: OR R8, R5, R2
I5: XOR R2, R4, R11
Program code
RAW
WAR
WAW
Notes: Instr window = range of instructions to search

## Slide 41
HW Register Renaming
Example
  Let’s rename R5 to decouple I2 and I3
  R5 = S
  Removed WAR
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
I4: OR R8, R5, R2
I5: XOR R2, R4, R11
Program code
RAW
WAR
WAW
I3: AND S, R11, R7
Notes: Instr window = range of instructions to search

## Slide 42
I4: OR R8, S, R2
HW Register Renaming
Example
  I4 also needs to change since R5 is S
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
I5: XOR R2, R4, R11
Program code
RAW
WAR
WAW
I3: AND S, R11, R7
Notes: Instr window = range of instructions to search

## Slide 43
HW Register Renaming
Example
  Let’s rename R2 to decouple I2 and I5
  R2 = T
  Removed WAW
Program code
I5: XOR T, R4, R11
I4: OR R8, S, R2
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
RAW
WAR
WAW
I3: AND S, R11, R7
Notes: Instr window = range of instructions to search

## Slide 44
HW Register Renaming
Register renaming eliminates
WAR dependencies
WAW dependencies
Program code
I5: XOR T, R4, R11
I4: OR R8, S, R2
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
RAW
WAR
WAW
I3: AND S, R11, R7
Notes: Instr window = range of instructions to search

## Slide 45
HW Register Renaming
Implementation
  Space for S, T, etc.
  How do we know when to rename a register?
Program code
I5: XOR T, R4, R11
I4: OR R8, S, R2
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
RAW
WAR
WAW
I3: AND S, R11, R7
Notes: Instr window = range of instructions to search

## Slide 46
HW Register Renaming
Simple Solution
  Do renaming for every instruction
  Change the name of a register each time we decode an instruction that will write to it.
  Remember what name we gave it 
Program code
I5: XOR T, R4, R11
I4: OR R8, S, R2
I1: ADD R1, R2, R3
I2: SUB R2, R1, R5
I3: AND R5, R11, R7
RAW
WAR
WAW
I3: AND S, R11, R7
Notes: Instr window = range of instructions to search

## Slide 47
Register File Organization
We need some physical structure to store the register values
PRF
ARF
RAT
Register
Alias
Table
Physical
Register
File
Architected
Register
File
One PREG per instruction in-flight
“Outside” world sees the ARF
Notes: Instr window = range of instructions to search

## Slide 48
Putting it all together
top:
  R1 = R2 + R3
  R2 = R4 – R1
  R1 = R3 * R6
  R2 = R1 + R2
  R3 = R1 >> 1
  BNEZ R3, top
R1
R2
R3
R4
R5
R6
X1
X2
X3
X4
X5
X6
X7
X8
X9
X10
X11
X12
X13
X14
X15
X16
R1
R2
R3
R4
R5
R6
RAT
R1
R2
R3
R4
R5
R6
List all instructions for 2 loop iterations
Show graph when only RAW enforced
Show graph when all deps enforced
Rename the registers
Free pool:
X9, X11, X7, X2, X13, X4, X8, X12, X3, X5…
Notes: Instr window = range of instructions to search

## Slide 49
Putting it all together
R1 = R2 + R3
R2 = R4 – R1
R1 = R3 * R6
R2 = R1 + R2
R3 = R1 >> 1
BNEZ R3, top
R1 = R2 + R3
R2 = R4 – R1
R1 = R3 * R6
R2 = R1 + R2
R3 = R1 >> 1
BNEZ R3, top
List all instructions for 2 loop iterations
Notes: Instr window = range of instructions to search

## Slide 50
Putting it all together
2. Show graph when only RAW enforced
RAW
WAR
WAW
Notes: Instr window = range of instructions to search

## Slide 51
Putting it all together
3. Show graph when all deps enforced
RAW
WAR
WAW
Notes: Instr window = range of instructions to search

## Slide 52
Putting it all together
4. Rename the registers
RAW
WAR
WAW
R1
R2
R3
R4
R5
R6
X1
X2
X3
X4
X5
X6
X7
X8
X9
X10
X11
X12
X13
X14
X15
X16
Free pool:
X9, X11, X7, X2, X13, X4, X8, X12, X3, X5…
R1
R2
R3
R4
R5
R6
R1
R2
R3
R4
R5
R6
X9
X11
X7
X2
X13
X14
X8
X12
X3
X5
Notes: Instr window = range of instructions to search

## Slide 53
HW Register Renaming
We keep using new physical registers
  What happens when we run out?
  We stall the pipeline until they are freed
Notes: Instr window = range of instructions to search

## Slide 54
HW Register Renaming
When do we recycle physical registers?
  When not needed any more, i.e we have given its value to all instructions that use it as a source operand!
  Need to tracking mechanism
Notes: Instr window = range of instructions to search

## Slide 55
HW Register Renaming
Architected register file contains
the “official” processor state
When an instruction leaves the
pipeline, it makes its result
“official” by updating the ARF
The ARF now contains the
correct value; update the RAT
T42 is no longer needed, return
to the physical register free pool
ARF
R3
RAT
R3
PRF
T42
Free Pool
Notes: Instr window = range of instructions to search

## Slide 56
HW Register Renaming
ARF
R3
RAT
R3
PRF
Free Pool
T42
T17
Update ARF as usual
Deallocate physical register
Don’t touch the RAT!
(Someone else is the most
recent writer to R3)
At some point in the future,
the newer writer of R3 exits
Deallocate physical register
This instruction was the most
recent writer, now update the RAT
R3 could be using a different PRF at commit
Notes: Instr window = range of instructions to search

## Slide 57
Q&A

## Slide 58
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech