## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
Out of order Processors

## Slide 4
Processor Types (Recap)
Scalar CPU: process at most one instruction per cycle
  Shortcomings: IPC<=1
SuperScalar CPU : process at most N instructions per cycle
  Shortcomings: IPC rarely reach N
  Why? Data dependencies
Out of Order CPU: process instructions out of order
  Goal: Resolve data dependencies

## Slide 5
Modern Processor Requirements
Fetching multiple instructions each cycle
Executing multiple instructions concurrently
Partitioned execute stage
  Multiple functional units (e.g. ALU, FPU, LSU)
  Variable-latency units
Commit instructions in order
  Preserving external states

## Slide 6
Issue (ID)
Modern Processor Pipeline
Three main stages: Issue, Execute, Commit
Fetch
Decode
Execute (EX, MEM, WB)
Commit
ALU
LSU
Register File
Data Memory
In-order
Out-of-order
In-order

## Slide 7
Out of Order Execution
OoO Design Challenges?
  How do we resolve data dependencies?
  How do we handle pipeline hazards?
  How do we preserve ordering for external states?
Notes: Instr window = range of instructions to search

## Slide 8
Issue (ID)
Register Renaming
Resolving Data dependencies
Fetch
Decode
Execute (EX, MEM, WB)
Retire
ALU
LSU
Register File
Data Memory
In-order
Out-of-order
In-order
Register
Renaming

## Slide 9
Register Renaming Structures
ARF, PRF, and RAT
PRF
ARF
RAT
Register
Alias
Table
Physical
Register
File
Architected
Register
File
One PREG per instruction in-flight
“Outside” world sees the ARF
Notes: Instr window = range of instructions to search

## Slide 10
Register Renaming Summary
Advantages?
  Eliminate WAR data dependencies (anti-dep)
  Eliminate WAW data dependencies (output-dep)
Limitations
  Doesn’t remove RAW data dependencies (true-dep)
Notes: Instr window = range of instructions to search

## Slide 11
Issue (ID)
Scoreboarding
Resolving RAW dependencies
Fetch
Decode
Execute (EX, MEM, WB)
Retire
ALU
LSU
Register File
Data Memory
In-order
Out-of-order
In-order
Register
Renaming
Scoreboad

## Slide 12
Scoreboarding
CDC6600’s scoreboard: first OOO processor!
  1964 - Seymour Cray from CDC
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 13
CDC6600 - Scoreboarding
Supporting multiple fixed-latency functional units
  FP Mult x2
  FP Div
  FP Add
  Integer
    ALU
    Branch
    Mem
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 14
CDC6600 – Four-Stages Pipeline
Issue
Register Operands
Execute
Writeback
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 15
CDC6600 – Four-Stages Pipeline
Issue
  Fetch next instruction
  Wait for no hazards
    Data hazards:
      WAR: check if previous instruction is writing to any of my source operands
      WAW: check if previous instruction is writing to my destination operand
    Structural hazards: check if functional unit not available
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 16
CDC6600 – Four-Stages Pipeline
Read Operands
  Read register file
  Not check is needed
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 17
CDC6600 – Four-Stages Pipeline
Execute
  Each functional unit execute its issued instruction
  RAW data dependencies:
    Wait until all source operands are available
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 18
CDC6600 – Four-Stages Pipeline
Writeback
  Update register file
  Ensuring program ordering
    Wait until all prior instructions have completed before serving current one using Instruction Status state
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 19
CDC6600 – Scoreboard States
Instruction Status: which pipeline stage it is in
Functional Units (FU) status
  Busy - is busy
  Op - operation to execute
  Fi - destination register id
  Fj, Fk - source register ids,
  Qj, Qk - FUs producing source registers
  Rj, Rk - FUs producing source registers are ready
Register result status: which FU is producing the register
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 20
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMULT F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
INT FM1 FM2 FA FD

## Slide 21
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMULT F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Y |  |  | 
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Y | LD | F6 |  | R2 |  |  |  | Y
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
 |  |  |  |  |  | INT |  |  |  | 
Cycle1
INT FM1 FM2 FA FD

## Slide 22
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMULT F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Y | Y |  | 
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Y | LD | F6 |  | R2 |  |  |  | Y
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
 |  |  |  |  |  | INT |  |  |  | 
Cycle2
INT FM1 FM2 FA FD

## Slide 23
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMULT F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Y | Y | Y | 
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Y | LD | F6 |  | R2 |  |  |  | Y
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
 |  |  |  |  |  | INT |  |  |  | 
Cycle3
INT FM1 FM2 FA FD

## Slide 24
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMULT F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Y | Y | Y | Y
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
Cycle4
INT FM1 FM2 FA FD

## Slide 25
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMULT F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Y |  |  | 
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Y | LD | F2 |  | R3 |  |  |  | Y
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
 |  | INT |  |  |  |  |  |  |  | 
Cycle5
INT FM1 FM2 FA FD

## Slide 26
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMUL F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Y | Y |  | 
Y |  |  | 
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Y | LD | F2 |  | R3 |  |  |  | Y
Y | FMUL | F0 | F2 | F4 | INT |  | N | Y
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
FM1 |  | INT |  |  |  |  |  |  |  | 
Cycle6
INT FM1 FM2 FA FD

## Slide 27
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMUL F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Y | Y | Y | 
Y |  |  | 
Y |  |  | 
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Y | LD | F2 |  | R3 |  |  |  | Y
Y | FMUL | F0 | F2 | F4 | INT |  | N | Y
Y | FADD | F8 | F6 | F2 |  | INT | Y | N
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
FM1 |  | INT |  |  |  |  |  | FA |  | 
Cycle7
INT FM1 FM2 FA FD

## Slide 28
CDC6600 – Scoreboard Example
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
LD F6 34 R2
LD F2 45 R3
FMUL F0 F2 F4
FADD F8 F6 F2
FDIV F10 F0 F6
IS | RO | EX | WB
Y | Y | Y | Y
Y |  |  | 
Y |  |  | 
Y |  |  | 
Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Y | LD | F2 |  | R3 |  |  |  | Y
Y | FMUL | F0 | F2 | F4 | INT |  | Y | Y
Y | FADD | F8 | F6 | F2 |  | INT | Y | Y
Y | FDIV | F10 | F0 | F6 | FM1 |  | N | Y
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10
FM1 |  | INT |  |  |  |  |  | FA |  | FD
Cycle8
INT FM1 FM2 FA FD

## Slide 29
CDC6600 – Limitations
No register renaming
Detect WAR and WAW but stalls
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 30
Dynamic Scheduling
Tomasulo’s Algorithm
  Used in IBM 360/91 (in the 60s)
  Tracks when operands are available to satisfy data dependences
  Removes name dependences through register renaming
  Very similar to what is used today
    Almost all modern high-performance processors use a derivative of Tomasulo’s… much of the terminology survives to today.
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 31
Dynamic Scheduling
Tomasulo’s Algorithm
  Used in IBM 360/91 (in the 60s)
  Tracks when operands are available to satisfy data dependences
  Removes name dependences through register renaming
  Very similar to what is used today
    Almost all modern high-performance processors use a derivative of Tomasulo’s… much of the terminology survives to today.
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 32
Dynamic Scheduling
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
Reservation Stations
Instruction
Queue
LD/ST Buffers
Common data Bus

## Slide 33
Three Stages of Tomasulo Algorithm
Issue—get instruction from Instruction Queue
Execution—operate on operands (EX)
Write result—finish execution (WB)
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 34
Issue Stage
Get next instruction from instruction queue.
Find a free reservation station for it (if none are free, stall until one is)
Read operands that are in the registers
If the operand is not in the register, find which reservation station will produce it
In effect, this step renames registers (reservation station IDs are “temporary” names)
https://hackmd.io/@a5180352/S1FFbP6pz?type=view

## Slide 35
Issue Stage
https://hackmd.io/@a5180352/S1FFbP6pz?type=view
F1 = F2 + F3
F4 = F1 – F2
F1 = F2 / F3
Instruction Buffers
0
a
0
0
F2=F4+F1
Adder
FP-Cmplx
F1
F2
F3
F4
RAT
3.141593
-1.00000
2.718282
0.707107
F1
F2
F3
F4
Reg File
0.7071
3.14
To-Do list (from last slide):
Get next inst from IB’s
Find free reservation station
Read operands from RF
Record source of other operands
Update source mapping (RAT)
1.
2.
3.
Reservation stations
F1 = F2/F3
a(A1)
2.718282
A1 (a)
A2 (b)
A3 (c)
C1 (d)
C2 (e)
F2 = F4 + F1
0.

## Slide 36
Execute
Monitor results as they are produced
Broadcast result to all reservation stations with operands waiting for it (via common data bus)
When all operands available for an instruction, it is ready for execution.
When multiple instructions in RS are ready?
  Pick any
  Except for load/store (must be ordered to avoid memory hazards)

## Slide 37
Execute
F4=F1-F2
F1=F2+F3
F1=F2/F3
Adder
FP-Cmplx
A1 (a)
A2 (b)
A3 (c)
C1 (d)
C2 (e)
(d)
(a)
(a)
2.718
To-Do list (from last slide):
Monitor results from ALUs
Capture matching operands
Compete for ALUs
2.718
(a)
F2=F4+F1
(a) 3.8487
3.8487
3.8487
3.8487
F1 = F2 + F3
F4 = F1 – F2
F1 = F2 / F3
1.
2.
3.
F2 = F4 + F1
0.

## Slide 38
Execute
F4=F3-F2
F1=F2+F3
F1=F2/F3
Adder
FP-Cmplx
2.718
(a)
(a)
2.718
2.718
(a)
F2=F4+F1
(a) 3.8487
3.8487
3.8487
3.8487
Common heuristic: oldest first
You can do whatever: it only
affects performance, not correctness
A1 (a)
A2 (b)
A3 (c)
C1 (d)
C2 (e)
F1 = F2 + F3
F4 = F3 – F2
F1 = F2 / F3
1.
2.
3.
F2 = F4 + F1
0.

## Slide 39
Write Result
When result is computed, make it available on the “common data bus” (CDB), where waiting reservation stations can pick it up
Stores write to memory
Result stored in the register file
This step frees the reservation station
For our register renaming, this recycles the temporary name (future instructions can again find the value in the actual register, until it is renamed again)

## Slide 40
Write Result
Only update RAT
(and RF) if RAT still
contains your mapping!
0
0
3.8486994
F4=F1-F2
F1=F2+F3
F1=F2/F3
Adder
FP-Cmplx
(d)
2.718
To-Do list (from last slide):
Broadcast on CDB
Writeback to RF
Update Mapping
Free reservation station
2.718
3.141593
-1.00000
2.718282
0.707107
F1
F2
F3
F4
Reg File
c
a
0
b
F1
F2
F3
F4
RAT
(a)
(a)
(a)
F2=F4+F1
0.7071
3.14
(a) 0.7071+3.14
F1 = F2 + F3
F4 = F1 – F2
F1 = F2 / F3
1.
2.
3.
F2 = F4 + F1
0.
3.8487
3.8487
3.8487
X
A1 (a)
A2 (b)
A3 (c)
C1 (d)
C2 (e)

## Slide 41
Tomasulo’s Algorithm: Load/Store
The reservation stations take care of dependencies through registers.
Dependences also possible through memory
  Loads and stores not reordered in original IBM 360
  We’ll talk about how to do load-store reordering later

## Slide 42
Tomasulo Drawbacks
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Multiple CDBs => more FU logic for parallel associative stores

## Slide 43
Q&A

## Slide 44
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech