## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Logistic
Bruinlearn
Campuswire

## Slide 3: Attendance

## Slide 4: The Power of Abstraction
What is an abstraction?
Common abstractions we use in computer science?

## Slide 5: The Power of Abstraction
The classic OSI Model of Networking
Presentation layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Application Layer
Cables
Ethernet
IP
TCP
RPC
JPEG
EMAIL

## Slide 6: The Power of Abstraction
Hardware Abstraction
System Level
RTL Level
Gates Level
Transistors
NAND Gate
FIFOs, MUXs , Arbiters
MATMUL

## Slide 7: The Power of Abstraction
Computer System Abstraction
System Libraries
OS Kernel
HAL
Hardware
Applications
Video codecs
Youtube
Media decoder
Media HAL

## Slide 8: The Power of Abstraction
Computer System Abstraction
System Libraries
OS Kernel
HAL
Hardware
Applications
Video codecs
Youtube
Media decoder
Media HAL
Re-use
Portability
Scalability (apps)

## Slide 9: The Power of Abstraction
Reduction of complexity
Modularity
  Enhanced focus
  Reusability
  Scalability
  Maintainability
Portability
Divergence
  Separate growth

## Slide 10: A basic computer model
Perform tasks
  Input
    Instructions
    Data
  Execution
  Output
    Result
Computer
Instructions
Data
Output

## Slide 11: Early computers
Operated more like programmable calculators
  Manual configuration using switches
  Simple arithmetic
  Instructions physical media
    Punched cards
  Electromechanical
  e.g. Mark I
    Storage 72 numbers
    3 additions / sec
IBM Harvard Mark I (1940s)

## Slide 12: The Von-Newman Architecture
First digital computer model (1945)
  Input device
  Central processing unit (CPU)
  Memory Unit
  Output Device

## Slide 13: The Von-Newman Architecture
Memory Unit
  Digital storage
  Store Instructions and data
  Programmable
  Flexibility

## Slide 14: The Von-Newman Architecture
Single address space
  Address Partitioning
    Data region
    Instruction region
    I/O region
CPU
FFFF
0000
7FFF
8FFF
Instructions
Data
Inputs/Ouputs

## Slide 15: The Von-Newman Architecture
Single address space
  CPU microarchitecture
    One program counter
      Next instruction location
    Single memory interface
    Simple control logic
    Shared system bus
    Efficiency
CPU
FFFF
0000
7FFF
8FFF
Instructions
Data
Inputs/Ouputs
PC

## Slide 16: The Von-Newman Architecture
System Bus
  Address bus
    Specify memory address
  Data bus
    Specify data to transfer
  Control bus
    Schedule transfer

## Slide 17: The Von-Newman Architecture
Limitations
  Shared bus bottleneck
    Too many connected devices
    Control switching
  One instruction at the time

## Slide 18: The Von-Newman Architecture
Sample Exercise:
  Assume following system bus design
    2-bit control bus [O][S]
      O: read/write enable
        0 => read
        1 => write
      S: chip select
        0 => Memory
        1 => I/O
    32-bit address bus
    8-bit data bus

## Slide 19: The Von-Newman Architecture
Sample Exercise:
  CPU wants to read a byte from memory at address 0x80000000
  Step1: CPU places 0x80000000 on address bus.
  Step2: CPU selects memory for read by placing 00 on control bus
    R=0, S=0
  Step3: Memory loads the byte at specified address location in memory and puts it on the data bus
  Step4: CPU reads the byte from the data bus

## Slide 20: The Von-Newman Architecture
Sample Exercise:
  CPU wants to write a byte to I/O at address 0xFF000000
  Step1: CPU places 0xFF000000 on address bus.
  Step2: CPU places the byte to be sent on the data bus
  Step3: CPU selects I/O for write by placing 11 on control bus
    O=1, S=1
  Step4: I/O reads byte from the data bus and stores it to the specified address location in I/O

## Slide 21: The Von-Newman Architecture
Harvard Architecture Model
  Separate memory buses
    Instruction memory
    Data memory

## Slide 22: The Von-Newman Architecture
Harvard Architecture Model
  Advantages
    Simultaneous access
      Fetch data and instructions in parallel
      Increases performance
    Can specialize instruction memory
      Can be read-only (security)
      Can be non-volatile (flexibility)
      Can be faster technology (speed)

## Slide 23: The Von-Newman Architecture
Harvard Architecture Model
  Limitations
    Complexity and cost
      Multiple memory buses
    Flexibility
      Self-modifying code

## Slide 24: The Von-Newman Architecture
Von-Newman “bottleneck”
  High memory access latency
  High I/O latency
  High CPU idle time
    Waiting for memory or I/O
<10 cycles
>100 cycles
>10000 cycles

## Slide 25: The Von-Newman Architecture
CPU
Mitigations
  Caches
    Instruction cache
    Data cache
  On-chip memory
  I/O
    Data cache
    Or bypass
      Less traffic
      Typically not on critical path
Control
Logic
ALU
I-Cache
D-Cache
Memory

## Slide 26: The Von-Newman Architecture
Memory wall
  The problem still present today
  Worsen by multicore
  We use deeper caches
  Cache area getting larger than CPU
Registers (~1KB, 0.3ns)
L1 cache (~256KB, ~1.1ns)
L2 cache (~1 MB, ~5ns)
L3 cache (~8 MB, ~15ns)
L4 cache (~128MB, ~40ns)
Memory (~32GB, ~60ns)

## Slide 27: Writing the program
Simply write machine code
  Early software
Disadvantages
  Hard to write
  Difficult to debug
01010101010101010101
CPU

## Slide 28: Writing the program
Simply write machine code
Possible advantages?
  Full h/w control
  Can write efficient code
01010101010101010101
CPU

## Slide 29: Writing the program
Use a high-level language
  C++, Fortran, Python
  Higher abstraction
    Closer to the problem domain
    Objects and algorithms
mov r0 r1
add r2 r0 r1
mul r1 r3 r2
void main() {
print(“Hello world!”);
}
C++ Compiler

## Slide 30: Writing the program
Compiler
  Convert to assembly code
  Enable advanced optimizations
    Requiring program analysis
    Difficult to do by manually
mov r0 r1
add r2 r0 r1
mul r1 r3 r2
void main() {
print(“Hello world!”);
}
C++ Compiler

## Slide 31: Writing the program
Assembly code
  Textual representation of instructions
  Depend on target machine architecture
mov r0 r1
add r2 r0 r1
mul r1 r3 r2
void main() {
print(“Hello world!”);
}
C++ Compiler

## Slide 32: Writing the program
Assembler
  Convert assembly code to machine code
  Machine code contains encoded binary
    Instructions and data
  Why is this step separate from the compiler?
mov r0 r1
add r2 r0 r1
mul r1 r3 r2
Assembler
001010101010101010101010101010101010101010101010101010111110

## Slide 33: Writing the program
Machine code variations
  Context-specific pseudo instructions
  Context-specific macro expansion
  Can depend on the platform or machine
mov r0 r1
add r2 r0 r1
mul r1 r3 r2
Assembler
A
001010101010101010101010101011111111111111111111111
Assembler
B
001010101010101010101010101010101011010101010101
binary A
binary B

## Slide 34: Writing the program
Software portability challenges
  Using different CPUs
  Using different Operating Systems
void main() {
print(“Hello world!”);
}
OS-1
OS-2
CPU
A
CPU
B

## Slide 35: Writing the program
Software Abstraction layers
  Instruction Set Architecture
  Application Binary Interface
void main() {
print(“Hello world!”);
}
Operating System
Hardware
ABI
ISA
Compiler

## Slide 36: Writing the program
Application Binary Interface
  A contract between S/W and OS
  Binary compatibility
    Can OS launch App A
    Can App A interact with App B
  How?
    Function calls convention
    Stack frame organization
    Binary object format
    Etc..
void main() {
print(“Hello world!”);
}
Operating System
Hardware
ABI
ISA
Compiler

## Slide 37: Writing the program
Instruction Set Architecture
  A contract between S/W and H/W
  Software/Hardware divergence
    Can evolve independently
  Hardware abstraction
    H/w Simulation
void main() {
print(“Hello world!”);
}
Operating System
Hardware
ABI
ISA
Compiler

## Slide 38: Writing the program
Instruction Set Architecture
  S/W view
    Operations
    Storage locations
  Hardware view
    Instructions
    Data
void main() {
print(“Hello world!”);
}
Operating System
Hardware
ABI
ISA
Compiler

## Slide 39: Instruction Set Architecture
Background
  IBM System/360 architecture (1964)
  First introduction of separation between H/W and S/H
  Features
    Complex Instruction Set Computer (CISC)
    16 * 32-bit general-purpose registers
    4 * 64-bit floating-point registers

## Slide 40: Instruction Set Architecture
Mainstream ISA’s
  x86/x86-64 (AMD64) ISA: Intel, AMD
  ARM ISA: Apple, Samsung, Qualcomm
  MIPS ISA: Embedded systems, network routers, etc..
  SPARC ISA: Sun Microsystems
  RISC-V ISA: SiFive, academia, enthusiasts

## Slide 41: Computer Storage Model
Register File
  Hold a number of register slots
  Very fast (<3 cycles)
  Expensive
  Small (KB)
  Inside the CPU
Memory
  Very slow (> 100 cycles)
  Cheaper
  Larger (GB)
  Outside the CPU
Register File
Memory
ALU’s

## Slide 42: Computer Execution Model
Basic Instruction Format
  Opcode
    Type of operation
    e.g. ADD, MUL
  Operands
    Source data to use
    register identifier (e.g. r0)
    Or memory address (e.g. 0x8000)
OPCODE
OPERANDS

## Slide 43: Computer Execution Model
Fetch
  Fetch next instruction
  From program counter (PC)
Decode
  Extract opcode & operands
Execute
  Perform the operation
Update
  PC and memory
Fetch
Decode
Execute
Update

## Slide 44: How do you design an ISA?
How fast can we fetch?
How fast can we decode?
How fast can we execute?
How efficient will the hardware be?
Fetch
Decode
Execute
Update