## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Computer Hardware Model
CPU
Control Logic
  Fetch and schedule Instructions
Arithmetic Logic Unit
  Execute instructions
Register File
  Array of registers
  Fast, small storage
  Inside the CPU
Memory
  Slow, large storage
  Outside the CPU
Register File
Memory
ALU
Control Logic

## Slide 3: The Register File
Array of registers
Made of fast flip-flop devices
Addressing an entry
  Register index
Operation
  CPU read/write into array
  Providing the index
Given example
  4-entry 32-bit register file
  r2 contains 0xF0F0F0F0
ID | DATA
0 | 0x00FF00FF
1 | 0xAA008800
2 | 0xF0F0F0F0
3 | 0x00000000
Notes: Flip-flops are logic elements that store data

## Slide 4: The Main Memory
Large array of words
Made of slower DRAM devices
Addressing an entry
  word address
Operation
  CPU send read/write requests
  via the system bus
Given example
  256KB 32-bit memory device
  Total entries = capacity / word size
  0x3 contains 0x00000001
ADDRESS | DATA
0 | 0x00FF00FF
1 | 0xAA0088AA
2 | 0xF0F0F0FF
3 | 0x00000001
…. | …
.... | …
0xFFFF | 0x00000000

## Slide 5: A Memory Address Space
A mapping contiguous range of address locations that a computer used to access main memory or other peripherals connected to the computer.
The computer address bus carries the address to access a connected peripheral.
CPU
FFFF
0000
7FFF
8FFF
FFFE
Address Bus
mouse
monitor
memory
keyboard

## Slide 6: A Memory Address Space
Example2:
  CPU receives load instruction:
  e.g. LD r0, 0xFFFE
  Load the value of 0xFFFE into r0
  It will read the mouse input
  Then save the value it into register r0
CPU
FFFF
0000
7FFF
8FFF
FFFE
Address Bus
mouse
monitor
memory
keyboard

## Slide 7: A Memory Address Space
Example2:
  CPU receives store instruction:
  e.g. ST r1, 0xF
  Store the value of r1 into 0xF
  It will write r1 into memory
  At the memory location 0xF
CPU
FFFF
0000
7FFF
8FFF
FFFE
Address Bus
mouse
monitor
memory
keyboard

## Slide 8: Computer Execution Model
Basic Instruction Format
  Opcode
    Type of operation
    e.g. ADD, MUL
  Operands
    Source data to use
    register identifier (e.g. r0)
    Or memory address (e.g. 0x8000)
OPCODE
OPERANDS

## Slide 9: What is included in the ISA?
Instructions formats
Opcodes description
Data types
The registers description
Addressing modes
Memory alignment
Endianness
Control/status registers
Others
  Extensions
Software
Hardware
ISA

## Slide 10: ISA: Data Type
Data types
  Types of data that CPU can directly process
  Size information as well (32-bit or 64-bit)
Common Data Types
  Integers
  Floating-points

## Slide 11: ISA: Data Type
Extended data types
  Strings
  Complex numbers
  Vectors
  Matrices

## Slide 12: ISA: Addressing Modes
Addressing modes:
  Schemes to encode source operands
  Immediate addressing
  Register addressing
  Direct addressing
  Indirect addressing
  Displacement addressing
  Indexed addressing
  Relative addressing
  Stack addressing

## Slide 13: ISA: Addressing Modes
Immediate addressing
The operand is directly embedded within the instruction
Example:
  ADD r0, #5
Pros:
  Fast to decode
Cons:
  Limited range due to instruction size
  Cannot change operand value at runtime

## Slide 14: ISA: Addressing Modes
Register addressing
The operand is located in a register
Example:
  ADD r0, r1
Pros:
  Fast to decode
  Fast access from registers
Cons:
  Limited register file size
  Register dependencies tracking cost

## Slide 15: ISA: Addressing Modes
Direct addressing
The memory operand is directly embedded within the instruction
Example:
  LD r0, #5
Pros:
  Fast to decode
  Large memory storage
Cons:
  Memory latency
  Limited range due to instruction size
  Static address, cannot access dynamic offsets

## Slide 16: ISA: Addressing Modes
Indirect memory addressing
The instruction specifies a register that contains the address of the operand
Example:
  ADD r0, (r1)
Pros:
  Flexible dynamic address
  Flexible address range
Cons:
  Slower access: indirection
  Complex execution: indirection

## Slide 17: ISA: Addressing Modes
Displacement addressing
This combines an address held in a register with an offset value from the instruction to calculate the effective address
Example:
  ADD r0, #5(r1)
Pros:
  Flexibility for offset-based objects (e.g. structs)
  Compact S/W translation => less instructions
Cons:
  Limited offset range due to instruction size
  Computation overhead: Addition

## Slide 18: ISA: Addressing Modes
Indexed addressing
Similar to displacement addressing but typically used with arrays. A base address is combined with an index from another register.
Example:
  ADD r0, r1(r2)
Pros:
  Flexibility for array-based indexing (e.g. widgets[i])
  Compact S/W translation => less instructions
Cons:
  Registers limit and dependency cost
  Hardware complexity: addition

## Slide 19: ISA: Addressing Modes
Relative addressing
Often used in branch instructions, where the operand is a memory address relative to the Program Counter (PC)
Example:
  JMP +4 (Jump to memory at PC + 4)
Pros:
  Flexible branching: relocatable program
  Compact S/W translation => less instructions
Cons:
  Limited range due to instruction size limit

## Slide 20: ISA: Addressing Modes
Stack addressing
Operands are implicitly located on the stack.
Example:
  PUSH r0
  POP r1
Pros:
  Simplify function calls: call stack
  Automatic memory management: implicit allocation/deallocation
Cons:
  Restricted access pattern: top of the stack
  Limited applications: call stack

## Slide 21: ISA: Encoding large Immediate
Variable-length instructions
  Use multiple fetch operations
  e.g. loading 0xaaff into r0 using 16-bit instructions (8-bit immediate)
    word0 = LD r0, 0xff
    word1 = 0xaa

## Slide 22: ISA: Encoding large Immediate
Pseudo instructions
  Compute value using standard instructions (e.g. SHIFT, ADD)
  e.g. loading 0xaaff into r0 using 16-bit instructions (8-bit immediate)
    MOV r1, 0xaa;
    SHL r1, 8; // shift left by 8 bits
    OR r1, 0xff;
    LD r0, (r1)

## Slide 23: ISA: Encoding large Immediate
Fixed offset
  Assume a fixed offset to construct the full value
  For instance, using the upper half of the range
  e.g. loading 0xaaff into r0 using 16-bit instructions (8-bit immediate)
    LUI r0, 0xaa // load 0xaa into upper half (0xaa00)
    OR r0, r0, 0xff

## Slide 24: ISA: Memory alignment
Memory can be described as a contiguous array of bytes
Restrict memory accesses to addresses that are multiples of some fixed value (usually the size of the data being accessed).
e.g. 4-byte alignment: can only read words at addresses 0, 4, 8, 12, 16, …
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
FF | 7 | 0 | EE | EF | CC | 1B | A0

## Slide 25: ISA: Memory alignment
Motivation:
  When data is aligned, it is easier to access it in a single memory operation
  Affect performance and hardware cost
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
FF | 7 | 0 | EE | EF | CC | 1B | A0

## Slide 26: ISA: Memory alignment
Example:
  Assume a 32-bit CPU wants to support unaligned memory
  But its fetch unit can only load 4 bytes of word at the time.
  How will CPU execute LD r0, #1?
  Answer: send two fetch requests:
    Read w0: EFCC1BA0
    Read w1: FF0700EE
    Combine w0 & w1: EEEFCC1B
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
FF | 7 | 0 | EE | EF | CC | 1B | A0

## Slide 27: ISA: Endianness
Endianness refers to the order in which bytes are arranged and accessed in computer memory
Big-Endian: the most significant byte (the "big end") of a word is stored at the smallest memory address and the least significant byte at the highest.
  e.g. word0 = A01BCCEF
Motivation: human readable, network-friendly format
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
FF | 7 | 0 | EE | EF | CC | 1B | A0

## Slide 28: ISA: Endianness
Motivations
Little-Endian: the least significant byte (the "little end") of a word is stored at the smallest memory address and the most significant byte at the highest.
  e.g. word0 = EFCC1BA0
Motivation: arithmetic-friendly format for computation
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
FF | 7 | 0 | EE | EF | CC | 1B | A0

## Slide 29: What is included in the ISA?
Control/status registers
Special storage locations where the CPU stores its states to enable dynamic configuration and monitoring of the processor.
Example: divide by zero flags
FPU config flags (rounding mode)
FPU status flags (overflow)

## Slide 30: Computer Execution Model
Fetch
  Fetch next instruction
  From program counter (PC)
Decode
  Extract opcode & operands
Execute
  Perform the operation
Update
  Advance PC
  Update memory (result)
Fetch
Decode
Execute
Update

## Slide 31: How do you design an ISA?
Ultimate goal?
  Execute the program as fast as possible
How?
  Make all the steps execute fast
  How do you design the ISA to achieve that?
Fetch
Decode
Execute
Update

## Slide 32: How do you design an ISA?
How does the ISA affect the Fetch stage?
Fetch
Decode
Execute
Update
Instruction size
Instruction alignment

## Slide 33: How do you design an ISA?
How does the ISA affect the Decode stage?
Fetch
Decode
Execute
Update
Instruction formats
Addressing modes

## Slide 34: How do you design an ISA?
How does the ISA affect the Execute stage?
Fetch
Decode
Execute
Update
Opcode description
Registers
Data types
Addressing modes
Memory alignment
Endianness

## Slide 35: Example: 6502 8-bit CPU
Usage: poplar in the 80’s: Apple 1, 2, Nintendo NES, Atari 2600
  Variable-length instruction: 1-3 bytes
    1 byte opcode
    1-2 bytes operands
  5 Registers: A, X, Y, SP, SR
Accumulator-based architecture
A reserved register (A) used for intermediate operations.
e.g. LDA 0x10: load immediate 0x10 into accumulator.
Advantages of this design?

## Slide 36: Example: 6502 8-bit CPU
Accumulator benefits?
  Programmability
    Simplify register allocation
    Manual assembly development
  Efficiency
    Fast decode: simple instruction set
    Fast execute: single register operand
    Reference: https://en.wikibooks.org/wiki/6502_Assembly