## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3: ISA Classification
Organizing ISAs based on their characteristics
  Instruction Complexity
  Addressing mode
  Encoding style
  Parallelism

## Slide 4: ISA Classification
Instruction complexity
  CISC: Complex instruction set computing
  RISC: Relaxed instruction set computing

## Slide 5: ISA Classification
CISC Characteristics
  Small register File
  Large number of instructions
  Some instructions are complex (can perform multiple operations, taking several cycles).
    e.g. x86 string instructions: LODS, STOS
  Complex addressing modes
    immediate, register, memory
  Complex data types
    string, complex numbers
  Variable-length instructions
    Enables compact representation

## Slide 6: ISA Classification
CISC Design Motivations
  Reducing register file
    Transistor cost was high
  Reducing program size
    Memory was very expensive
  Complex instructions
    Simplify assembly programming
    Compilers were very primitive

## Slide 7: ISA Classification
RISC Characteristics
  Smaller set of instructions
  Optimized instructions to execute in single clock
  Uniform instruction format
  Identical general purpose registers
  Simple address mode
  Fewer data type
  Fixed-Length Instruction
    Simplify instruction decoding

## Slide 8: ISA Classification
RISC Design Motivations
  Simpler was often faster
    Complex instructions took more time than multiple simpler ones
  Memory got cheaper and larger
    Could store more instructions
  Transistors got cheaper
    Could afford larger register file
  Compiler got better
    Move complexity to the compiler
How did Intel address the shortcoming of CISC?

## Slide 9: ISA Classification
Intel solutions
  Intel cannot drop CISC
    Legacy software and operating systems
    Some critical applications cannot be modified (no sources)
    Introducing a new ISA versus licensing ARM both costly
  Introduce RISC-like microarchitecture
    Translate CISC into RISC micro-ops

## Slide 10: ISA Classification
CISC-like ISA is still relevant today
  Domain-specific accelerators
  e.g. Google TPU’s MatrixMul instruction
TPU paper:
https://dl.acm.org/doi/pdf/10.1145/3079856.3080246

## Slide 11: ISA Classification
Parallelism
  VLIW ISA
  Vector ISA

## Slide 12: ISA Classification
VLIW ISA (Very Long Instruction Word)
  Encode multiple operations into a single long instruction word
  The idea is to execute each operation on a different execution unit in parallel
  Example: Intel IA64 (2001)
    [Load R1, Add R2, Store R3, NOP]
  Static instruction scheduling
    The compiler is responsible to ensuring that that all operations within the instruction have no dependencies and can execute in parallel.

## Slide 13: ISA Classification
VLIW ISA (Very Long Instruction Word)
  Need multiple fetches to get a long instruction?
    No, relies on wide data bus (e.g. 64-bit)
    Otherwise, fetch will be too slow

## Slide 14: ISA Classification
VLIW ISA Design Motivation
  Hardware simplification
    Move the complexity of instruction scheduling to the compiler
    No need to worry about data dependency
  High Parallelism
    Enable multiple operations to execute in parallel
    Exploit Instruction-level parallelism (ILP)

## Slide 15: ISA Classification
VLIW ISA Shortcomings
  Compiler complexity
    Expensive if hardware changes
  Portability
    Too much coupling with hardware
    Process changes renders binary incompatible
  Static Scheduling
    Limits runtime adaptation
      e.g. cache miss, branch prediction, etc…
  Code Size
    Instructions are typical large, increase memory bandwidth

## Slide 16: ISA Classification
Vector ISAs
  Single Instruction Multiple Data (SIMD)
  Fetch multiple Data at once
  Parallel data processing
  Examples:
    Intel AVX
      Vfmadd231ps y3, y2, y1, y0
      y37-0 = y07-0 * y17-0 + y27-0
    ARM Neon
      vmla.f32 v2, v1, v0
      v23-0 += v03-0 * v13-0
ID | DATA0 | DATA1 | DATA2 | DATA3
0 | 0x00FF00FF | 0x00000000 | 0x00FF00FF | 0x00FF00FF
1 | 0xAA008800 | 0xFFFFFFFF | 0x00FF00FF | 0xFFFFFFFF
2 | 0xF0F0F0F0 | 0xF0F0F0F0 | 0xF0F0F0F0 | 0xF0F0F0F0
3 | 0x00000000 | 0x00000000 | 0xFFFFFFFF | 0x00FF00FF
Vector Register File

## Slide 17: ISA Classification
Vector ISAs Limitations
  Memory bandwidth
    Increased memory requests
  Control-flow limitations
    Divergent conditional values
  Programmability
    Vectorization not always possible
    Data alignment restrictions

## Slide 18: ISA Classification
Vector ISAs Limitations
  Memory bandwidth
    Increased memory requests
  Control-flow limitations
    Divergent conditional values
  Programmability
    Vectorization not always possible
    Data alignment restrictions

## Slide 19: The RISC-V ISA
The fifth RISC Instruction Set Architecture
  First generation: efficient ISA proposal 80-70’s IBM 801
  Second generation: commercialization (SPARC from Sun Microsystems)
  Third generation: segmentation (embedded market)
  Fourth generation: widespread adoption (ARM)
  Fifth generation?
    Open standard: no licensing and royalty constraints
    Free to use and adapt
    Focus: efficiency, extensibility, and accessibility.
Reference Specs: https://riscv.org/wp-content/uploads/2017/05/riscv-spec-v2.2.pdf

## Slide 20: RISC-V Extensions
RISC-V composable and Modular design
Base ISAs:
  RV32-I – 32-bit integer – this course only
  RV64-I – 64-bit integer
  RV128-I – 128-bit integer
Notes: A hypervisor is a host operating system for virtual machines

## Slide 21: RISC-V Extensions
Frozen Extensions:
  M: multiply and divide – why not including this into Baseline?
  C: compressed instructions
  F: single-precision floating-point
  D: double-precision floating-point
  Q: quad-precision floating-point
  A: atomics
  H: hypervisor
How to compose?
  e.g. RV32-IMF includes I, M, and F extensions
Notes: A hypervisor is a host operating system for virtual machines

## Slide 22: RISC-V Extensions
Open Extensions:
  V: Vector
  P: Packed SIMD – how different from V?
  B: Bit manipulation
  T: Transactional memory
  N: User-level interrupts
  J: JIT support
Notes: Vector: separate register file with multiple lanes of data
Packed SIMD: partition existing data in current register file. e.g A 32-bit data can be represented as 4 x 8-bit elements.
JIT support: garbage collection, context switching
Transactional memory: execute multiple memory operations as a single atomic transaction (e.g. start, commit, abort)

## Slide 23: RISC-V Instruction encoding
32-bit fixed-length instructions
  Naturally aligned at 32-bit boundaries
Compress extension use 16-bit instructions
  Aligned is relaxed to 16-bit boundaries
Variable-length encoding is supported via extensions
  Use LSB bits for detection

## Slide 24: RISC-V Base Instruction Formats
Formats classified based on addressing mode and operation type
  R-type: register
  I-type: direct
  S-type: store
  B-type: branch
  U-type: immediate
  J-type: jump
Notes: Jumps are unconditional branches

## Slide 25: RISC-V Base Instruction Formats (2)
Instructions encoding details
  Which opcode?
  Which func3 value?
  Which func7 value?
  See specs chapter 9
Notes: Jumps are unconditional branches

## Slide 26: Background: Integer extension
Motivation: increase the number of bits of a binary number while preserving its value.
  Useful for compatibility when using arithmetic units of varying data width.
Zero-extension: append 0’s
    e.g. 0xF000 => 0x0000F000
Sing-extension: append 1’s when MSB is 1 and 0’s otherwise
    e.g. 0x8000 => 0xFFFF8000 # note that 8 = 1000 where MBS=1
Notes: Jumps are unconditional branches

## Slide 27: RISC-V Immediate variants
Two immediate lengths
  S and B: 12 bits
  U and J: 20 bits
Sign-extension
  Fixed location for sign-bit in Inst[31] to enable sign-extension to execute in parallel
Notes: Jumps are unconditional branches

## Slide 28: RISC-V Integer Register-Immediate Instructions
ADDI: adds the sign-extended 12-bit sign-extended immediate to rs1
  NOP is pseudo instruction: encoded as ADDI x0, x0, 0
SLTI: set less than immediate – set rd to 1 if rs1 < sign-extended immediate
SLTU: set less than immediate – set rd to 1 if rs1 < unsigned immediate
ANDI, ORI, XORI; bitwise logical operations with 12-bit sign-extended immediate and rs1
Example: given opcode = 0010011 & func3 = 010, “SLTI x6, x5, 2” is encoded as
instruction word = 000000000010-00101-010-00110-0010011 = 0x0022A313
Notes: Jumps are unconditional branches

## Slide 29: RISC-V Integer Register-Immediate Instructions
SLLI: left-shift rs1 left by 5-bit immediate
SRLI: right-shift rs1 left by 5-bit immediate
SRAI: arithmetic right-shift rs1 left by 5-bit immediate
Notes: Jumps are unconditional branches

## Slide 30: RISC-V Load Immediate
LUI: move 20-bit unsigned immediate into upper 20 bits on rd and zero lower 12 bits
  Rd = signed(imm20 << 12)
  Useful for loading immediate values into a register
AUIPC: add upper immediate to PC
  Rd = signed(imm20 << 12) + PC
  Useful for computing a branch target address
Notes: Jumps are unconditional branches

## Slide 31: RISC-V Register-Register Operations
ADD, SUB: addition and subtraction using register operands
SLL, SRL, SRA: Shift operations using register operands
Notes: Jumps are unconditional branches

## Slide 32: RISC-V Control transfer Instructions
JAL: Plain unconditional jumps
  Target address = sign-extended 12-bit immediate
  Link register rd
  If (rd != 0) PC + 4 is written into rd
Notes: Jumps are unconditional branches

## Slide 33: RISC-V Control transfer Instructions
JALR: indirect jump
  Target address = sign-extended 12-bit immediate + src1
  Link register rd
  If (rd != 0) PC + 4 is written into rd
Notes: Jumps are unconditional branches

## Slide 34: RISC-V Control transfer Instructions
Conditional branches
  Compare rs1 and rs2
  Target address = sign-extended 12-bit immediate + PC
Notes: Jumps are unconditional branches