## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3: Homework #2
Questions 2 and 3 had a grading option error.
- fixed

## Slide 4: RISC-V Base Instruction Formats
Formats classified based on addressing mode and operation type
  R-type: register
  I-type: direct
  S-type: store
  B-type: branch
  U-type: immediate
  J-type: jump
Notes: Jumps are unconditional branches

## Slide 5: RISC-V Control transfer Instructions
JAL: Plain unconditional jumps
  Target address = sign-extended 12-bit immediate
  Link register rd
  If (rd != 0) PC + 4 is written into rd
Notes: Jumps are unconditional branches

## Slide 6: RISC-V Control transfer Instructions
JALR: indirect jump
  Target address = sign-extended 12-bit immediate + src1
  Link register rd
  If (rd != 0) PC + 4 is written into rd
Notes: Jumps are unconditional branches

## Slide 7: RISC-V Control transfer Instructions
Conditional branches
  Compare rs1 and rs2
  Target address = sign-extended 12-bit immediate + PC
Notes: Jumps are unconditional branches

## Slide 8: RISC-V Load and Store instructions
LOAD: load value from memory
  Rd = MEM[base + offset]
  Width = size of word
    LB: 000
    LH: 001
    LW: 010
    LBU: 100 (unsigned)
    LHU: 101 (unsigned)
    LWU: 110 (unsigned)
Notice anything about MSB value?
Notes: Jumps are unconditional branches

## Slide 9: RISC-V Load and Store instructions
Problem:
  Given a 32-bit RISC-V CPU, consider you have a memory segment starting at address 0x10010000, and you need to load an unsigned byte located at address 0x1001002A into register x5. Use x2 as your base address.
  Q1: Write the assembly code for this load instruction
  Q2: Write the instruction code for this load instruction
Notes: Jumps are unconditional branches

## Slide 10: RISC-V Load and Store instructions
Q1 Solution:
  Target address: 0x1001002A
  Base address: 0x10010000
  Offset: 0x1001002A - 0x10010000 = 0x2A = 42
  Which width mode to use?
    LBU (100)
  Assembly:
    lbu x5, 42(x2)
Notes: Jumps are unconditional branches

## Slide 11: RISC-V Load and Store instructions
Q1 Solution:
  We also need to update x2 with base address 0x10010000
  Which format can we choose?
    Let’s try Load upper immediate
Notes: Jumps are unconditional branches

## Slide 12: RISC-V Load and Store instructions
Q1 Solution:
  Load upper immediate
  Move upper 20-bits
  0x10010000
  shifted right by 12 = 0x10010
  Assembly: lui x2, 0x10010
Notes: Jumps are unconditional branches

## Slide 13: RISC-V Load and Store instructions
Q2: Solution
  Opcode: 0000011
  rd: The destination register, x5, in binary is 00101.
  func3: 100 (for LBU)
  rs1: The base register, x2, in binary is 00010.
  imm[11:0]: The offset 0x2A in 12-bit binary is 000000101010.
  Instruction code: 000000101010-00010-100-00101-0000011
  Instruction code: 0x02A14503
Notes: Jumps are unconditional branches

## Slide 14: RISC-V Load and Store instructions
STORE: store value to memory
  MEM[base + offset] = src
  Width = size of word
    SB: 000
    SH: 001
    SW: 010
<- No unsigned variants?
Notes: Jumps are unconditional branches

## Slide 15: RISC-V Load and Store instructions
Problem:
  Given a 32-bit RISC-V CPU, consider you have a memory segment starting at address 0x10010000, and you need to store a half-word from register x10 into memory address 0x1001002C. Use x2 as your base address.
  Q1: Write the assembly code for this load instruction
  Q2: Write the instruction code for this load instruction
Notes: Jumps are unconditional branches

## Slide 16: RISC-V Load and Store instructions
Q1 Solution:
  Target address: 0x1001002C
  Base address: 0x10010000
  Offset: 0x1001002C - 0x10010000 = 0x2C = 44
  Which width mode to use?
    SH (001)
  Assembly: sh x10, 44(x2)
Notes: Jumps are unconditional branches

## Slide 17: RISC-V Load and Store instructions
Q2: Solution
  opcode: 0100011 (for S-type store operations)
  imm[11:5]: Upper 7 bits of the offset 0x2C in binary is 0000010.
  rs2: The source register x10 in binary is 01010.
  rs1: The base register x2 in binary is 00010.
  func3: 001 (for SH)
  imm[4:0]: Lower 5 bits of the offset 0x2C in binary is 01100.
  Instruction code: 0000 010-01010-00010-001-01100-0100011
  Instruction code: 0x02A1C23
Notes: Jumps are unconditional branches

## Slide 18: RISC-V Control and Status Instructions
Read/Write to CSRs
  #csr = address to 12-bit CSR table
  CSRRW: atomic read/write: csr_new = source, dest = csr_old
  CSRRS: atomic read set: csr_new = csr_old | source , dest = csr_old
  CSRRC: atomic read & clear: csr_new = csr_old & ~source , dest = csr_old
Notes: Jumps are unconditional branches

## Slide 19: RISC-V Control and Status Instructions
Read/Write to CSRs
  #csr = address to 12-bit CSR table
  CSRRWI: atomic read/write: csr_new = uimm, dest = csr_old
  CSRRSI: atomic read set: csr_new = csr_old | uimm , dest = csr_old
  CSRRCI: atomic read & clear: csr_new = csr_old & ~ uimm , dest = csr_old
Notes: Jumps are unconditional branches

## Slide 20: RISC-V Control and Status Instructions
User-level CSR Table
Standard mapping
  FPU flags
  Cycle
  Time
  Instret
  HPM Counters
Notes: HPM: hardware performance monitoring counter

## Slide 21: RISC-V Control and Status Instructions
Problem:
  Write a RISC-V assembly instruction to read the value of the utime CSR, which holds the machine-mode timer's current value, and store it into general-purpose register x5.
Notes: Jumps are unconditional branches

## Slide 22: RISC-V Control and Status Instructions
Solution:
  Read-only: CSRRS with x0
  Time CSR address: 0xC01.
  Destination register: x5
  Assembly: csrrs x5, 0xC01, x0
Notes: Jumps are unconditional branches

## Slide 23: RISC-V Control and Status Instructions
Privilege Levels: defines the level of access that software has to the processor and system resources. They enable:
  Access control: control what an application can do
  Security: run an application in isolation from others
Notes: Jumps are unconditional branches

## Slide 24: RISC-V Control and Status Instructions
RIS-V Privilege Levels
  User-level (U)
  Hypervisor (H)
  Supervisor (S)
  Machine-level (M)
Hypervisor
H
Notes: Jumps are unconditional branches

## Slide 25: RISC-V Control and Status Instructions
User-level (U): User-level CSRs are accessible from the user mode, which is the least-privileged mode of operation. These registers typically contain information or controls that are safe to expose to user applications, such as performance counters that can be read without compromising system integrity.
Notes: Jumps are unconditional branches

## Slide 26: RISC-V Control and Status Instructions
Hypervisor-level (H): Hypervisor mode is an optional privilege level introduced in newer versions of the RISC-V specification, designed for virtualization. It sits between M-mode and S-mode and is used to run and manage virtual machines.
Notes: Jumps are unconditional branches

## Slide 27: RISC-V Control and Status Instructions
Supervisor-level (S): Supervisor mode is used by operating systems to control system resources and manage user applications. It has a lower privilege than M-mode but can still perform system-level tasks.
Notes: Jumps are unconditional branches

## Slide 28: RISC-V Control and Status Instructions
Machine-level: Machine-level CSRs are accessible from machine mode, which is the most privileged mode of operation. These registers are used for controlling low-level, sensitive aspects of the hardware, such as interrupt handling, exception handling, and access to physical memory.
Note: default level for low-level embedded CPUs
Notes: Jumps are unconditional branches

## Slide 29: RISC-V Control and Status Instructions
How is the privilege level set/modified?
CPU starts at machine level (M)
S/W can use CSR mstatus can be used to lower the privilege level
CPU can use exception handling to increase the privilege level
RISC-V mret, sret, uret are system return instructions for switching back to previous privilege level.
Notes: Jumps are unconditional branches

## Slide 30: RISC-V Control and Status Instructions
How is the privilege level enforced?
If software running at a lower privilege level attempts to execute a privileged instruction, protected address space, or privileged interrupt, the processor raises an exception
Notes: Jumps are unconditional branches

## Slide 31: RISC-V Control and Status Instructions
CSR Privilege Mapping
Why reserving dedicated bits for level?
Notes: Jumps are unconditional branches

## Slide 32: RISC-V Control and Status Instructions
Timers and counters
  64-bit registers
  RD_CYCLE: total cycle time
  RD_TIME: wall-clock time
  RD_INSTRET: total instructions
Notes: walltime is the actual time taken from the start of a computer program to the end

## Slide 33: RISC-V Control and Status Instructions
Timers and counters
  How to read RD_CYCLE on 32-bit machine?
  Why could this be challenging?
    Counter 32-bit overflow
  Solution
    Read Low 32-bit
    Read high 32-bit
Notes: walltime is the actual time taken from the start of a computer program to the end

## Slide 34: RISC-V Control and Status Instructions
Assembly code
  csrrs x2, cycle, x0
  csrrs x3, cycleh, x0
What timing issue may emerge from the above code?
  x2 and x3 may not match
  Hundreds of CPU cycles can happen between the two calls
  Reading cycleh could happen after cycle 32-bit overflow
Notes: walltime is the actual time taken from the start of a computer program to the end

## Slide 35: RISC-V Control and Status Instructions
Solution
  loop: csrrs x3, cycleh, x0
  csrrs x2, cycle, x0
  csrrs x4, cycleh, x0
  bne x3, x4, loop
How does this work?
  It takes a while for cycleh change
  The loop handle the overflow cases
Notes: walltime is the actual time taken from the start of a computer program to the end

## Slide 36: RISC-V Registers
32 general-purpose registers
Separate floating-point registers
Register r0=0x0 - why?
Hidden PC register
  accessible via CSRs only
Notes: Why Zero?
- predominant value for comparisons and arithmetic operations
- simple instruction decoding when no registers is needed
- simple register file access logic when no register is needed

## Slide 37: RISC-V Registers
ABI Calling convention:
Arguments: a0-7
Return: r0
Temporaries: t0-6
Saved registers: s0-11
Who back up registers during calls?
  Caller/parent
  or Callee/child
Notes: Why Zero?
- predominant value for comparisons and arithmetic operations
- simple instruction decoding when no registers is needed
- simple register file access logic when no register is needed

## Slide 38: RISC-V Registers
Return address (ra)
  Store the return address during function calls
  Hold the next PC of the caller
  Example: what is the value of ra when bar() is executing?
void bar() {
<print(“hello”);>
}
void foo() {
bar(); // call bar()
<print(“world\n”);>
}
# foo
0F00: ???
0F04: ???
0F08: jal ra, 0xF80
0F0C: ???
…
# bar
0F80: ???
0F84: ???
0F88: ???
0F8C: jalr x0, 0(ra)
Notes: ra will hold the next instruction address when calling jal.

## Slide 39: RISC-V Registers
Stack pointer (sp)
  Used for managing function call stack.
  The stack holds function’s temp variables that could not fit into registers.
  Initialized to a starting location at boot time.
  CPU determines the stack base address STACK_BASE_ADDR
  la is a “load address” pseudo instruction
    resolve to one or multiple RISC-V native instructions
    depending on address value
# stack initialization
la gp, STACK_BASE_ADDR
Notes: ra will hold the next instruction address when calling jal.

## Slide 40: RISC-V Registers
Stack pointer (sp)
  Example: A program uses 16 bytes of stack storage.
# Assume that x5 and x6 contain values that we want to preserve
# First, we'll adjust the stack pointer to allocate 8 bytes of space
addi sp, sp, -8 # Decrement the stack pointer by 8 bytes
# Now we'll store x5 and x6 onto the stack at the allocated space
sw x5, 0(sp) # Store x5 at the beginning of the allocated space
sw x6, 4(sp) # Store x6 right after x5
# ... the code can now use x5 and x6 for other operations…
add x5, x0, x1
add x6, x0, x1
# To restore the values of x5 and x6, we'll load them back from the stack
lw x5, 0(sp) # Load x5 from the stack
lw x6, 4(sp) # Load x6 from the stack
# Finally, we'll adjust the stack pointer back to free the 8 bytes
addi sp, sp, 8 # Increment the stack pointer by 8 bytes to restore its original value
Notes: ra will hold the next instruction address when calling jal.

## Slide 41: RISC-V Registers
Global pointer (gp)
  Points to the middle of a global data segment
  Why the middle?
    Reduces instruction’s immediate value when accessing to global variables
  Initialized to a starting location at boot time.
  Linker exports macro __global_pointer for a given program.
  la is a “load address” pseudo instruction
    resolve to one or multiple RISC-V native instructions
    depending on address value
# stack initialization
la gp, __global_pointer
Notes: ra will hold the next instruction address when calling jal.

## Slide 42: RISC-V Registers
Global pointer (gp)
  Example
.data
array: .word 0, 1, 2, 3, 4
.text # Assuming gp points to `array`
lw t0, 0(gp) # Loads the first element of `array` into t0
Notes: ra will hold the next instruction address when calling jal.

## Slide 43: RISC-V Registers
Thread pointer (tp)
  used to efficiently access thread-local storage (TLS)
  TLS holds data unique to each thread in a multi-threading environment
  Initialized to a starting location at boot time for each thread
# Assuming the thread-specific variable is at offset 0x10 from the thread pointer
lw t0, 16(tp) # Load the thread-specific variable into register t0
Notes: ra will hold the next instruction address when calling jal.

## Slide 44: RISC-V Registers
Thread pointer (tp)
  used to efficiently access thread-local storage (TLS)
  TLS holds data unique to each thread in a multi-threading environment
  Initialized to a starting location at boot time.
  __tcb_aligned_size is assigned by linker
csrr t0, VX_CSR_MHARTID
sll t1, t0, STACK_LOG2_SIZE #
sub sp, sp, t1
# set thread pointer register
# use address space after BSS region
# ensure cache line alignment
la t1, __tcb_aligned_size # allocated TLS size
mul t0, t0, t1
la tp, _end + 63
add tp, tp, t0
and tp, tp, -64
ret
Notes: ra will hold the next instruction address when calling jal.