## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
RISC-V Pipelined Architecture
Project #1

## Slide 4: 5-Stage Pipeline RISC-V Processor

## Slide 5: Basic RISC-V CPU Control Path
Data Path
Control Path

## Slide 6
Exercise: Single-Cycle vs Pipeline
Calculate cycle time (CT)
Unit | Latency (ps)
Instruction Fetch | 400
Register Access | 300
ALU | 200
Memory Access | 400

## Slide 7
Exercise: Single-Cycle vs Pipeline
Single-Cycle Datapath
Instr | Data Path
R/I-type | IF+RR+ALU+RW
LW | IF+RR+ALU+MR+RW
SW | IF+RR+ALU+MW
BEQ | IF+RR+ALU

## Slide 8
Exercise: Single-Cycle vs Pipeline
Single-Cycle Datapath
Instr | Data Path | Cycle Time | Total Time
R/I-type | IF+RR+ALU+RW | 400+300+200+300 | 1200 ps
LW | IF+RR+ALU+MR+RW | 400+300+200+400+300 | 1600 ps
SW | IF+RR+ALU+MW | 400+300+200+400 | 1300 ps
BEQ | IF+RR+ALU | 400+300+200 | 900 ps

## Slide 9
Exercise: Single-Cycle vs Pipeline
Pipeline Datapath
Instr | Data Path | Cycle Time | Total Time
R/I-type | IF¦RR¦ALU¦RW | Max(400,300,200,300) | 400 ps
LW | IF¦RR¦ALU¦MR¦RW | Max(400,300,200,400,300) | 400 ps
SW | IF¦RR¦ALU¦MW | Max(400,300,200,400) | 400 ps
BEQ | IF¦RR¦ALU | Max(400,300,200) | 400 ps

## Slide 10
Pipeline Hazards
Consider this scenario:
  I0: add x5, x1, x2
  I1: sub x20, x5, x4
Source registers:
  I0: x1, x2
  I1: x5, x4
Destination registers:
  I0: x5
  I1: x20

## Slide 11
Pipeline Hazards
Register dependency:
  X5’s result is not ready for I1
  Should we care?

## Slide 12
Pipeline Hazards
Programmer expects instructions ordering:
  To get expected result
  I0: add x5, x1, x2
  I1: sub x20, x5, x4

## Slide 13
Pipeline Hazards
Should the processor enforce instructions ordering?
  Only externally
    Memory is visible to S/W
    Registers are visible to S/W (e.g. debugger)
  Can do any optimization it wants internally

## Slide 14
Pipeline Hazards
What’s a pipeline hazard?
  Resource sharing conflict inside the pipeline
  Pipelining introduces resource sharing between instructions
    Register file
    Execution units

## Slide 15
Pipeline Hazards
Types of pipeline hazard
  Control hazard
  Structural hazard
  Data hazard

## Slide 16
Control Hazards
Control-flow dependency between instructions
  Target address or condition not yet available to a branch instruction

## Slide 17
Structural Hazards
Resource sharing between instructions
  Prior instruction still using a resource that current instruction need
  e.g. Multi-cycle integer divider unit

## Slide 18
Data Hazards
Register sharing between instructions
  Operands are not yet available to an instruction
  Because prior instruction has not yet produced result

## Slide 19
Data Hazards
Types of data Hazards
  Read after write (RAW)
  Write after write (WAW)
  Write after read (WAR)
  Read after read (RAR)

## Slide 20
Data Hazards: RAW
Reading a register before its write completes
Example:
  I0: add x5, x1, x2
  I1: sub x20, x5, x4

## Slide 21
Data Hazards: RAW
How many cycles should I1 stall?
  I0: add x5, x1, x2
  I1: sub x20, x5, x4
Notes: Solution: 2 cycles

## Slide 22
Data Hazards: WAW
Writing to a register before its write completes
Example:
  I0: add x5, x1, x2
  I1: sub x5, x3, x4
Is it a dependency issue?

## Slide 23
Data Hazards: WAW
I1 will update x5 after I0
  I0: add x5, x1, x2
  I1: sub x5, x3, x4
I0
I1
I2

## Slide 24
Data Hazards: WAW
WAW is not an issue here
  Due to in-order program execution
Problematic if out of order execution

## Slide 25
Data Hazards: WAR
Writing to a register before it is read
Example:
  I0: add x2, x1, x5
  I1: sub x5, x3, x4
Is it a dependency issue?

## Slide 26
Data Hazards: WAR
I1 will update x5 after I0
  I0: add x2, x1, x5
  I1: sub x5, x3, x4
I0
I1
I2

## Slide 27
Data Hazards: WAR
WAR is not an issue here
  Due to in-order program execution
Problematic if out of order execution

## Slide 28
Data Hazards: RAR
Reading from a register before it is read
Example:
  I0: add x2, x1, x5
  I1: sub x20, x5, x4
Is it a dependency issue?

## Slide 29
Data Hazards: RAR
No dependency issue
  We are only reading

## Slide 30
Resolving RAW hazards
Naïve approach:
  We stall the pipeline!
  Wait until the register value is ready

## Slide 31
Resolving RAW hazards
Example1:
  RAW?
  x2

## Slide 32
Resolving RAW hazards
Solution1:
  Insert 1 bubble
  Or NOP

## Slide 33
Resolving RAW hazards
Example2:
  I0: add x5, x1, x2
  I1: sub x20, x5, x4

## Slide 34
Resolving RAW hazards
Solution2:
  Insert 2 bubbles
  Or 2 NOPs

## Slide 35
Resolving RAW hazards
Better Solution:
  Stalls hurt pipeline performance
  How to prevent stalls?
  Use Data Forwarding instead

## Slide 36
Resolving RAW hazards
Data forwarding:
  Redirect computed result directly to ALU

## Slide 37
Resolving RAW hazards
Data forwarding:
  Will need two forwarding paths
  Any disadvantage?

## Slide 38
Resolving RAW hazards
Data forwarding: Cost
  Need extra wiring
  Need multiplex to choose ALU source
  Propagation delay may increase

## Slide 39
Resolving RAW hazards
Data forwarding: Memory-ALU
  Load-Use propagation cost
  Not practical

## Slide 40
Resolving RAW hazards
Data forwarding: Memory-ALU
  Do one-step forwarding instead of two
  Add one bubble

## Slide 41
Resolving RAW hazards
Data forwarding: design1
  Insert MUXs before ALU

## Slide 42
Resolving RAW hazards
Data forwarding: design2
  Insert MUXs before register

## Slide 43
Resolving RAW hazards
Data forwarding: which design is better?
  The one with shorter propagation delay
  Register File extension vs ALU extension
Design1
Design2

## Slide 44
Resolving RAW hazards
Data forwarding: detect RAW forwarding?

## Slide 45
Project #1
Context:
  Partial implementation of a RISC-V CPU in C++
  RISC-V RV32-I specs
  RISC-V conformance tests
  Decoder incomplete
  No data forwarding
  No control forwarding

## Slide 46
Project #1
CPU Architecture:
  Emulator: generate instruction trace
  Cycle-level simulator: generate instruction timing

## Slide 47
Project #1
To implement:
  Instruction encoding
  Data forwarding
  Control forwarding

## Slide 48
Project #1
Evaluation:
  Program compiles: 5 pts
  All tests passed: 5pts
  Timing is correct: 5 pts