## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
Control Hazards
Midterm Review

## Slide 4
Recap of Data Forwarding
Data forwarding: ALU to ALU
  Forwarding from EX/MEM pipeline latch
  Forwarding from MEM/WB pipeline latch

## Slide 5
Recap of Data Forwarding
Data forwarding: Memory-ALU
  Add one bubble/NOP
  Then forwarding from MEM/WB pipeline latch

## Slide 6
Control Hazards
Understanding branches
  e.g. for loop
int main() { for (int i = 0; i < 10; i++) { // loop body } return 0; }
main: li t0, 0 # i = 0 li t1, 10 # n=10
loop:
addi t0, t0, 1 # i = i + 1 bne t0, t1, loop # if (i != n) => loop
exit: li a0, 0 # return 0 ret

## Slide 7
Control Hazards
Data and control dependence
  I0: addi x5, x5, 1
  I1: bne x5, x6, loop
Whether to branch?
  (x5 == x6)
Where to branch?
  PC + imm
I0 I1

## Slide 8
Control Hazards
RISC-V branches
Conditional branches
  BEQ r1, r2, imm; // if (r1 == r2) => PC = PC + imm
Unconditional branches
  JAL rd, imm; // rd = PC + 4; PC = PC + imm
  JALR rd, rb, imm; // rd = PC + 4; PC = rb + imm

## Slide 9
Control Hazards
CPU must answer 3 questions:
Which type of branch?
Whether to branch?
Where to branch?

## Slide 10
Control Hazards
Which type of branch
  Where to determine this?
  ID stage

## Slide 11
Control Hazards
Whether to branch
  Where to determine this?
  MEM stage (PCSrc)

## Slide 12
Control Hazards
Where to branch
  Where to determine this?
  EX stage

## Slide 13
Control Hazards
Which stage should stall?
  ID stage
Why?
  Next PC

## Slide 14
Control Hazards
When is new PC updated?
  Next cycle after PCSrc

## Slide 15
Control Hazards
When is new PC updated?
  PCSrc is ready in MEM
  New PC is ready in WB

## Slide 16
Control Hazards
Stall cycles needed?
  3 cycles
Can we do better?

## Slide 17
Control Hazards Handling
Software Solution: Insert NOPs
  S/W insert NOPs in delay slots
  Pros:
    No H/W cost
  Cons:
    Bad performance: still stalling
    S/W depends on H/W stall count

## Slide 18
Control Hazards Handling
Software Solution: Delayed branch
  S/W insert useful instructions in delay slots
  Pros:
    No H/W cost
    Improved performance
  Cons:
    Hard to find useful instructions
    S/W depends on H/W stall count

## Slide 19
Control Hazards Handling
Hardware Solution: Stall the pipeline
  Pros:
    S/W independence
    Minimal H/W cost
  Cons:
    Bad performance

## Slide 20
Control Hazards Handling
Hardware Solution: Speculation
  Pros:
    S/W independence
    Better performance
  Cons:
    H/W cost

## Slide 21
Control Hazards: Speculation
Predict: Not taken
  Emulate delay branch
  Pros: no wasted cycles
  Cons: mis-prediction cost

## Slide 22
Control Hazards: Speculation
Predict: Not taken
  How to detect misprediction?
    Branch condition is taken
  When?
    MEM stage

## Slide 23
Control Hazards: Speculation
Predict: Not taken
  How to recover from misprediction?
    Flush the pipeline (invalidate each previous stage)
    Reset PC

## Slide 24
Control Hazards: Speculation
Practical Branch stats
  About 20% of instructions is control-flow
    50% of forward branches (if-then-else) are taken
    90% of backward branches (loops) are taken
    30% of all branches are not-taken

## Slide 25
Control Hazards: Speculation
Practical Branch stats
  About 20% of instructions is control-flow
    50% of forward branches (if-then-else) are taken
    90% of backward branches (loops) are taken
    30% of all branches are not-taken
Not-taken prediction accuracy?
  Only 30%
  Cost: 3 cycles

## Slide 26
Control Hazards: Speculation
Reducing Misprediction Cost
  Resolving branches sooner
  Making it 2 cycles can be done

## Slide 27
Control Hazards: Speculation
Reducing Misprediction Cost
  More aggressive solution: Branch only
  Move NextPC to DE
  Move PC + imm to DE
Warning: r1/r2 RAW
  Need data forwarding!

## Slide 28
Control Hazards: Speculation
Predict: Always Taken
What do we need?
  nextPC
  At fetch stage

## Slide 29
Control Hazards: Speculation
Predict: Always Taken
  How to obtain nextPC?
  We can predict

## Slide 30
Control Hazards: Speculation
Predict: Always Taken
  How to obtain nextPC?
  We can predict

## Slide 31
Midterm Review
performance/cost tradeoffs between single-cycle, multi-cycle, pipeline architecture.
memory alignment, motivation, hardware and software workarounds
RISC-V vs CISC vs VLIW
CPU time, CPI, cycle time, clock rate, clock frequency
the memory wall problem
what the memory address is, what the address bus is, what the data bus is, what the control bus is?
what is included and not included in the ISA, and why?
Addressing modes; should be able to compare two (pros/cons) given the description of how they work
How RISC-V immediate is encoded, e.g JAL format is [imm[20], imm[10:1], imm[11], imm[19:12], rd, opcode]
How to encode a RISCV instruction into binary
Given a RISCV assembly code to read and determine the final result
Understand the number of pipeline stalls due to RAW dependencies when we have pipeline latches versus pipeline registers
understanding data forwarding, how to detect it, also which RAW case data forwarding doesn't handle

## Slide 33
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech