## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
Precise exceptions
Caches

## Slide 4
Exceptions
What is exception?
  Unusual or unexpected program event.
  A system service is takes action to handle the event
System exception handler
User program
Notes: Instr window = range of instructions to search

## Slide 5
S/W Exceptions
Software exceptions are user-level unusual events
  Defined by the programing language
SW exception handler
User program
Notes: Instr window = range of instructions to search

## Slide 6
S/W Exceptions
Software exceptions triggers
  Hardware: try { z = y / x; } catch
  Software: if (x == 0) => throw
Exception handler
User program
Notes: Instr window = range of instructions to search

## Slide 7
Interrupts vs Exceptions
Interrupts
  Cased by external events
    e.g. network, keyboard, timer
  Asynchronous to program execution
  May be handled between instructions
  Simply suspend and resume user program
Notes: Instr window = range of instructions to search

## Slide 8
Interrupts vs Exceptions
Exceptions
  Caused by internal events
  Synchronous to program execution
  Condition must be remedied by the handler
  Program may resume or abort
Notes: Instr window = range of instructions to search

## Slide 9
Question
Which RISC-V instructions can execute without exceptions?
Notes: Instr window = range of instructions to search

## Slide 10
Types of Exceptions
Arithmetic
  Overflow, undeflow
  Division by zero
Faults
  Page fault
  Invalid opcode
Errors
  Parity
Traps
  Breakpoint
Notes: Instr window = range of instructions to search

## Slide 11
Precise Exceptions
What supporting precise exceptions entails?
  All previous instructions have been executed.
  All following instructions have not been modified the process state
  The faulting instruction may or may not have been executed, depending on the definition of the architecture and the cause of the exception.
Notes: Instr window = range of instructions to search

## Slide 12
Exceptions in in-order pipeline
Reg
ALU
DMem
Ifetch
Reg
Div
Div
Load
Load
Load
Div
Load
Load
Exception
Notes: Instr window = range of instructions to search

## Slide 13
Exceptions in out-of-order pipeline
What happens if a speculatively executed instruction faults?
A
B
C
D
E
A, B Commit
Divide by Zero!
Outside world sees: A, B, fault!
Should have been: A, B, C, D, fault!
A
B
C
D
E
Divide by Zero!
Branch mispred
W
X
Fault should never be seen!
Notes: Instr window = range of instructions to search

## Slide 14
Solution: handle faults like other results
ROB commits instructions to register file when
  It is oldest for in-order state update
  It is known to be non-speculative
Do the same with faults!
  At exec, make note of any faults, but don’t expose to outside world
  If the instruction gets to commit, then expose the fault

## Slide 15
Example
Fault deferred until architecturally correct point.
Other fault “never happened”!
A
B
C
D
E
LOAD R6 = 0[R7]
LOAD
P1
LOAD R1 = 0[R2]
ADD R3 = R1 + R4
SUB R1 = R5 – R6
DIV R4 = R7 / R1
ADD
P2
SUB
P3
DIV
P4
LOAD
P5
imm
P1
R5
R7
imm
R2
R4
R6
P3
R7
E
C
F
X
X
X
X
X
Miss
X
X
Fault!
X
X
Divide by zero
Resolved
X
X
(commit)
X
(3 commits)
Now raise fault
Flush rest of ROB,
Start fetching
Fault handler
Notes: E => execute
C => complete
F => faulted

## Slide 16
Caches

## Slide 17
Memory Latency is Long
60-100ns is common
What this really means for the CPU in term of clock cycles?
  Assume 2 GHz CPU
  Clock cycle time? = 0.5ns
  100ns memory  200 cycle memory latency!

## Slide 18
Memory Latency is Long
Why is accessing memory slow?
  Storage technology
    (DRAM) is slower (row buffer refreshes, DRAM cells) than SRAM
  Physical distance
    Usually outside the core, sharing of the memory by multiple cores and peripherals (hard-drive)
  Bus bandwidth
    Growing number of cores saturate the memory bus

## Slide 19
Memory Latency is Long
Solution: hardware caches

## Slide 20
Today’s caches occupy a large die area
Intel Sandy Bridge (2011) - 6x L1-D: 64 KB - 6x L1-I: 64 KB
- 6x L2: 256 KB - 1x L3: 20,480 KB (20 MB)

## Slide 21
Storage Hierarchy and Locality
Register File
ICache
DCache
L2 Cache
L3 Cache
Main Memory
Disk
Row buffer
SRAM Cache
Capacity +
Speed -
Speed +
Capacity -
ITLB
DTLB
Scratchpad

## Slide 22
Data Locality
Temporal Locality
  If data item needed now, it is likely to be needed again in near future
  Spatial Locality
  If data item needed now, nearby data likely to be needed in near future

## Slide 23
Locality with caches
Exploiting Temporal locality
  Keep recently used data in fast memory close to the processor
  Hierarchy
  Replacement policies
  Exploiting spatial locality
  Also bring nearby data close
  Block size
  Cache size

## Slide 24
Review Questions
Memory addresses A, A+1, A+2, A+3, A+4
  Spatial locality or temporal locality?
  Spatial
Memory addresses A,B,C,A,B,C,A,B,C
  Spatial locality or temporal locality?
  Temporal

## Slide 25
Locality and caches
Solution: hardware caches

## Slide 26
Cache Basics
Fast (but small) memory close to processor
When data referenced
  If in cache, use cache instead of memory
  If not in cache, bring into cache (actually, bring entire block of data, too)
  Maybe have to kick something else out to do it!
Key: Optimize the
average memory
access latency

## Slide 27
Cache Basics
Important decisions
  Placement: where in the cache can a block go?
  Identification: how do we find a block in cache?
  Replacement: what to kick out to make room in cache?
  Write policy: what do we do about stores?

## Slide 28
Cache Basics
Cache consists of block-sized lines
  Line size typically power of two
    Why?
  Typically 16 to 128 bytes in size
    Why?
MSB
LSB
Block size
Notes: Power of two => addressing efficiency, memory alignment
Block size=> memory transfer efficiency, miss penalty, memory architecture

## Slide 29
Cache Basics
Example
  Suppose cache block size is 128 bytes
  Read data at address A=0x7fffa3f4
  What is the block base address?
  Answer: 0x7fffa380

## Slide 30
Cache Basics
Example
  Suppose cache block size is 64 bytes
  Lowest 6 bits determine offset within block
  What do we use the offset for?
  Answer: Access to CPU data (e.g. 4 bytes - 32-bit)

## Slide 31
Cache Placement
Placement
  Where to place a memory block in cache lines?
Placement Policies
  Direct mapped (block can go to only one line)
    Index the cache using memory address
  Fully Associative (block can go to any line)
    Lookup the cache using tag
  Set-associative (block can go to one of N lines)
    Mixing indexing and lookup

## Slide 32
Cache Placement
Direct Mapped
  Fast access (indexing)
    block A can only be stored in one location
    No search
  Has block conflicts

## Slide 33
Cache Placement
Fully Associative
  Slow access (lookup)
    Compare address with each tag
    Block A can be stored in any cache line
    Expensive search
  No block conflicts

## Slide 34
Cache Placement
Set Associative
  Average access (indexing + lookup)
  Compare address with N tags
  Block A can be stored in exactly one set but in any cache line in the set
  Less block conflicts

## Slide 35
Cache Identification
When address referenced, need to
  Find whether its data is in the cache
  If it is, find where in the cache
  This is called a cache lookup
Each cache line must have
  A valid bit (1 if line has data, 0 if line empty)
    We also say the cache line is valid or invalid
  A tag to identify which block is in the line (if line is valid)

## Slide 36
Cache Address
Offset: Byte offset in block
Index: Which set in the cache is the block located
Tag: Need to match address tag in cache
Set: Group of blocks corresponding to same index
MSB
LSB
Offset
Index
TAG
Data
address

## Slide 37
Cache Indexing
dex
Index
TAG
Block offset
DATA1
TAG0
TAG2
=
=
HIT
YES
YES
Data
Logic
DATA0

## Slide 38
Tag Array
Any information related to cache other than data is stored in the tag storage.
Necessary: valid bit, tag bits
Also: dirty bits, replacement info, coherence info, atomic info, etc..

## Slide 39
Parallel/Serial TAG and Data Array Access

## Slide 40
Exercice
Here is a series of address references given as word address: 1,4,8,5,20,17,19,56,9,11,4,43,5,6,9,17. Assuming a direct-mapped cache with 16 one-word blocks that is initially empty, label each reference in the list as a hit or miss and show the final contents of the cache.
1%16 =1
4%16 = 4
8%16 =8
5%16 =5
20%16 = 4
17%16 = 1
19%16 =3
56%16 = 8
9%16 =9
11%16 =11
4%16 = 4
43 % 16 = 11
5%16 = 5 Hit
6%16 = 6
9%16 = 9 Hit
17%16 =1 Hit
0 | 
1 | 1 17
2 | 
3 | 19
4 | 4 20 4
5 | 5
6 | 6
7 | 
8 | 8 56
9 | 9
10 | 
11 | 11 43
12 | 
13 | 
14 | 
15 | 

## Slide 41
Cache Replacement
Need a free line to insert new block
  Which block should we kick out?
Several strategies
  Random (randomly selected line)
  FIFO (line that has been in cache the longest)
  LRU (least recently used line)
  LRU Approximations (Pseudo LRU)
Notes: Pseudo LRU use a binary tree as optimization

## Slide 42
Cache Replacement
Random Replacement
  We care about speed!
  Use a global incrementing counter
  On replacement, use counter current value

## Slide 43
Cache Replacement
LRU Replacement
  Have LRU counter for each line in a set
  When line accessed
    Get old value X of its counter
    Set its counter to max value
    For every other line in the set
      If counter larger than X, decrement it
  When replacement needed
    Select line whose counter is 0

## Slide 44
Write Policy
Do we allocate cache lines on a write miss?
  Write-allocate
    A write miss brings block into cache
  No-write-allocate
    A write miss leaves cache as it was
  Pros and cons?
    Depends on temporal locality

## Slide 45
Write Policy
Do we update memory on writes?
  Write-through
    Memory immediately updated on each write
    Generally combined with no-write-allocate
  Write-back
    Memory updated when line replaced
    Generally combined with write-allocate

## Slide 46
Write Policy
Do we update memory on writes?
  Write-through
    Memory immediately updated on each write
    Generally combined with no-write-allocate
  Write-back
    Memory updated when line replaced
    Generally combined with write-allocate

## Slide 47
Write through / Write back
PROC
CACHE
MEM
PROC
CACHE
MEM
  Write-through
  Write-back
replacement

## Slide 48
Writeback Caches
Need a Dirty bit for each line (stored in the Tag!)
  A dirty line has more recent data than memory
Need dirty bytes storage as well (optional)
Line starts as clean (not dirty)
Line becomes dirty on first write to it
  Memory not updated yet, cache has the only up-to-date copy of data for a dirty line
Replacing a dirty line
  Must write data back to memory (write-back)

## Slide 49
Cache Performance
Miss rate
  Fraction of memory accesses that miss in cache
  Hit rate = 1 – miss rate
Miss penalty ~ cache access + memory latency
Average memory access time
  AMAT = hit latency + miss rate * miss penalty
CPU runtime latency
CPUtime = CycleTime x (CyclesExec + CyclesMemoryStall)
CyclesMemoryStall = CacheMisses x (MissLatencyTotal – MissLatencyOverlapped)

## Slide 50
Improving Cache Performance
AMAT = hit time + miss rate * miss penalty
  Reduce miss penalty
  Reduce miss rate
  Reduce hit time

## Slide 51
Improving Cache Performance
CyclesMemoryStall = CacheMisses x (MissLatencyTotal – MissLatencyOverlapped)
  Increase overlapped miss latency
  Increase memory level parallelism

## Slide 52
Improving Cache Performance
Memory latency = 100 cycles
16KB cache, 3 cycle latency, 85% hit rate
What’s the baseline AMAT?
= 3+100*0.15 = 18 cycles
What’s the best way to reduce latency?
  Smaller 8KB cache: 1 cycle latency, 75% hit rate
  = 1+ 100*0.25 = 26 cycles
  Larger 32KB cache: 4 cycle latency, 90% hit rate
  = 4 + 100*0.1 = 14 cycles

## Slide 53
Hiding Miss latency
Idea: overlap miss latency with useful work
  Also called “latency hiding”
Non-blocking (Lockup-free) caches
  A blocking cache services one access at a time
    While miss serviced, other accesses blocked (wait)
  Non-blocking caches remove this limitation
    While miss serviced, can process other requests
Prefetching
  Predict what will be needed and get it ahead of time

## Slide 54
Q&A

## Slide 55
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech