## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
Caches

## Slide 4
Exercise: let’s design a cache
We need a cache for a 32-bit RISC-V CPU
Our load/store unit can only fetch word-aligned block
How many bits is the address bus?
Answer: 32-log2(4) = 30 bits

## Slide 5
Exercise: let’s design a cache
We can only afford 512 bytes of cache storage and our memory bus is 64 bytes
How many total blocks can we host inside our cache?
Answer: 512 / 64 = 8 blocks or 8 cache lines

## Slide 6
Exercise: let’s design a cache
Assume direct mapped placement
Describe the cache address bits mapping?
  [ tag | index | offset ]
Answer
  offset = 64 / 4 = 16 words => 4 bits
  Index = 8 / 1 = 8 => 3 bits
  Tag = 30 – 4 – 3 = 23 bits
7
6
5
4
3
2
1
0
8 sets of 1 way each

## Slide 7
Exercise: let’s design a cache
Assume 2-way set associative placement
Describe the cache address bits mapping?
  [ tag | index | offset ]
Answer
  offset = 64 / 4 = 16 words => 4 bits
  Index = 8 / 2 = 4 => 2 bits
  Tag = 30 – 4 – 2 = 24 bits
0
1
4 sets of 2 ways each
2
3
4
5
6
7

## Slide 8
Exercise: let’s design a cache
Assume fully associative placement
Describe the cache address bits mapping?
  [ tag | index | offset ]
Answer
  offset = 64 / 4 = 16 words => 4 bits
  Index = 8 / 8 = 1 => 0 bits
  Tag = 30 – 4 – 0 = 26 bits
0
1
1 set of 8 ways each
2
3
4
5
6
7

## Slide 9
Exercise
Assume direct-mapped cache with 8 blocks that is initially empty
Here is a series of address references given as block address (offset removed): 1,4,2,5,12,4,1,5.
Label each reference in the list as a hit and show the final contents of the cache.
1%8 =1
4%8 = 4
2%8 = 2
5%8 = 5
12%8 = 4
4%8 = 4
1%8 = 1
5%8 = 5
0 | 
1 | 1,1
2 | 2
3 | 
4 | 4,12,4
5 | 5,5
6 | 
7 | 
0 | 
1 | 1
2 | 2
3 | 
4 | 4
5 | 5
6 | 
7 | 

## Slide 10
Exercise
Assume 2-way set associative cache with 8 blocks and LRU replacement that is initially empty
Here is a series of address references given as block address (offset removed): 1,4,2,5,12,4,1,5.
Label each reference in the list as a hit and show the final contents of the cache.
1%4 =1
4%4 = 0
2%4 = 2
5%4 = 1
12%4 = 0
4%4 = 0
1%4 = 1
5%4 = 1
0 | 4,4 | 12
1 | 1,1 | 5,5
2 | 2 | 
3 |  | 
0 | 4 | 12
1 | 1 | 5
2 | 2 | 
3 |  | 

## Slide 11
Review: Cache Indexing
dex
offset
Index
TAG
DATA1
TAG0
TAG2
=
=
HIT
YES
YES
Data
Logic
DATA0
2 Ways set associative

## Slide 12
Parallel TAG and Data Array Access Pipeline
Four pipeline stages
Tag & Data parallel access
Need a way multiplexer
  Fetch ways lines from data array
  Since we don’t have the way index yet from tag compare
Two critical paths
  Tag access + compare + mux
  Data access + mux

## Slide 13
Serial TAG and Data Array Access Pipeline
Five pipeline stages
  One extra cycle
Tag & Data serial access
No way multiplexer
  We have the way index
  We can select our data line
One smaller critical path
  Tag access + compare

## Slide 14
Cache Replacement
Need a free line to insert new block
  Which block should we kick out?
Several strategies
  Random (randomly selected line)
  FIFO (line that has been in cache the longest)
  LRU (least recently used line)
  LRU Approximations (Pseudo LRU)
Notes: Pseudo LRU use a binary tree as optimization

## Slide 15
Cache Replacement
Random Replacement
  Use per-set counter
  Increment on set access
  On replacement, use counter current value
Pros: efficient
Cons: bad approximation

## Slide 16
Cache Replacement
LRU Replacement
  Have LRU counter for each line in a set
  When line accessed
    Set its counter to max value
    Saturate-decrement other lines counters
  When replacement needed
    Select line whose counter is 0
Pros: expensive
Cons: good approximation

## Slide 17
Cache Replacement
Example: 4 lines cache
  Initial state: 0,0,0,0
  Fill line0: 3,0,0,0 (LRU=1)
  Fill line1: 2,3,0,0 (LRU=2)
  Hit line0: 3,2,0,0 (LRU=2)
  Fill line2: 2,1,3,0 (LRU=3)
  Fill line3: 1,0,2,3 (LRU=1)
  Fill line1: 0,3,1,2 (replaced line1)
  Fill line0: 3,2,0,1 (replaced line0)

## Slide 18
Cache Replacement
Tree-based Pseudo-LRU Replacement
  Use binary tree to locate your cache line
    0=> left, 1=>right
  On access construct the MRU path
  Save MRU path into a per-set register
    On replacement LRU=~MRU
Pros: efficient
Cons: weak approximation
Line | Encoding bits
Line0 | _00
Line1 | _10
Line2 | 0_1
Line3 | 1_1
‘_’ means unchanged

## Slide 19
Cache Replacement
Assume 4-way set associative cache
  Need 3 bits to address each block
  MRU initially set to 000
Line | Encoding bits
Line0 | _00
Line1 | _10
Line2 | 0_1
Line3 | 1_1
Accesses: line2 -> line1 -> line3 -> line0 -> line2
MRU register: 001 -> 010 -> 111 -> 100 -> 001
PLRU = ~001 = 110 => line1
‘_’ means unchanged

## Slide 20
Write Policy
Do we allocate cache lines on a write miss?
  Write-allocate
    A write miss brings block into cache
  No-write-allocate
    A write miss leaves cache as it was
  Pros and cons?
    Depends on temporal locality

## Slide 21
Write Policy
Do we update memory on writes?
  Write-through
    Memory immediately updated on each write
    Generally combined with no-write-allocate
  Write-back
    Memory updated when line is replaced
    Generally combined with write-allocate

## Slide 22
Write through / Write back
PROC
CACHE
MEM
PROC
CACHE
MEM
  Write-through
  Write-back
replacement

## Slide 23
Writeback Caches
Need a Dirty bit for each line (stored in the Tag!)
  A dirty line has more recent data than memory
Need dirty bytes storage as well (optional)
Line starts as clean (not dirty)
Line becomes dirty on first write to it
  Memory not updated yet, cache has the only up-to-date copy of data for a dirty line
Replacing a dirty line
  Must write data back to memory (write-back)

## Slide 24
Types of Cache Misses
The “3 Cs”
  Compulsory: have to have these
    Miss the first time each block is accessed
  Capacity: due to limited cache capacity
    Would not have them if cache size was infinite
  Conflict: due to limited associativity
    Would not have them if cache was fully associative
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 25
Cache Performance
Miss rate
  Fraction of memory accesses that miss in cache
  Hit rate = 1 – miss rate
Miss penalty ~ cache access + memory latency
Average memory access time
  AMAT = hit_latency + miss_rate * miss_penalty

## Slide 26
Cache Performance
Another CPU runtime latency model
CPUTime = CycleTime x (CyclesExec + CyclesMemoryStall)
CyclesMemoryStall = CacheMisses x (MissLatencyTotal – MissLatencyOverlapped)
Overlapped miss latency: duration of memory access time while processor is doing other work

## Slide 27
Improving Cache Performance
Improving Average Memory Access Time
AMAT = hit_time + miss_rate * miss_penalty
  Reduce miss penalty
  Reduce miss rate
  Reduce hit time

## Slide 28
Improving Cache Performance
Improving memory stall cycles
CyclesMemoryStall = CacheMisses x (MissLatencyTotal – MissLatencyOverlapped)
  Increase overlapped miss latency
  Increase memory level parallelism (MLP)
Notes: Increase overlapped miss latency
- Need a non-blocking cache
- Schedule more instructions while waiting on memory (OOO)
Memory level parallelism => handling multiple memory requests in parallel
Banking
MHSR

## Slide 29
Improving Cache Performance
Memory latency = 100 cycles
16KB cache, 3 cycle latency, 85% hit rate
What’s the baseline AMAT?
= 3+100*0.15 = 18 cycles
Which cache configuration reduces latency?
  Smaller 8KB cache: 1 cycle latency, 75% hit rate
  = 1+ 100*0.25 = 26 cycles
  Larger 32KB cache: 4 cycle latency, 90% hit rate
  = 4 + 100*0.1 = 14 cycles

## Slide 30
Hiding Miss latency
Idea: overlap miss latency with useful work
  Also called “latency hiding”
Non-blocking (Lockup-free) caches
  A blocking cache services one access at a time
    While miss serviced, other accesses blocked (wait)
  Non-blocking caches remove this limitation
    While miss serviced, can process other requests
Prefetching
  Predict what will be needed and get it ahead of time

## Slide 31
Non-Blocking (Lockup-Free) Caches
Hit Under Miss
  Allow cache hits while one miss in progress
  But another miss has to wait
Miss Under Miss, Hit Under Multiple Misses
  Allow hits and misses when other misses in progress
  Memory system must allow multiple pending requests
  MSHR (Miss Status Holding Register): Stores missed cache requests that are pending for memory.

## Slide 32
MSHR
Track address, data, and status for outstanding cache misses
Provide correct memory ordering, other information (e.g, cache coherence)
Can be shared by multiple caches
Has fixed capacity: isfull check
CPU Pipeline
DCache
MSHR
Memory

## Slide 33
Reducing Cache Miss Penalty
Multilevel caches
  Very Fast, small Level 1 (L1) cache
  Fast, not so small Level 2 (L2) cache
  May also have slower, large L3 cache, etc.
Why does this help?
  Miss in L1 cache can hit in L2 cache, etc.
    AMAT = HitTimeL1+MissRateL1 x MissPenaltyL1
    MissPenaltyL1= HitTimeL2+MissRateL2x MissPenaltyL2
    MissPenaltyL2= HitTimeL3+MissRateL3x MissPenaltyL3

## Slide 34
Reducing Cache Miss Penalty
Handling memory overlap with multi-level caches
  Inclusion Property
    If block A is in L1 cache, it must also be in L2 cache
    Simpler data management (fill/eviction)
  Exclusion Property
    If block is in L1 cache, it is not in L2 cache
    Higher total capacity => improved hit rate
    Complex data management (fill/eviction)

## Slide 35
Reducing Cache Miss Penalty
Exercise: Which is better?
  Memory latency = 100 cycles
  Single cache
    16KB L1 cache, 3 cycle latency, 85% hit rate
  Two-level of caching
    Smaller 8KB cache: 1 cycle latency, 75% hit rate
    Larger 128KB cache: 6 cycle latency, 60% hit rate

## Slide 36
Reducing Cache Miss Penalty
Prioritizing memory transactions
  Block transfer can take time if bus too narrow
  Give data to loads before entire block arrive
Early restart
  When needed word arrives, let processor use it
  Then continue block transfer to fill cache line
Critical Word First
  Transfer loaded word first, then the rest of block
    Why this can be expensive?
  Use with early restart to let processor go ASAP
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 37
Reducing Cache Miss Penalty
Prioritize load misses
  Loads can have dependent instructions
  If a load misses and a store needs to go to memory, let the load miss go first
  Need a write buffer to hold stores
Merge write requests
  If multiple write misses to the same block, combine them in the write buffer
  Use block-write instead of a many small writes
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 38
Reducing Cache Miss Rate
Victim Caches
  Recently evicted blocks are kept in small cache
  If we miss on those blocks, can get them fast
  Why does it work?
    Exploit conflict misses
  Example:
    A 64KB direct-mapped L1 cache combined with a 1KB fully associative victim cache
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 39
Reducing Cache Miss Rate
Larger blocks
  Helps if there is more spatial locality
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 40
Reducing Cache Miss Rate
Larger caches
  Fewer capacity misses,
  But longer hit latency!
Higher associativity
  Fewer conflict misses
  But longer hit latency!
Which is better?
  Need to work through AMAT equations to figure out which is better
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 41
Reducing Cache Miss Rate
Pseudo Associative Caches
  Similar to way prediction
  Start with direct mapped indexing
  If miss on “primary” entry, try another entry
  Use hash function to determine other indices to check
  Results in varying access
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 42
Reducing Cache Miss Rate
Compiler optimizations
  Loop interchange
  Blocking (e.g., tiled matrix multiplication)
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 43
Reducing Cache Miss Rate
For loops over multi-dimensional arrays
  Example: matrices (2-dim arrays)
Change order of iteration to match layout
  Gets better spatial locality
  Layout in C: last index changes first
for(j=0;j<10000;j++) for(i=0;i<40000;i++) c[i][j]=a[i][j]+b[i][j];
for(i=0;i<40000;i++) for(j=0;j<10000;j++) c[i][j]=a[i][j]+b[i][j];
a[i][j] and a[i+1][j] are 10000 elements apart
a[i][j] and a[i][j+1] are next to each other
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 44
Reducing Cache Miss Rate
Reduce the working set size.
To make the code fit into the cache
Example
1D case
for (k = 0; k < N; k++)
  for (j=0; j<M; j++)
  if (B[j] == a[k]) sum[k]++;
  If one element in B is 4B and the total cache size is 1KB.
  1KB/4B = 256 elements; So
  for (j=0; j<M/256; j++)
  for (k = 0; k < N; k++)
  for (l = 0; l< 256; l++)
  if (B[j*256+l] == a[k]) sum[k]++;
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 45
Other software Optimization for caches
Data alignment
increase spatial locality in cache block
aligned_malloc(addr, alignment);
Use Hint bits:
Indicate temporal locality
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 46
Reducing Hit Time
Small & Simple Caches are faster
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 47
Reducing Hit Time
Pipelined Caches
  Improves bandwidth, but not latency
  Essential for L1 caches at high frequency
    Even small caches have 2-3 cycle latency at N GHz
Multi-banked caches
  Increases bandwidth and MLP
Trace Caches
  For instruction caches
Way Prediction
  Speeds up set-associative caches
  Predict which of N ways has our data, fast access as direct-mapped cache
  If mispredicted, access again as set-assoc cache
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 48
Q&A

## Slide 49
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech