## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
Caches

## Slide 4
Improving Cache Performance
Improving Average Memory Access Time
AMAT = hit_time + miss_rate * miss_penalty
  Reduce miss penalty
  Reduce miss rate
  Reduce hit time

## Slide 5
MSHR
Track address, data, and status for outstanding cache misses
Provide correct memory ordering, other information (e.g, cache coherence)
Can be shared by multiple caches
Has fixed capacity: isfull check
CPU Pipeline
DCache
MSHR
Memory

## Slide 6
Reducing Cache Miss Penalty
Multilevel caches
  Very Fast, small Level 1 (L1) cache
  Fast, not so small Level 2 (L2) cache
  May also have slower, large L3 cache, etc.
Why does this help?
  Miss in L1 cache can hit in L2 cache, etc.
    AMAT = HitTimeL1+MissRateL1 x MissPenaltyL1
    MissPenaltyL1= HitTimeL2+MissRateL2x MissPenaltyL2
    MissPenaltyL2= HitTimeL3+MissRateL3x MissPenaltyL3

## Slide 7
Reducing Cache Miss Penalty
Handling memory overlap with multi-level caches
  Inclusion Property
    If block A is in L1 cache, it must also be in L2 cache
    Simpler data management (fill/eviction)
  Exclusion Property
    If block is in L1 cache, it is not in L2 cache
    Higher total capacity => improved hit rate
    Complex data management (fill/eviction)

## Slide 8
Reducing Cache Miss Penalty
Exercise: Which is better?
  Memory latency = 100 cycles
  Single cache
    16KB L1 cache, 3 cycle latency, 85% hit rate
  Two-level of caching
    Smaller 8KB cache: 1 cycle latency, 75% hit rate
    Larger 128KB cache: 6 cycle latency, 60% hit rate

## Slide 9
Reducing Cache Miss Penalty
Prioritizing memory transactions
  Block transfer can take time if bus too narrow
  Give data to loads before entire block arrive
Early restart
  When needed word arrives, let processor use it
  Then continue block transfer to fill cache line
Critical Word First
  Transfer loaded word first, then the rest of block
    Why this can be expensive?
  Use with early restart to let processor go ASAP
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 10
Reducing Cache Miss Penalty
Prioritize load misses
  Loads can have dependent instructions
  If a load misses and a store needs to go to memory, let the load miss go first
  Use a write buffer to hold stores
Merge write requests
  If multiple write misses to the same block, combine them in the write buffer
  Use block-write instead of a many small writes
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 11
Reducing Cache Miss Rate
Victim Caches
  Recently evicted blocks are kept in small cache
  If we miss on those blocks, can get them fast
  Why does it work?
    Exploit conflict misses
  Example:
    A 64KB direct-mapped L1 cache combined with a 1KB fully associative victim cache
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 12
Reducing Cache Miss Rate
Larger blocks
  Helps if there is more spatial locality
Cache size
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 13
Reducing Cache Miss Rate
Larger capacity caches
  Fewer capacity misses
  But longer hit latency!
Higher associativity
  Fewer conflict misses
  But longer hit latency!
Which is better?
  Need to work through AMAT equations to figure out
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 14
Reducing Cache Miss Rate
Pseudo Associative Caches
  Similar to way prediction
  Start with direct mapped indexing
  If miss on “primary” entry, try another entry
  Use hash function to determine other indices to check
  Results in varying access
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 15
Reducing Cache Miss Rate
Compiler optimizations
  Loop interchange
  Blocking (e.g., tiled matrix multiplication)
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 16
Loop Interchange Optimization
For loops over multi-dimensional arrays
  Example: matrices (2-dim arrays)
Change order of iteration to match layout
  Gets better spatial locality
  Layout in C: last index changes first
for(j=0;j<10000;j++) for(i=0;i<40000;i++) c[i][j]=a[i][j]+b[i][j];
for(i=0;i<40000;i++) for(j=0;j<10000;j++) c[i][j]=a[i][j]+b[i][j];
a[i][j] and a[i+1][j] are 10000 elements apart
a[i][j] and a[i][j+1] are next to each other
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 17
Blocking Optimization
Reduce the working set size.
To make the code fit into the cache
Example: 1D case
for (k = 0; k < N; k++) for (j=0; j<M; j++) if (X[j] == Y[k]) sum[k]++;
If one element in X is 4B and the total cache size is 1KB. 1KB/4B = 256 elements;
  for (j=0; j<M/256; j++)
  for (k = 0; k < N; k++)
  for (i = 0; i< 256; i++)
  if (X[j*256+i] == Y[k]) sum[k]++;
Notes: - Increasing the reuse of X

## Slide 18
Other software Optimization for caches
Data alignment
    Increase spatial locality in cache block
    aligned_malloc(addr, alignment);
Use Hint bits
    Indicate temporal locality
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 19
Small & Simple Caches are faster
What could be affecting access time?
Reducing Hit Time
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 20
Reducing Hit Time
Pipelined Caches
  Improves bandwidth, but not latency
  Essential for L1 caches at high frequency
    Even small caches have 2-3 cycle latency at N GHz
Multi-banked caches
  Increases bandwidth and MLP
Trace Caches
  Storing fetched and decoded instructions.
Way Prediction
  Speeds up set-associative caches
  Predict which of N ways has our data, fast access as direct-mapped cache
  If mispredicted, access again as set-associative cache
Notes: - Applicable to
- Critical word first will reorder the transfer

## Slide 21
Virtual Memory

## Slide 22
Running Multiple Programs
Early machines only run one program with unrestricted access to memory.
Program memory layout contained
  code, data, heap, stack, etc..
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Stack
Dynamic
Data
Static Data
Program
STACK_BASE_ADDR
I/O
__global_pointer
TLS Data

## Slide 23
Running Multiple Programs
Modern systems need to run multiple applications concurrently.
  User apps and OS
How do we run different programs in isolation on the same CPU?
  Storing in different location
  Enforcing memory security
Main Memory
Program 1
Program 2
Program 3
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23

## Slide 24
Running Multiple Programs
How do we run different programs in isolation on the same CPU?
  Each program address layout
    code, data, heap, stack, etc..
  Portion of the memory is shared (e.g. libraries)
  Portion of the memory is reserved for OS services
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Main Memory
Program 1
Program 2
Program 3

## Slide 25
Sharing memory between applications
Static Partitioning
  Features
    Protection
      Applications shouldn’t be able to access other user memory
      Use bound checking
    Location-independence
      Applications can be allocated anywhere in memory
      Use base pointer
Main Memory
Program 1
Program 2
Program 3

## Slide 26
Sharing memory between applications
Static Partitioning address translation
  PhysicalAddr = BaseReg + LogicalAddr
  Bound check before translation!
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Bound Reg.
Bounds Violation?
Physical Memory
Program X
Base Reg.
+
Physical Address
Logical Address
Base Physical Address
≥
(from CPU)

## Slide 27
Sharing memory between applications
Static Partitioning Limitations
  Not able to share libraries
  What if pre-allocated program needs more space?
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Main Memory
Library
Program 1
Program 2
OS

## Slide 28
Sharing memory between applications
Dynamic Partitioning (Virtual Memory)
  Divide memory into fixed-size blocks called pages
  Assign pages to each program as needed
  Pages can be scattered in memory
  Each page is typically 4 KB
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
0
1
2
3
0
1
2
3
0
1
2
3
Program A
Program B
Program C
1
0
1
3
3
2
0
0
2
2
3
1
Operating
System
Pages
Main Memory

## Slide 29
Virtual Memory
How we track pages mapping?
  We use a page table
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
1
0
1
3
3
2
0
0
2
2
3
1
Operating
System
Pages
Main Memory
0
1
2
3
p0
p1
p2
p3
0
1
2
3

## Slide 30
Virtual Memory
Virtual to physical address translation
  Each program sees a uniform virtual address space
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Reserv. | 
Code | 
Data | 
Heap | 
Stack | 
Program A
Virtual Space
Reserv. | 
Code | 
Data | 
Heap | 
Stack | 
Program B Virtual Space
232
v0
v1
p0
p1
Physical Memory

## Slide 31
Virtual Address Translation
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
virtual page number (VPN) page offset
virtual address
p p–1
physical page number (PPN) page offset
physical address
0
address translation
p p–1
m–1
n–1
0
2n: virtual address size
2m: physical address size
2p: page size

## Slide 32
Virtual and Physical Memory
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
System:
  Virtual memory size: 4 GB = 232 bytes
  Physical memory size: 256 MB = 228 bytes
  Page size: 4 KB = 212 bytes
Organization:
  Virtual address: 32 bits
  Physical address: 28 bits
  Page offset: 12 bits
  # Virtual pages = 232/212 = 220 (VPN = 20 bits)
  # Physical pages = 228/212 = 216 (PPN = 16 bits)

## Slide 33
Page Table
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
virtual page number (VPN) page offset
physical page number (PPN)
VPN acts as table index
p p–1
n–1
0
m–1
p p–1
0
physical page number (PPN)
physical address
page offset
page table base register (per process)

## Slide 34
Page Table
Page table base register
  Physical base address of the page table in memory (per process)
  Effective method for swapping to another process memory
  Set by memory management unit (MMU) during context switch
  On RISC-V, this is done via satp CSRs
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23

## Slide 35
Page Table
What is store in the page table
  Physical address mapping
  Flags
    Valid bit
    Accessed bit
    Dirty bit
    Permission bits (R/W/E)
    Protection bits (User/Supervisor)
    etc…
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Flags Physical page number (PPN)

## Slide 36
Page Table
Where is the page table stored?
  In memory as well
  Each memory access is two transactions:
    Accessing page table:
      PPN = Memory[base + VPN]
    Accessing the translated address
      Value = Memory[PPN + page_offset]
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23

## Slide 37
Page Table
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
How large is a page table?
  # Virtual pages = 232/212 = 220 (VPN = 20 bits)
  Each page table entry (PTE) size = PPN+flags ≃ 32 bits (4 bytes)
    220 x 32 = 4 MB for each application!
    Much larger for 64-bit address!
  Need to compress the table

## Slide 38
Hierarchical Page Table
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Store the page table as a page table
p1 | p2 | offset
Level 1 Page Table
p1
offset
p2
Base pointer
0
31 22 21 12 11
L1 index
L2 index
Physical Memory
Level 2 Page Tables
Virtual Address
Page Walk!

## Slide 39
Hierarchical Page Table
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Instead of one large table, we have a small p1-entries page directory and we allocate p2-entries table on demand
Total allocated table size:
  Given p1=10-bit, p2=10-bit
  Size = (1k * 4B) + 1k * (1k * 4B) > 4 MB
p1 | p2 | offset
31 22 21 12 11
L1 index
L2 index
Virtual Address

## Slide 40
Hierarchical Page Table
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Longer memory access transaction
Directory: base2 = Memory[base + p1]
Page Table: PPN = Memory[base2 + p2]
Translation: value =Memory[PPN + page_offset]
Expensive!
p1 | p2 | offset
31 22 21 12 11
L1 index
L2 index
Virtual Address

## Slide 41
Translation Lookaside Buffer (TLB)
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
CPU |  | 
 | Regs | 
D$
Main Memory
I$
L2, L3
MMU
TLB
Hit?
PT
Miss?
PA (to cache)
Store most recent translations into a cache (TLB)

## Slide 42
Translation Lookaside Buffer (TLB)
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Cache translations in TLB
  TLB hit ⇒ Single-Cycle Translation
  TLB miss ⇒ Page-Table Walk to refill
  TLB is flushed during context switch (avoidable with tagged PID)
VPN
offset
tag
PPN
physical address
PPN
offset
virtual address
hit?

## Slide 43
Translation Lookaside Buffer (TLB)
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
TLB Design
  32-128 entries fully associative
  256-512 entries are 4/8 way set associative
  Random or FIFO replacement policy
VPN
offset
tag
PPN
physical address
PPN
offset
virtual address
hit?

## Slide 44
Reducing Virtual Memory Access Time
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Memory addresses to L1 are virtual
  Hit time = tTLB + tL1cache
  Possible optimization?
VPN
offset
tag
PPN
physical address
PPN
offset
virtual address
hit?

## Slide 45
Reducing Virtual Memory Access Time
Nader Sehatbakhsh - ECE-M116C/CS-M151B - Fall 23
Virtually-Indexed Physically-Tagged Cache
Hit time = max(tTLB,tL1cache)
VPN
TLB
PPN
Page Offset
physical Cache (L1)
tag
data
=
cache hit?
TLB hit?
Index Offset

## Slide 46
Q&A

## Slide 47
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech