## Slide 1
UCLA Computer Science
Blaise Tine
CS-M151B
Computer Systems Architecture

## Slide 2: Attendance

## Slide 3
Agenda
High-Level-Synthesis
Roofline Model
Power

## Slide 4: High-Level Synthesis (HLS)
2
▸ What
Automated design process that transforms a high- level functional specification to optimized register-transfer level (RTL) descriptions for efficient hardware implementation
▸ Why
Productivity
  lower design complexity and faster simulation speed
Portability
  single source -> multiple implementations
Permutability
  rapid design space exploration -> higher quality of result (QoR)
©Zhiru Zhang (Cornell)

## Slide 5: High-Level Synthesis
Compiles High-Level code to RTL
  - input C/C++, output RTL
Lower HW entrance barrier
  Alleviates design costs
Source: FPGA HLS tutorial, ISCA 2015

## Slide 6: Typical C/C++ Synthesizable Subset
▸ Data types:
Primitive types: (u)char, (u)short , (u)int, (u)long, float, double
Arbitrary precision integer or fixed-point types
Composite types: array, struct, class
Templated types: template<>
Statically determinable pointers
▸ No support for dynamic memory allocations
▸ No support for recursive function calls
©Zhiru Zhang (Cornell)

## Slide 7: Hardware Specialization with HLS
▸ Data type specialization
arbitrary-precision fixed-point, custom floating-point
▸ Communication/interface specialization
streaming, memory-mapped I/O, etc.
▸ Memory specialization
array partitioning, data reuse, etc.
▸ Compute specialization
unrolling (ILP/DLP), pipelining (ILP/DLP/TLP), dataflow (TLP), multithreading (DLP/TLP)
4
ILP/DLP/TLP: Instruction-/Data-/Task-level parallelism
©Zhiru Zhang (Cornell)
Notes: ILP: concurrent instructions (ooo, superscalar)
DLP: concurrent memory accesses (SIMD)
TLP: concurrent tasks (multithreading)

## Slide 8: Typical C/C++ Constructs to RTL Mapping
Control flows
Scalars
Arrays
Memories
Wires or registers
Control logics



C Constructs |  | HW Components
Functions |  | Modules
Arguments |  | Input/output ports
Operators |  | Functional units
©Zhiru Zhang (Cornell)

## Slide 9: Function Hierarchy
▸ Each function is usually translated into an RTL module
– Functions may be inlined to dissolve their hierarchy
void A() { .. body A .. }
void C() { .. body C .. } void B() {
C();
}
void TOP( ) {
A(…);
B(…);
}
TOP
A
B
C
Source code
RTL hierarchy
©Zhiru Zhang (Cornell)

## Slide 10: Function Arguments
▸ Function arguments become ports on the RTL blocks
Additional control ports are added to the design
▸ Input/output (I/O) protocols
– Allow RTL blocks to automatically synchronize data exchange
TOP
out1
Datapath
FSM
in1 in2
in1_vld in2_vld
out1_vld
void TOP(int* in1, int* in2, int* out1)
{
*out1 = *in1 + *in2;
}
©Zhiru Zhang (Cornell)

## Slide 11: Expressions
char A, B, C, D, int P;
P = (A+B)*C+D
×
+
+
▸ HLS generates datapath circuits mostly from expressions
– Timing constraints influence the degree of registering
B
C
D
P
©Zhiru Zhang (Cornell)
A

## Slide 12: Arrays
▸ By default, an array in C code is typically implemented by a memory block in the RTL
– Read & write array -> RAM
- Constant array -> ROM
▸ An array can be partitioned and map to multiple RAMs
▸ Multiples arrays can be merged and map to one RAM
▸ An array can be partitioned into individual elements and map to registers
void TOP(int)
{
int A[N];
for (i = 0; i < N; i++) A[i+x] = A[i] + i;
}
N-1
N-2
…
1
0
TOP
RAM
DIN DOUT
ADDR
CE WE
A[N]
A_out
A_in
©Zhiru Zhang (Cornell)

## Slide 13: Loops
▸ By default, loops are rolled
Each loop iteration corresponds to a “sequence” of states
This state sequence will be repeated multiple times based on the loop trip count
void TOP (…) {
...
for (i = 0; i < N; i++) b += a[i];
}
TOP
S1
a[i]
b
+
LD
S2
©Zhiru Zhang (Cornell)

## Slide 14: HLS Design Flow
Scheduling: Determines which operations occur during each clock cycle based on
  Length of the clock cycle or clock frequency
  Time it takes for the operation to completes as defined by the target device
  User-specified optimization directives
Binding: Maps operations onto instantiated hardware
From: Towards automatic high-level code deployment on reconfigurable platforms: A survey of high-level synthesis tools and toolchains ,from : https://www.so-logic.net/documents/upload/Basic_HLS_Tutorial.pdf
Notes: CDFG =-> Control/data flow graph

## Slide 15: Design Steps
From: https://www.so-logic.net/documents/upload/Basic_HLS_Tutorial.pdf
https://github.com/Xilinx/HLx_Examples/blob/master/Math/squared_difference_accumulate/src/diff_sq_acc.cpp

## Slide 16: Vivado HLS Design Flow
Inputs:
  C function written in C/C++/SystemC, OpenCL API
  Constrains
  Directives (optional)
  C test bench
Outputs:
  RTL implementation files (verilog or VHDL)
  Report files
From: https://www.so-logic.net/documents/upload/Basic_HLS_Tutorial.pdf

## Slide 17: Vivado Optimizations

## Slide 18: Optimizing HLS Designs
Directives guide HLS optimizations
  Loop unrolling
  Loop pipelining
  Memory partitioning
  Resource allocation and implementation
~30 unique directives
  User can provide as much detail as desired
  Can achieve performance on order of handwritten RTL
Source: FPGA HLS tutorial, ISCA 2015

## Slide 19: Pragmas
From: vivado HLs Optimization methodology guide
Notes: + hls::allocation => limit number of instances of a function (area)
+ hls::clock => specify target clock
+ hls::reset => async | sync reset
+ hls::lartency =>min/max latency of a function in cycles
+ hls:;resource => specify which type of memory to use (e.g. sram|bram)
+ hls::expression_balance => specify a balance area/perf
+ hls::top =>specify top module + hls::function_instantiate => no sharing + hls::interface => specifies I/O ports + hls::protocol => handshake protocol + hls::dependence => hind for false loop dependencies + hls::loop_flatten => remove nested loops + hls::data_pack => packed vs aligned structs elements + hls::array_map => array to memory mapping (e.g. #banks) + hls::array_partition => break array into partitions + hls::array_reshape => change array layout

## Slide 20: Optimization-I : Loop Unrolling
By default, loops are rolled
  Each C loop iteration
    Implemented with same resources
    Implemented in the same state
    Use loop counter for iteration and resource access
void foo_top (…)
for(i=3;i>=0;i--)
b = a[i] + b;
Standard HLS
foo_top
+
a[N]
b
Source: FPGA HLS tutorial, ISCA 2015

## Slide 21: Optimization-I : Loop Unrolling
Exploits loop iteration parallelism
  Instantiate resources for simultaneous execution
  Respects iteration dependencies
foo_top
+
a[N]
b
Standard HLS
HLS & Unrolling
Takes 4 Cycles
Takes 1 Cycles
Source: FPGA HLS tutorial, ISCA 2015

## Slide 22: Optimization II: Loop pipelining
Latency = 3 cycles
Without Pipelining
Throughput = 3 cycles
RD
CMP
WR
RD
CMP
WR
With Pipelining
Latency = 3 cycles
Throughput = 1 cycle
RD
CMP
WR
RD
CMP
WR
Loop_tag : for( II = 1 ; II < 3 ; II++ ) {
op_Read;
op_Compute;
op_Write;
}
RD
CMP
WR
Loop Latency = 6 cycles
Loop Latency = 4 cycles
Source: FPGA HLS tutorial, ISCA 2015
Notes: Throughput ~= IPC base on one iteration of the loop

## Slide 23: Optimization III: Loop pipelining
Iteration Interval (II)
  Cycles loop must do before next iteration
II = 1 cannot always be implemented
  Port cannot be read at the same time
  Similar effect with other resource limitations
Source: FPGA HLS tutorial, ISCA 2015
Notes: Iteration interval

## Slide 24: Optimization IV: Array Partitioning
Split arrays to improve memory bandwidth
Source: FPGA HLS tutorial, ISCA 2015
Notes: Complete split use elements directly as registers Cyclic partitioning enables parallel access of consecutive entries block partitioning enables parallel access on seprate partitions

## Slide 25: Permutability: Faster Design Space Exploration
Latency Area Throughput
Untimed
Combinational
Sequential
Pipelined
+
+
+
out1
in1 in2 in3 in4
+
+
+
out1
in1 in2 in3 in4
clk add
t 3 *d
f1 = 1 / tclk
A1 = 3* Aadd
tclk  dadd  ds etup f2 1 / (3* tclk )
A2  Aadd
2 * Areg
tclk dadd + dsetup
f3 = 1/ tclk
A3 = 3* Aadd + 6* Areg
+
+
in
+
out
1 | 2 | 3 | 4
 | 1 | 2 | 3
 |  | 1 | 2
out1 = f (in1,in2,in3,in4)
+
out1
in1 in2 in3 in4
REG
Control-Data Flow Graph
3
©Zhiru Zhang (Cornell)

## Slide 26: Other HLS
From: Towards automatic high-level code deployment on reconfigurable platforms: A survey of high-level synthesis tools and toolchains

## Slide 27
Roofline

## Slide 28: Roofline Model
©Zhiru Zhang (Cornell)
Goal: Estimating the performance of your accelerator given its application domain.
How should your hardware be optimized to improve the performance of a given application?
Analogy: the 3’Cs of cache misses.
Application
Memory
Processing
Elements

## Slide 29: Roofline Model
©Zhiru Zhang (Cornell)
A simplified model of a processor
  Compute Bandwidth: ops / sec
  Memory Bandwidth: bytes / sec
A simplified model for a program
  Operations and data: ops / bytes
  Also known as Arithmetic Intensity (I)
Application
Memory
Processing
Elements

## Slide 30: Roofline Model
©Zhiru Zhang (Cornell)
System peak performance (P)
  Maximum computational performance the system can achieve
  Correlated to CPU fmax
  Example: P = 100 GFlops
Application
Memory
Processing
Elements
Notes: Log scale makes it easier to extrapolate performance along Moore’s Law (e.g. 2x scale)

## Slide 31: Roofline Model
©Zhiru Zhang (Cornell)
System memory bandwidth (B)
  Maximum memory (Rd/Wr) transfer speed the system can achieve
  Correlated to DRAM b/w
  Example: B= 25 GB/s
Application
Memory
Processing
Elements
Notes: Log scale makes it easier to extrapolate performance along Moore’s Law (e.g. 2x scale)

## Slide 32: Roofline Model
©Zhiru Zhang (Cornell)
Operational Intensity (I)
  Measure how many operations are performed foe each byte of data transferred from memory
  Ratio of the total number of operations to the total amount of data movement (operations per byte)
Application
Memory
Processing
Elements
Notes: Log scale makes it easier to extrapolate performance along Moore’s Law (e.g. 2x scale)

## Slide 33: Roofline Model
©Zhiru Zhang (Cornell)
Peak op/s
Attainable op/s
Memory Bandwidth byte/s
Operational Intensity (op/byte)
Attainable Performance
  The actual performance that can be achieved for a given workload
Attainable op/s = min(I * B, P)
Axis in log scale
Memory/compute-bound?
Attainable op/s
Memory-bound
Compute-bound
Notes: Log scale makes it easier to extrapolate performance along Moore’s Law (e.g. 2x scale)

## Slide 34: Roofline Model
©Zhiru Zhang (Cornell)
Consider 32-bit VMADD kernel
  Foreach(i): c[i] += a[i] * b[i]
  Operational Intensity=?

## Slide 35: Roofline Model
©Zhiru Zhang (Cornell)
32-bit VMADD kernel
  Foreach(i): c[i] += a[i] * b[i]
  2 flops (+, *) and 12 bytes (a, b, c)
  I = 2 flops / 12 bytes = 1/6 flop/b
Consider Machine
  P = 2 Gflop/s
  B = 10 Gbyte/s
Attainable Performance =?

## Slide 36: Roofline Model
©Zhiru Zhang (Cornell)
Peak op/s
Attainable op/s
Memory Bandwidth byte/s
Operational Intensity (op/byte)
Memory-bound
Compute-bound
Consider Machine
  P = 2 Gflop/s
  B = 10 Gbyte/s
  I = 1/6 flops/b
Attainable Performance
= min(I x B, P) = min(1.6, 2)
= 1.6 Gflop/s
Memory/compute bound?
What should we optimize?
1/6
2
1/2
1/4
1
1
4
Attainable!

## Slide 37
Power

## Slide 38: Why power?
Wattch (Brooks et al. ‘00)
Increasing CPU cores count => more power
  Difficult to supply and cool

## Slide 39: Power Modeling Techniques
Why do we do power modeling?
  Microarchitectural tradeoff
  Compiler optimization
  Hardware optimization
  Power and Performance correlation
  Forecasting
Wattch (Brooks et al. ‘00)

## Slide 40: Power Dissipation in CMOS
Vin
V out
V dd
CL
V dd
Vcc
I leakage
0
Dynamic
Static
α
Notes: CMOS = Complementary Metal Oxide Semiconductor
Above diagram is a CMOS inverter that is made of a PMOS(vdd) and NMOS(grnd) transistors.
Capacitor stores energy and is used to hold voltage stable for some time when it goes low. The leackage current is a small current flowing into the transistor when it is switched off

## Slide 41: Power in FPGA
Static power(PSTATIC): independent of user clocks
  Leakage power from all FPGA functional blocks except for I/O
  Transistor junction temperature, selected device, and power characteristics (process technology)
Dynamic power
  Dependent on activity factor
I/O power
  DC bias power and transceiver DC bias power, which are accounted for in the I/O and transceiver sections.
Notes: transistor junctions are the two diodes that make up the transitor (e.g. PN or NP). Transceiver = transmitter/receiver module
Activity factor [0..1] = fraction of time the transistors in the circuit are switching

## Slide 42: FPGA Power estimation
FPGA tool chain provide power estimation
Quartus (Power Analyzer)
Design guide:
  Earlier power estimation (process of design)
  Power analyzer (uses VCD trace)

## Slide 43: Power Modeling Techniques
Estimate circuit related parameters & access patterns
Simulation based modeling
Hardware performance counter-based modeling
Circuit simulation-based power modeling
  e.g. cacti
Analytical based modeling

## Slide 44: Power Modeling
Static Power
Dynamic Power
Area,
Circuit technology
Design parameters
Access patterns,
Frequency
Operating Voltage

## Slide 45: Analytical Power Models
Wattch: Processor
Cacti: Cache, memory
Orion: NoC
McPAT: Processor
DRAM Power

## Slide 46: Low-Power Optimization Techniques
Clock gating
Power gating
Dynamic voltage and frequency scaling (DVFS)
Multiple voltage islands(MVI)

## Slide 47: Clock Gating
Reduce dynamic events
  Reducing the activity factor
Prune clock tree
Sequential
Circuit
clk
data
Sequential
Circuit
clk
data
clk gate signal
gclk

## Slide 48: Basics of Power Gating
‘Sleep’ signal is applied when the logic detects sufficiently long idle period
Switch off Vdd
from: Microarchitectural Techniques for Power Gating of Execution Units. Hu et al.’04

## Slide 49: Power Gating
D
L
L
D
L
L
D
L
L
L
L
Sleep
wake
Sleep
Sleep
wake
wake
wake
Sleep
Power gating
D
L
L
D
L
L
Sleep
wake
wake
Sleep
realistic power gating
Notes: D=dynamic power
L=leakage/static power changes linearly

## Slide 50: Power Gating
When to power-gate?
Power gating policies:
  Idle Policy
    Shut the unit after use if future idle period > break even point
    Assumes perfect knowledge of the future when the component will go idle
  Flag policy
    Shut the unit when idle counter reaches a threshold
  Immediate policy
    Shut the unit immediately after use
Notes: Break even point may vary depending on the application

## Slide 51: Power Gating
Power reduction policies
  Branch mispredictions
  L2 misses
  Lock contentions
  TLB misses
  Early thread terminations
  I-cache with trace cache or loop buffer
Notes: The processor will be waiting on those events to resolved, no need for it to run at full power.

## Slide 52: Intel’s Power Management States
Power management states
  C states, P states
  C states: idle states
  P states: power saving states
AMD Hotchip23 presentation

## Slide 53: Intel Turbo Boost Technology

## Slide 54
Q&A

## Slide 55: References
https://www.xilinx.com/html_docs/xilinx2020_1/vitis_doc/programmingvitishls.html#tlb1539734222626
Vitis High-Level Synthesis User Guide : https://www.xilinx.com/support/documentation/sw_manuals/xilinx2021_1/ug1399-vitis-hls.pdf
AXI DMA v 7.1 https://www.xilinx.com/support/documentation/ip_documentation/axi_dma/v7_1/pg021_axi_dma.pdf
https://www.xilinx.com/html_docs/xilinx2020_1/vitis_doc/programmingvitishls.html#tlb1539734222626

## Slide 56
Acknowledgement
This course is partly inspired and use materials from the following courses created by my colleagues:
  ECE-M1126C: Nader Sehatbakhsh @ UCLA
  CS3220: Hyesoon Kim @ gatech